## Slide 1: ShowerPointFinder (org.lcsim.recon.cluster.mipfinder)
Ron Cassell

## Slide 2: Code changes
Current algorithm: Attach mip trace to a track by stepping through calorimeter layers and looking for isolated hits to attach. End when >3 layers missed or > 3 consecutive layers with non-isolated hits.
Problems: Wrong distance variable used in adding hits. Last 2 hits for direction(no lever arm in ecal). Concurrent checking for border crossing (missed layer allows skipping all the way to Hcal, i.e.)
Proposed changes: Use correct distance variable. Use track direction until >= 4 hits, then hit n and n-3. Go as far as possible in current calorimeter before checking for crossovers.

## Slide 3: Checks
Use single pions, E={5,10,20,50} GeV.
Run pfa and look at ShowerFinderMips.
Use MCParticle endpoint as actual interaction point. Divide into epEcal and epHcal.
Look at Barrel, Endcap and Crossover regions.
Compare results: (original, modified)

## Slide 7
For showers starting in Hcal, expect 31 Ecal hits in mip. Modified code reduces skipped layers problem.
For showers starting in Ecal, expect # Hcal hits to be 0.

## Slide 8
0 hits:
Original – 12784
Modified - 13262

## Slide 9
0 bin:
Original – 5508
Modified - 5608

## Slide 10
0 bin:
Original – 1901
Modified - 1935

## Slide 11
dR = R(xy)(last mip hit) –
R(xy)(MC endpoint)

## Slide 13
Small improvement attaching extra Hcal hits.
Small improvement in shower point accuracy.

## Slide 14: Unsolved problems
How do we handle the overlapping staves in the Ecal design?
Algorithm effectiveness drops as RPC multiplicity becomes > 1.
HCAL: Many interactions produce a forward charged particle, with # non-isolated layers small. (Other charged particles quickly branch away with field and large separation between layers)
MuonFinder: Should use same code to attach mip to track.