## Slide 1: A GLIMPS at FTFP_BERT: hadron interactions in GEANT4
Adam Para
July 6, 2010

## Slide 2: Using GEANT4 to Evaluate High Resolution Hadron Calorimeter?
We want to explore the limits of performance of dual readout calorimetry. Monte Carlo simulation is the only practically available tool.
To explore high resolution calorimetry it is necessary that the Monte Carlo simulation conserves energy on the event-by-event basis with the accuracy better than the resolution of the calorimeter
So far: QGSP_BERT is the only model which conserves energy event-by-event
But the model is valid only at low energies. Other models are phased in somewhere around 10 GeV.
Recent suggestion: FTFP_BERT. Use Bertini at low energies, switch to Fritjof above 5 GeV. Expectation is that Fritjof is a better model for interactions on nuclei
Will illustrate FTFP_BERT performance for 50 GeV protons (1000 events)

## Slide 3: Inelastic Processes Simulated
Collection of processes similar to QGSP_BERT. Need to find a good metric for comparison.
per event ~ 20 proton inelastic interactions, ~ 20 interactions of charged pions
~ 500 neutron captures per event  4 GeV (8%) of energy recovered

## Slide 4: High Energy Proton Interactions (Above 1 GeV)

## Slide 5: Space-time Characteristics
primary protons and protons produced in p-nucleus interactions. Notice the leading particle effect (good!)
All interactions very prompt, within 10 nsec
Interactions confined to a very narrow tube along the beam direction, few cm radius.

## Slide 6: Spectra of Produced Particles
Typical spectra of hadron-nucleus interactions
protons (and even neutrons) have harder spectra than pions (leading quark effect)
huge number of very soft protons and neutrons (nuclear evaporation and spallation)

## Slide 7: Nuclear Reactions
Large energy transfers to a nucleus  large number of neutrons kicked out  broad spectrum of produced nuclids
relatively infrequent fission with large surplus of neutrons released

## Slide 8: Binding Energy Losses?
At ‘low’ energies (below 10 GeV)
  missing energy increases with the number of released neutrons (binding energy)
  missing energy somewhat smaller (at the same number of neutrons) for fission events (fission energy release!)
At ‘high’ energies (above 10 GeV)
  not much correlation between the numbver of neutrons and the missing energy  non-conservation of energy
  Missing energy appears smaller than in QGSP_BERT

## Slide 9: Low Energy Neutron Interactions (below 100 MeV)

## Slide 10: Space-Time Characteristics
most of neutron interactions at very low energies < 20 MeV
most interactions relatively prompt, within 100-200 nsec
interactions over large volume, both radially and along the shower axis

## Slide 11: Nuclear Processes
interactions of low energy neutrons with nuclei typically produce very few neutrons, most probably one and produce nuclids very close to the original nucleus
Fission is very infrequent ~0.2 fission per event

## Slide 12: Binding Energy Losses

## Slide 13: Preliminary Impressions
Most of the features/distributions look quite sensible
Low energy behavior similar to QGSP_BERT (probably good)
High energy model seems ‘better’ that those in the case of QGSP_BERT (smaller missing energy), albeit there is no correlation between the missing energy and number of neutrons
It may be a better ‘test case’ for the dual readout calorimetry than QGSP_BERT
Further studies necessary. In particular a comparison with CHIPS of interest
Need to find a good metric for comparison of different models.