## Slide 1
Simulation of the RPC Response
José Repond
Argonne National Laboratory
SiD Calorimeter Meeting, by phone
July 15, 2010

## Slide 2
Simulation Strategy
GEANT4
Experimental set-up
Beam (E,particle,x,y,x’,y’)
Points (E depositions in
gas gap: x,y,z)
RPC response simulation
Measured signal Q distribution
Hits
DATA
Hits
Comparison
Parameters
Exponential slope a
Threshold T
Distance cut dcut
Charge adjustment Q0
With muons – tune a, T, (dcut), and Q0
With positrons – tune dcut
Pions – no additional tuning

## Slide 3
RPC_sim
Input: ASCII file
-1 IL -1 -1 -1 Nevt = 1
LN x y
LN x y
…
-1 IL -1 -1 -1 Nevt = 2
LN x y
LN x y
…
Language: Fortran 77
276 lines of code
(I think it is well documented)
Output: ASCII file
EV IL -1 -1
EV x y LN
EV x y LN
…
EV IL -1 -1
EV x y LN
EV x y LN
…
Same format as
ASCII output of event builder
IL … true interaction layer
LN … layer number
EV … event number
GEANT4
RPC_sim

## Slide 4
RPC_sim: Step I
Discard close-by hits
RPCs do not generate multiple avalanches very close by
Check distance d between all pairs of points
If d < dist_cut, discard one of the points

## Slide 5
Generated charge distributions
for different HV settings
Measured charge distribution
for HV = 6.2 kV
RPC_sim: Step II
Generate overall charge
Fit to y = α (x-2900)β e-γ(x-2900)
Allow for shift of Q spectrum by Q0

## Slide 6
RPC_sim: Step III
Distribute charge over pads
Measured charge distribution as
function of y in the pick-up plane
D.Underwood et al.
Throw 10,000 points in x,y plane within radius R0 of avalanche
Calculate charge Q(r)
Sum up charge on 1 x 1 cm2 pads
Assume exponential dependence on distance from avalanche
Cross check:
sum of charges on pads
Exponential with slope a

## Slide 7
RPC_sim: Step IV
Identify hits
Pad identified as hit if Qpad > T
Note:
This procedure reproduces the average efficiency and pad multiplicity of RPCs for
single tracks (muons)
It deals properly with the overlap of avalanches within a shower or from
different particles
It does not deal with the effect of particles crossing the chambers at an angle
(we know that the efficiency (pad multiplicity) is slightly (somewhat) dependent
on the angle of incidence).

## Slide 8
RPC_sim: Tuning I
Location and angle of particles
Procedure
Cluster hits in each layer
Fit straight line to clusters
Compare MC and data:
Clusters in first layer
Slopes of straight lines
Adjust MC to reproduce data
Simulation
Data

## Slide 9
RPC_sim: Tuning II
Tune parameters Q0, a, and T
Broadband muons
from FNAL test beam (with 3 m Fe blocker)
Tune
slope a
threshold T
charge adjustment Q0
(Muon data not sensitive to dist_cut)
→ reproduce the distributions of the sum of hits and hits/layer
Data
Simulation

## Slide 10
RPC_sim: Tuning III
Tune parameter dist_cut
Adjust dist_cut to reproduce Σhits for 4 GeV positrons
8 GeV Positrons

## Slide 11
RPC_sim: Tuning IV
Cross – check with pions
Fit to 2 components
- Pions (from MC)
- Positrons (from MC)
Note
MC curves = absolute predictions,
apart from general scaling due
to efficiency problems (rate) at
16 GeV (-9%)

## Slide 12
RPC_sim: Predictions I
Response curves
107 layers (minimal leakage)
Each 1.5 x 1.5 m2
Reasonable Gaussian fits for E > 2 GeV

## Slide 13
Reasonable Gaussian fits for E > 2 GeV
Discontinuity at E ~ 8 GeV (surprising, changes with physics list)
Non-linearity above E ~ 20 GeV (saturation)
Resolution ~ 58%/√E(GeV) (for E < 28 GeV)
Resolution degrades above 28 GeV (saturation)
Resolution of 1m3 with containment cut somewhat better than for extended calorimeter
RPC_sim: Predictions II
Linearity and resolution

## Slide 14
Efficiency and pad multiplicity have
only minor effect on resolution
(Large ε/small μ might be desirable for PFAs)
However values need to be known (calibration)
Note: Linear calibration corrections for ε,μ will work (P1 ~ 0)
RPC_sim: Predictions III
Dependence on ε and μ

## Slide 15
Discontinuity seems
to move from 8 to 4 GeV
Discontinuity due to transition
in hadron showering models
These physics lists obsolete
by now
RPC_sim: Predictions IV
Different physics lists

## Slide 16
60 GeV Pions
GEANT4 simulation +
RPC response simulation
RPC_sim: Predictions V
Event displays