## Slide 1: A Model for Industrialization
Total numbers of SCRF 9-cell cavities required for ILC (Main Linac +Damping Ring + others)
  15,764
A model for 9-cell cavity productions
  15,764 + spare + production back-up (~ 10%)
   ~ 18,000 cavities / 4~ 5 years
Possible models for manufacturing
  Single consortium/vendor
  Three regional consortiums/vendors
  Six (or more) consortiums/vendors
    < 3,000 > cavities / vendor
    < 3 > cavities / day / vendor (assuming 5 yrs & 200 days/yr)

## Slide 2: Industrialization Models
Global Vendors/Consortiums/Laboratories
  Research Instruments (ACCEL) and Zanon in Europe
  AES, Niowave/Roark, and PAVAC in Americas
  MHI, (Hitachi, Toshiba, and others ) in Asia
Production Models and Rate of SCRF Cavities |  |  |  | 
Project | # of Cavities assumed | # of Vendors | Production period (years) | Production Rate: (Cavities/day/vendor) (at 200 ~ 250 work-days/yr)
SNS | ~ 110 (including +20%) | 1 | 3 | 0.2 ~0.15
XFEL | (~640) | (1) (2) | (3) (3) | (1.1 ~ 0.85) (0.55 ~ 0.43)
ILC | (~ 18,000) (including +10%) | (1) (3) (6) | (5) (5) (5) | (18 ~ 14.4) (6 ~ 4.8) (3 ~ 2.4)

## Slide 3: Prepare for ILC-scale Industrialization
Learn from previous efforts and current status:
  Industrialization study for TESLA (1990’s)
  Recent R&D progress (in ~ 10 years)
  Current status in industries (in progress)
Learn from industrialization of XFEL Project
Encourage Laboratory / Industry partnerships
  Realized in all 3 regions
    Europe: XFEL, Americas: Venders manufacturing, Asia: A pilot plant at KEK
  Prepare for cost-effective production and quality control in cooperation with industries
Communication with Industries
  1st: Visit Venders (done in 2009)
  2nd: Workshop (done at IPAC-10 satellite meeting)
  3rd: Call for Response with a preliminary specification and cost estimate by industries

## Slide 4: SCRF-ML Technology Required
RDR Parameters | Value
C.M. Energy | 500 GeV
Peak luminosity | 2x1034 cm-2s-1
Beam Rep. rate | 5 Hz
Pulse time duration | 1 ms
Average beam current | 9 mA (in pulse)
Av. field gradient | 31.5 MV/m
# 9-cell cavity | 14,560
# cryomodule | 1,680
# RF units | 560
RDR  SB2009

## Slide 5: Global Plan for SCRF R&D
Year | 07 | 2008 |  | 2009 |  | 2010 |  | 2011 | 2012
Phase | TDP-1 |  |  |  |  |  | TDP-2 |  | 
Cavity Gradient in v. test to reach 35 MV/m |  Yield 50% |  |  |  |  |  |  Yield 90% |  | 
Cavity-string to reach 31.5 MV/m, with one-cryomodule |  | Global effort for string assembly and test (DESY, FNAL, INFN, KEK) |  |  |  |  |  |  | 
System Test with beam acceleration |  |  | FLASH (DESY) , NML (FNAL) STF2 (KEK, test start in 2013) |  |  |  |  |  | 
Preparation for Industrialization |  |  |  |  | Production Technology R&D |  |  |  | 

## Slide 6: Numbers of processes trade-off
 | Yield % | Fabrication of Dumb-bell with EBW | Fabrication of End group EBW | Assemble 9-cell Cavity With EBW | Number of machines and processes required |  | 
 |  |  |  |  | EB Welding | Vertical Test | Electro-polishing
Case1 R&D phase | 100 | 1 seam / welding cycle (3 hrs/3 cycle) | 1 seam / welding cycle (11 hrs / 11 cycle) | one 2(4,8)-cell / welding cycle (9 hrs/9 cycle) | 12 | 6 7 | 6
 | 90 |  |  |  |  |  | 
Case2 Current prod. | 100 | 8 dumb-bell / welding cycle (6.5/8 hrs/3 cycle) |  | one 9-cell / 2 welding cycle (4.7 hrs / 2 cycle) | 8  7* | 6 7 | 6
 | 90 |  |  |  |  |  | 
Case3 Mass Production Study | 100 |  | 8 end group / welding cycle (46.7/8 hrs/11 cycle) |  | 5  4* | 6 7 | 6
 | 90 |  |  |  |  |  | 
* In case of common EBW machines for dumb-bell and end-group