Comments on the DAQv2 advancement
Vincent Boudry
LLR, École polytechnique
Calice Week
23/09/2010

---
HW status
- 10 ECAL DIF ready and working; 10 in prod; mat for 40 in total (CAM)
- DHCAL DIF: 165/170 cards tested & ready (LAPP)
- AHCAL DIF: in design, prod in NIU → 4 unit
- CCC: 10 cards ready; 4 in use in 4 labs; 3 more shipped → LLR
- DCC: 3 prototypes ready; 2 cards being tested → 20 end of october
- LDA: 20 main board OK
  - 5 v1 + 15 v2 Ethernet mezzanine : ✔
  - 6 CCC mezzanine; clock OK — Busy & Trigger not yet tested (TBC)
  - 20 HDMI Mezzanine: faulty connectors on 8 → in repair
- ODR + PC
  - 8 ODR ready ; network card being used instead for debugging
  - 6 PC available: 1 in LLR ; 3 other ready; OS needs to be upgraded
- BIF: to be developped (part of AIDA)
~ No more basic problem with HW
Reliability of HDMI connectors mechanics ?

---
HW status
- 10 ECAL DIF ready and working; 10 in prod; mat for 40 in total (CAM)
- DHCAL DIF: 165/170 cards tested & ready (LAPP)
- AHCAL DIF: in design, prod in NIU → 4 unit
- CCC: 10 cards ready; 4 in use in 4 labs; 3 more shipped → LLR
- DCC: 3 prototypes ready; 2 cards being tested → 20 end of october
- LDA: 20 main board OK
  - 5 v1 + 15 v2 Ethernet mezzanine : ✔
  - 6 CCC mezzanine; clock OK — Busy & Trigger not yet tested (TBC)
  - 20 HDMI Mezzanine: faulty connectors on 8 → in repair
- ODR + PC
  - 8 ODR ready ; network card being used instead for debugging
  - 6 PC available: 1 in LLR ; 3 other ready; OS needs to be upgraded
- BIF: to be developped (part of AIDA)
~ No more basic problem with HW
Reliability of HDMI connectors mechanics ?

---
FW status
LDA+CCC comm (M.Warren)
Reuse MUX from DCC (FG)
	LDA	DCC	DIF's
Ethernet	✔ at full speed
CCC	Clk; Trig; Busy	Clk; Trig; Busy	Clk; Trig; Busy
Nlinks up	7/10 conn. no MUX	9	1
Fast Commands	✔	✔	✔
Block transfert	✔	✔	✔
Data1)	✔ (< 50 MHz)	✔ (< 50 MHz)	✔ (<50 MHz)
ROC			Structure ✔ Adapt SDHCAL USB Code on going...
Simple
but critical
- FW have been advancing rather fast during the last months
  - effort on going (⊃ in UK) → MW, MW & BH at LLR on 28th of July
  - G.V. → integration of ROC management in DIF started but needs finalisation
Many progresses recently
End of October for first full minimal usable chain ?

---
SW status
- Many progress
  - XDAQ (L. Mirabito, Ch. Combaret) “critical part“ complete:
    - Writing of LCIO data in RAW format
    - versatile online analysis framework (root histos)
  - DAQ2 interface ←→ XDAQ being worked on (D. Decotigny, G. Vouters)
- Missing utilities
  - Semi-automatic noisy channels spotting & correcting (moniting) ←←←
  - Clean Slow control
  - interface to CondDB;
  - event display (most probly DRUID)
  - interface to the GRID
  - interface to the machine
- Analysis environment (IPNL)
  - rec. data format in LCIO
~
✔
✔
~
✔
×
×
×
×
×
~
 USB ✔
DAQv2 ×
×
✔
✔

---
Installation
- mechanics
  - mod. VME crate for
    - DCC
    - CCC
  - Special box for LDA
  - Support for cables
- Final set-up not yet known:
  - stand alone SDHCAL
  - stand alone ECAL
  - Stand alone AHCAL
  - Combined test
- → 5 m long HDMI cables
  - halogen free;

---
Plans
1. Critical: Complete the FW → full acquisition chain & check perfs (stability)
  1. Trigger logics → M. Warren
  2. LDA MUX → F. Gastaldi
  3. Finish adaptation of USB FW → DAQv2 FW → G. Vouters
    1. Adapt SDHCAL DIF FW → ECAL DIF & AHCAL DIF
2. Complete the SW critical part
  1. Integration of DAQv2 in XDAQ → D. Decotigny
3. Continue development SW of utilities
  1. Define optimal PC configuration: Stand alone SDHCAL → Combined tests
  2. Writing to GRID; interface to beam → L. Mirabito, Ch. Combaret
4. Prepare the set-ups
  1. SDHCAL m³ TB
  2. Electronics & Cosmic ECAL test bench in LLR
  3. μMegas, ECAL & AHCAL TB (to be defined): brute perf to be ×-checked