## Slide 1
Status of GEM DHCAL
Jae Yu
For GEM-TGEM/DHCAL Group
Sept. 24, 2010
CALICE Collaboration Meeting
Univ. Hassan II, Casablanca
Introduction
What has been done?
2D readout with KPiX chip
TGEM Beam Test at CERN
Large GEM Foil Certification
Large Chamber Mechanics Design
Summary

## Slide 2: Why GEM?
Flexible configurations: allows small anode pads for high granularity
Robust: survives ~1012 particles/mm2 with no performance degradations
Based on electron collection, ~few ns rise time
Short recovery time  can handle high rates
Uses simple gas (Ar/CO2) – no long-term issues
Runs at relatively low HV ( ~400V across a foil)
Stable operations

## Slide 3
GEM-based Digital Calorimeter Concept
Use Double GEM layers
{
~6.5mm
-2100V
∆V ~400V
∆V ~400V
0V

## Slide 4: What have been done so far?
Bench tested with various source and cosmic ray
  Used QPA02 chip based preamp
  Verified the signal shape, responses and gain
Took a beam test at a high flux electron beam
  Prototype chamber built with 3M’s 30cmx30cm GEM
  Used QPA02 chip based preamp
  Verified that the chamber can survive
Took two beam tests at FNAL’s MTBF
  Used QPA02 chip based preamp
  8 GeV pion beams and 120GeV proton beams
  Measured chamber responses, efficiencies and gain

## Slide 5
1024 channel 13 bit ADC chip
Developed for Si/W ECAL@ SLAC
DHCAL anode pad
Dynamic gain select (GEM/Si)
Event triggered by the ILC clock
Leakage current subtraction
calibration
Storage until end of train.
Pipeline depth presently is 4
13 bit A/D
KPiX Analog Readout for GEM DHCAL
New version equipped with self and ext. trigger
Notes: 5

## Slide 6
GEM-DHCAL/KPiX boards with Interface and FPGA boards

## Slide 7
HV power
Analog signal
Gas outlet
LV power
Data cable
Top side
Fe55 Source Signal

## Slide 8: GEM+kPiX Fe55 and Ru106 Spectra
Fe55
Ru106
Good conformation to characteristic Minimum Ionizing Landau fit

## Slide 9: Charge Weighted Lego for Fe55
HV=1960 V, Self Trigger Th=1.8 V= 14fC
Inactive area
(HV not applied)

## Slide 10: Histogram Map for Fe55
HV=1960 V, Self Trigger Th=1.8 V= 14fC

## Slide 11: Gain vs HV
1960V
1930V
1900V
1860V
Typical operating point: Gain ~6000

## Slide 12
Pressure Dependence of Gain

## Slide 13: Cosmic Ray Data with External Trigger – kPiX
Noise spectrum

## Slide 14
Thick Gas Electron Multiplier (THGEM)
SIMPLE, ROBUST, LARGE-AREA
Intensive R&D
Many applications
1e- in
104- 105 e-s out
E
THGEM
Double-THGEM: 10-100 higher gains
~ 10-fold expanded GEM
PCB Based GEM  Cost effective
0.5 – 1mm thick PCBs
Drilled 0.4mm holes with 1mm pitch
Expected to have higher gain per GEM
10cmx10cm tested, up to 30cmx30cm produced
Thickness 0.5-1mm
drilled
etched
THGEM Recent review
NIM A 598 (2009) 107
THGEM - A. Breskin et al

## Slide 15
2-THGEM BEAM TESTS with Q-preamp/MCA
2-THGEM BEAM TESTS with KPIX
First kpix spectrum with muons.
Double-THGEM, Ne/5%CH4; Average gain 5300
Trigger: large scint + ~1cm2 scint
3.4 mm
drift
First Q-preamp spectrum with muons.
Double-THGEM, Ne/5%CH4; Average gain 5000
Trigger: large scint + ~1cm2 scint
3.4 mm
drift
e-
1x1 cm pad electrode
THGEM
MIP
KPIX or Q-preamp/MCA
Here we had:
0.5mmholes/1mm space
Muons w Double-THGEM
KPIX or Q-preamp/MCA
August 2010
THGEM - A. Breskin et al

## Slide 16
CERN TGEM test-beam detector
10x10 cm2 THGEM
64 pads electrode
with KPiX behind
Installation
at CERN
THGEM - A. Breskin et al

## Slide 17
Single THGEM 10x10cm
Thickness: 0.4 mm
Particles: muons
Gas: Ne/5%CH4
Drift gap: 3 mm
Charge preamp/MCA
0.5 cm2 trigger
Efficiency: ~95%
Chart: 
| 550.0 | 560.0 | 570.0 | 580.0 | 590.0 | 600.0 | 610.0 | 620.0 | 630.0 | 640.0 | 650.0 | 660.0
3mm gap 20-08-2010 THGEM 0.4 | 0.4 | 0.5 | 0.61 | 0.66819 | 0.7425 | 0.80623 | 0.84021 | 0.89968 | 0.92316 | 0.94191 | 0.94811 | 0.95734
20 August 2010: Single-THGEM with muons
muons
e~96%
August 2010
THGEM - A. Breskin et al

## Slide 18
Single-THGEM/3mm drift gap
PIONS
MUONS
Measured very low discharge rates even with pions
THGEM - A. Breskin et al

## Slide 19: 33cmx100cm GEM Foil Design
Designed to work with DCAL boards
Active area 468x306 mm2
Number of HV sectors = 32x2=64
HV sector dimension= 9.9x479.95 mm2
Sept. 24, 2010
GEM DHCAL, J. Yu

## Slide 20: 33cmx100cm Large Area GEM
First 5 of 33cmx100cm GEM foils delivered early July, 2010
Design for Large Area GEM detector frames
Sept. 24, 2010
GEM DHCAL, J. Yu

## Slide 21: Temporal Behavior of Strips
Strip #4 - Trial 1
Strip #4 – Trial 2
Strip #9 –trial 1
Strip #9 – trial 2
Strip #9 – trial 3
Sept. 24, 2010
GEM DHCAL, J. Yu

## Slide 22: Times to reach full charge saturation
Chart: 
| 21.0 | 23.0 | 25.0 | 27.0 | 29.0 | 31.0 | 33.0 | 35.0 | 37.0 | 39.0 | 41.0 | 43.0 | 45.0
 | 1 | 9 | 6 | 9 | 4 | 2 | 1 | 1
Sept. 24, 2010
GEM DHCAL, J. Yu
Indication of general health of each strip
Most of them reaches full charge up in 30min
Two strips took 15min longer
Resistance of each strip is over 260GOhms!!

## Slide 23
Base steel plate, t=2 mm
Readout Board
320x500 mm2
320 mm
1000 mm
33cmx100cm DHCAL Unit Chamber Construction
1mm pad board
2mm FE board
1mm assister strong back
2mm steel strong-back + thin cathode layer
3mm
1mm
1mm
1cm thick support from G10 spacers
We might be able to avoid this dead zone by gluing the two boards directly together!!
Readout boards are part of the gas volume!! How do we mate these together with minimal dead area?

## Slide 24
UTA’s 33cm x 100cm DHCAL Unit Chamber
Glue the boards directly on their edges??

## Slide 25
UTA’s 100cmx100cm Digital Hadron Calorimeter Plane
(32x96 mm2)
(32x96 mm2)
100cm
100cm
96 ~ 97cm
32cm
100cm

## Slide 26: GEM DHCAL Plans
Phase I  Completion of 30cm x 30cm characterization
  Mid 2010 – Early 2011: using one to three planes of 30cm x 30cm double GEM chamber with 64 channel KPiX7 and DCAL chips
  Oct. 2010: Joint Test with THGEM/KPiX at CERN (Using RD51 setup)
Phase II  33cm x 100cm unit chamber construction and characterization
  Early 2011 – late 2011 at FTBF: Using available KPiX chips (V9?) and DCAL chips
Phase III  100cm x 100cm plane GEM DHCAL performances in the CALICE stack
  Late 2011 – Late 2012 at Fermilab’s FTBF or CERN
  Five 100cm x 100cm planes inserted into existing CALICE calorimeter stack and run with either Si/W or Sci/W ECALs, and RPC or other technology planes in the remaining HCAL

## Slide 27: Summary
Steady progress has been made reading out 30cmx30cm GEM prototype chambers with 64 channel KPiX v7 chips
  Observed clean characteristic peaks from Fe55 and Ru106 sources as well as cosmic ray muons
  Getting ready to beam test these chambers
  Higher channel count (512 channel) KPiX V9 chips available
  Pressure dependence measured and data corrected
TGEM made a quantum jump and had a beam test at CERN
  Will have another one in Oct. 2010  RD51 setup
33cmx100cm unit chamber construction proceeding
  First 5 foils of 33cmx100cm delivered and one HV tested
Mechanical design being worked out for constructing 33cmx100cm unit chambers and 1mx1m planes for DHCAL testing