Analysis of PCB Exposure Tests
        Roman Pöschl
        LAL Orsay
- Motivation
- Analysis and Results
- Summary, Conclusion and Outlook
CALICE Collaboration Meeting Casablanca/Maroc Sept. 2010

---
Introduction
Calorimeter Electronics to be interleaved with layer structure
Do high energetic showers create signals directly in electronics ?
If yes, rate of faked signals ?

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup I
Test PCB
- equipped with
  PHY3 chip set
Prepared slab
- W dummy
- capton and paper
  for electrical shielding
Usual slab
Picture courtesy of B.Lutz

---
Special PCB in Ecal Prototype during CERN 07 testbeam – Experimental Setup II
- PCB positioned at place of layer 12 in Ecal ~ shower maximum
  x,y position identical to layer 2
- Schematic view of test PCB - 'Expect' signals from 72 pads, 4x18 = 2 Wafer
Nominal
positions
of
chips
Scanning
points
Sketch by M.Reinhard/F.Salvatore
- 2.6 106 events with 90 GeV electrons (- 5.8 105 with 70 GeV electrons)
  At least 70 K at each scan point
  Runs 331462 – 331518

---
Statistics of Analysis
Scan 3
Scan 4
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 9831 Evts.
Run331495: e-90 GeV
Signal: 314275 Evts.
Pedestal: 15264 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331498: e- 90 GeV
Signal: 66655 Evts.
Pedestal: 4223 Evts.
Run331493: e- 90 GeV
Signal: 85884 Evts.
Pedestal: 4949 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331497: e- 90 GeV
Signal: 214418 Evts.
Pedestal: 13666 Evts.
Run331494: e- 90 GeV
Signal: 217415 Evts.
Pedestal: 11698 Evts.
Scan 1
Scan 2
Run331473: e- 70 GeV
Signal: 209312 Evts.
Pedestal: 38361 Evts.
Run331488: e- 90 GeV
Signal: 213369 Evts.
Pedestal: 13719 Evts.
Run331470: e- 70 GeV
        331471
Signal: 78293 Evts.
Pedestal: 14624 Evts.
Run331479: e- 90 GeV
Signal: 85543 Evts.
Pedestal: 4306 Evts.
Run331480: e- 90 GeV
Signal: 85188 Evts.
Pedestal: 4678 Evts.
Run331492: e- 90 GeV
Signal: 89435Evts.
Pedestal: 4254 Evts.
Run331472: e- 70 GeV
Signal: 189966 Evts.
Pedestal: 37137 Evts.
Run331478: 90 e- GeV
Signal: 65249 Evts.
Pedestal: 3602 Evts.
Run331491: e- 90 GeV
Signal: 217711Evts.
Pedestal: 11053 Evts.
Run331486: e- 90 GeV
Signal: 129778 Evts.
Pedestal: 6146 Evts.
Run331518: e-90 GeV
Signal: 90395 Evts.
Pedestal: 4347 Evts.
Run331516: e- 90 GeV
Signal: 228138 Evts.
Pedestal: 10926 Evts.
Run331513: e- 90 GeV
Signal: 216877 Evts.
Pedestal: 38295 Evts.
Run331511: e-?? GeV
Signal: 86989 Evts.
Pedestal: 3909 Evts.
Run331512: e- 90 GeV
Signal: 218519 Evts.
Pedestal: 9462 Evts.
Scan 4

---
On Run Selection and Observations
- Runs selected according to entries in the logbook
  No comments on bad quality by shift crew
- Switch of energy between Run 331473 and Run 331478
  - Change in pedestal rate
    20% of all events -> 5% of all events
    Still at least 3500 of (valuable) pedestal events
- at least 70k events at each point
   - mostly 90 kEvents for off center runs
   - > 200k at (nominal) chip center

---
Accompanying Remarks
Disclaimer I:
The following is based on the motivation to quantify
parasitic effects (upper limits) and on the observation that
the noise spectra of the chips are not “simple”
Disclaimer II:
- Concentration of runs with central nominal impact on cells
- Otherwise prohibitive number of plots
- If at all largest effect
- Still enough means for comparison with chips out of beam

---
Principal Component Analysis - PCA
       Following 'cooking recipe' a la ATL-LARG-99-009
        (Mathematical 'proof' for the following in my lab book)
1) Noise Vector:
color red {vec b = vec u + c vec %alpha}
Magnitude and 'direction'
of coherent noise
Incoherent
noise
color red {B=%sigma^{2} cdot I+%sigma^{2}_{c}vec %alpha {vec %alpha}^{T} }
2) Covariance Matrix:
   With: <uiuj>=σ2δij incoherent noise
        σc2= Variance of c
3) Eigenvalues and eigenvectors of covariance matrix:
vec %alpha " is eigenvector to (largest) eigenvalue" %sigma^{2}+%sigma^2_{c}
"Any other eigenvector (orthogonal) to " vec %alpha " is eigenvector to eigenvalue " %sigma^{2}
=> Expect flat spectrum of matrix B except for one (or few) eigenvalue associated with 
"Coherent channel noise via " %sigma_{c} cdot vec %alpha
color red {B'= B-%sigma^{2}_{c}%alpha%alpha^{T}}
4) Incoherent Channel noise via:
=> Matrix with incoherent channel noise on diagonal and
      off-diagonal elements flat and zero

---
      5) Estimation of c -Parameter
Since all channels are equal, the variance reaches a minimum
        Estimation of c-Parameter by minimising
color red {sum u^{2}_{i} }
color red {sum (b_{i}-c%alpha_{i})^2}
color red { c=vec %alpha vec b}
⇒
By determining αi and measuring bi (the actual ADC count)
c can be calculated on an event-by-event basis

---
Eigenvalues of Covariance Matrix
%sigma^{2}+%sigma^2_{c}
- Mostly clear
  prominent
  eigenvalues
=> Coherent
      noise
- Where less
  prominent:
  Still visible
  step
- Fairly flat
  spectrum of
  other
  eigenvalues
- Excellent
  agreement
  between Signal
  and Pedestal
Channel Nr.

---
   Elements of Eigenvector
- Excellent
  agreement
  between Signal
  and Pedestal
modulo
sign ambiguity
(known feature
 of PCA)
Reveal channels
with coherent
noise
Channel Nr.

---
Coherent Noise Level
Different Patterns
- Concentrated for
  Chip 1 and Chip 3
- Flat spectrum
  for Chip 2 and 4
- Excellent
  agreement
  between Signal
  and Pedestal
- Coherent noise
  level
  ~1 ADC Count
Channel Nr.

---
Matrix B' for Signal Events
Diagonal: Prominent with value ~20 (ADC Counts)2
Off-Diagonal: Flat with value ~0

---
Incoherent Noise Level
Results for Scan 1
- Flat spectrum
  for all chips
- Incoherent noise
  level
~√20 ~4.5 ADC C.
- In agreement with
  rms (see earlier)
- Excellent
  agreement
  between Signal
  and Pedestal
color red {sqrt{%sigma^{2}_{ic}+%sigma^{2}_{cn}}approx sqrt{4.5^{2}+1} approx 4.6}
Channel Nr.

---
Spectrum of c-Parameter
 - Good
   agreement
   between Signal
   and Pedestal
- In future
  application the
  values in these
  spectra can
  be used to
  subtract coherent
  noise!
- Here:
  Spectra used
  as input pdf
  for simulation
  of noise

---
Simulation of Noise
color red {vec b = vec u + c vec %alpha}
  Noise vector:
Incoherent noise:
Simulated by Gaussian with width i (see page 14)
        and mean xm (see talk 3/5/10)
Coherent noise:
αi see above
c parameter spectrum, see above, as input to kernel estimation
à la Cranmer (hep-ph/005309) as implemented in RooFit package
(extension to root)
Final formular for channel i:
color red {b_{i} = G(x_{m}-p_{m}, sqrt{%sigma^2_{i}-p_{%sigma}}) + (sign)K(c) %alpha_{i}}
color red {(sign) = vec %alpha_{ped} cdot vec %alpha_{sig} }
pm, pσ = corrections for imperfections of PCA
Strategy: - Establishment of noise model reduces drawback
        by relative small number of pedestal events
- Optimise model (i.e. adjust pm, pσ ) for pedestal
        events to make predictions for signal events
        Optimisation of agreement between model and
        pedestal w.r.t to χ2/ndf
        Already now: Typical value for pσ ~ 1.5
        Range for pm = [-0.01, 0.15]

---
Agreement Pedestal Data and Model
Example: Chip 1 in Scan 1 – All noise spectra see below
Data
(Pedestal)
Model
Black: Data (Pedestal)
Red: Model
Excellent agreement over several orders of magnitude
Non gaussian component in tail correctly reproduced by Model
(remember only trivial component tuned, see page 16)

---
Agreement Pedestal Data and Model
Example: Chip 2 in Scan 2 – All noise spectra see below
Data
(Pedestal)
Model
Black:
Data (Pedestal)
Red: Model
Excellent agreement over several orders of magnitude
Non gaussian component in tail correctly reproduced by model
(remember only trivial component tuned, see page 16)
Extreme outliers not-reproduced

---
χ2/ndf between Data and Model
Optimisation for central impact only
χ2/ndf ~ 2 for 100k simulated events – at least 2.5 times data statistics
Worst results for Chip 2

---
A Final Correction
erf left ( {%DELTA x} over {2 sqrt{2} %sigma } right )
Errorfunction:
With x = Difference between data and model
 = statistical uncertainty of data
Errorfunction gives probability that true value lies within x
erfc = 1- erf left ( {%DELTA x} over {2 sqrt{2} %sigma } right )
Complementary Errorfunction:
f(%DELTA x, %sigma)= left [ 1- erf left ( {%DELTA x} over {2 sqrt{2} %sigma } right ) right ] cdot %DELTA x
Correction of Model by adding:
to the individual bin content of the model spectra
Remark: Correction inspired by recent BABAR analysis (B. Malaescu, M. Davier)

---
Agreement (Pedestal) Data – Model in Tail – Positive Hits
- Data – Model
  agree mostly
  within 97.3% CL
  (≙ 3 for n->∞)
- Remember
  complexity
  of noise
  distribution!!!
Satisfactory up to excellent reproduction of noise spectra by model

---
Agreement (Pedestal) Data – Model in Tail – Negative Hits
- Data – Model
  agree mostly
  within 97.3% CL
  (≙ 3 for n->∞)
- Remember
  complexity
  of noise
  distribution!!!
Satisfactory up to excellent reproduction of noise spectra by model

---
Upper Limits for “Parasitic” Hits for Pedestals – Positive Hits
Limits at 95% CL
- Expect points exactly
  on lines
- Observe points
  relative close to
  lines
- Residual “weakness”
  of model
- Lines: expected upper limit from model
Reliable model => Extraction of Reliable upper limits possible

---
Upper Limits for “Parasitic” Hits for Pedestals – Negative Hits
Limits at 95% CL
- Expect points exactly
  on lines
- Observe points
  relatively close to
  lines
  Works better for
  negative than for
  postive hits
- Residual “weakness”
  of model
- Lines: expected upper limit from model
Reliable model => Extraction of Reliable upper limits possible

---
Application of Model to Signal Events
Some remarks:
- The model was only tuned to pedestals and is “blindly” applied
  to signal spectra
- Number of Signal events > 10xNumber of Pedestal Events
  => Considerable extrapolation
- For signal events there are signals (=> activity) in the rest of
  the detector which may influence the spectra of the chips under
  study

---
Agreement (Signal) Data – Model in Tail – Positive Hits
- Data – Model
  agree still often
  within 97.3% CL
  (≙ 3 for n->∞)
- Remember
  complexity
  of noise
  distribution!!!
x50
x50
x50
x10
x10
x20
x10
x10
Satisfactory reproduction of noise spectra by model
However significant differences visible

---
Agreement (Signal) Data – Model in Tail – Negative Hits
- Data – Model
  agree still mostly
  within 97.3% CL
  (≙ 3 for n->∞)
- Remember
  complexity
  of noise
  distribution!!!
- Better agreement
  for negative hits
Satisfactory reproduction of noise spectra by model
However significant differences visible

---
Upper Limits for “Parasitic” Hits for Signal Events – Positive Hits
Limits at 95% CL
- Points further away
  from lines
- Amplification of
  residual disagreement
  observed for
  pedestal events
Expected and derived limit agree always within factor of 10 (often better)

---
Upper Limits for “Parasitic” Hits for Signal Events – Negative Hits
Limits at 95% CL
- Points further away
  from lines
- Amplification of
  residual disagreement
  observed for
  pedestal events
Expected and derived limit agree always within factor of 10 (often better)

---
Comments on Upper Limits and final Results
- Model often successful in predicting upper limits also for
  signal events!!!
- No visible influence of beam in noise spectra
  Exposed chips vary comparable to non-exposed chips
  => Effect of beam is smaller than other effects on the noise spectrum
- The partially large differences in the upper limits are an amplification
  of the residual discrepancies observed already for the pedestal events
- Weaknesses of the model
   - Relative small number of pedestal events
     => Difficult to construct model and to extrapolate it to signal statistics
   - Cross talk between chips (not taken into account)
   - Interspersed noise from signals in other parts of detector
- Upper limit ~5x10-6 for typical noise cut of 25 ADC Counts (0.6 of a MIP)
   At e.g. ILC: Typically ~2500 cells in a tt event above noise
   10 k for 0.5x0.5 cm2 cells

---
Summary and Conclusion
- Detailed monitoring of mean of noise distributions
        and
  noise analysis based on PCA gives confidence that pedestals
  can well be used to model the chip responses
- PCA allows for dedicated investigation of noise structure
  of detector
- PCA gives no evidence that beam in VFE distorts signals
- No visible influence of beam on exposed chips
  effects of beam smaller than other parasitic effects
- As fruitful side goodie of analysis:
  - Algorithms at hand for “professional” noise analysis of at least all analogue
    calorimeters of CALICE!!!!
  - Can be transformed into general “Noise analysis suite”
    (after cleaning and structuring of my code)
  - Be very careful with simple analysis to obtain coherent noise
    (Not reliable)

---
Improvements of the measurement
- Need better controlled setup
  Layer integrated into full detector maybe not beneficial for
  measurement
  - Layer would need to be super-isolated from rest of detector
  - Maybe single board in low energy (~10 MeV) not too intensive
    electron beam would lead to better results
- Number of pure pedestal events are to be at least equal to number
  pedestal events to construct a reliable model

---
Backup Slides

---
Basic Spectra and Alignment
90 GeV run (331495)
- Clear Energy Peak
- Special Board place at
  ~ shower maximum
Projected Chip
Position
Hit Maps
- Layer 2
  Same xy-Position as
  Special Board
- Layer 14
  First instrumented Layer
  after Special board
Chip(s) well within
lateral shower extension
Paper Plot
Paper Plot

---
        Disabling of zero suppression in reco output
- Three Scenarios:
1) No pedestal correction
2) Full pedestal Corrections
3) Pedestal Corrections restricted to signals from Chips
    Remember that there are still 216 entries for the layer in the data files
- General Methodology:
  Subdivision of Runs into BeamTrigger and
  Pedestal Trigger Events (Oscillator Trigger) interleaved with beam events
  Corrections are applied (or not) to pedestal as well as to signal events
  Note: The reconstruction s/w had to be tweaked a bit for that

---
Eigenvalues of Covariance matrix
Scan Point
Results for Scan 1
%sigma^{2}+%sigma^2_{c}
Blue:Pedestals
Red: Signal
- Mostly clear
  prominent
  eigenvalues
=> Coherent
      noise
- Where less
  prominent:
  Still visible
  step
- Fairly flat
  spectrum of
  other
  eigenvalues
- Excellent
  agreement
  between Signal
  and Pedestal
Channel Nr.
Chip

---
Eigenvalues of Covariance matrix
Scan Point
Results for Scan 2
%sigma^{2}+%sigma^2_{c}
Blue:Pedestals
Red: Signal
- Mostly clear
  prominent
  eigenvalues
=> Coherent
      noise
- Where less
  prominent:
  Still visible
  step
- Fairly flat
  spectrum of
  other
  eigenvalues
- Excellent
  agreement
  between Signal
  and Pedestal
Channel Nr.
Chip

---
Eigenvalues of Covariance matrix
Scan Point
Results for Scan 3
%sigma^{2}+%sigma^2_{c}
Blue:Pedestals
Red: Signal
- Mostly clear
  prominent
  eigenvalues
=> Coherent
      noise
- Where less
  prominent:
  Still visible
  step
- Fairly flat
  spectrum of
  other
  eigenvalues
- Excellent
  agreement
  between Signal
  and Pedestal
Channel Nr.
Chip

---
Eigenvalues of Covariance matrix
Scan Point
Results for Scan 4
%sigma^{2}+%sigma^2_{c}
Blue:Pedestals
Red: Signal
- Mostly clear
  prominent
  eigenvalues
=> Coherent
      noise
- Where less
  prominent:
  Still visible
  step
- Fairly flat
  spectrum of
  other
  eigenvalues
- Excellent
  agreement
  between Signal
  and Pedestal
Channel Nr.
Chip

---
New - Elements of Eigenvector
Scan Point
Results for Scan 1
%alpha_{i}
Blue:Pedestals
Red: Signal
- Excellent
  agreement
  between Signal
  and Pedestal
modulo
Sign ambiguity
(known feature
 of PCA)
Reveal channels
with coherent
noise
Channel Nr.
Chip

---
New - Elements of Eigenvector
Scan Point
Results for Scan 2
%alpha_{i}
Blue:Pedestals
Red: Signal
- Excellent
  agreement
  between Signal
  and Pedestal
modulo
Sign ambiguity
(known feature
 of PCA)
Reveal channels
with coherent
noise
Channel Nr.
Chip

---
New - Elements of Eigenvector
Scan Point
Results for Scan 3
%alpha_{i}
Blue:Pedestals
Red: Signal
- Excellent
  agreement
  between Signal
  and Pedestal
modulo
Sign ambiguity
(known feature
 of PCA)
Reveal channels
with coherent
noise
Channel Nr.
Chip

---
New - Elements of Eigenvector
Scan Point
Results for Scan 4
%alpha_{i}
Blue:Pedestals
Red: Signal
- Excellent
  agreement
  between Signal
  and Pedestal
modulo
Sign ambiguity
(known feature
 of PCA)
Reveal channels
with coherent
noise
Channel Nr.
Chip

---
Coherent Noise Level
Scan Point
Results for Scan 1
%sigma^2_{c} cdot %alpha^{2}_{i}
Blue:Pedestals
Red: Signal
Different Patterns
- Concentrated for
  Chip 1 and Chip 3
- Flat spectrum
  for Chip 2 and 4
- Excellent
  agreement
  between Signal
  and Pedestal
- Coherent Noise
  level
  ~1 ADC Count
  in agreement
  with simple
  analysis
Channel Nr.
Chip

---
Coherent Noise Level
Scan Point
Results for Scan 2
%sigma^2_{c} cdot %alpha^{2}_{i}
Blue:Pedestals
Red: Signal
Different Patterns
- Concentrated for
  Chip 1 and Chip 3
- Flat spectrum
  for Chip 2 and 4
- Excellent
  agreement
  between Signal
  and Pedestal
- Coherent Noise
  level
  ~1 ADC Count
  in agreement
  with simple
  analysis
Channel Nr.
Chip

---
Coherent Noise Level
Scan Point
Results for Scan 3
%sigma^2_{c} cdot %alpha^{2}_{i}
Blue:Pedestals
Red: Signal
Different Patterns
- Concentrated for
  Chip 1 and Chip 3
- Flat spectrum
  for Chip 2 and 4
- Excellent
  agreement
  between Signal
  and Pedestal
- Coherent Noise
  level
  ~1 ADC Count
  in agreement
  with simple
  analysis
Channel Nr.
Chip

---
Coherent Noise Level
Scan Point
Results for Scan 4
%sigma^2_{c} cdot %alpha^{2}_{i}
Blue:Pedestals
Red: Signal
Different Patterns
- Concentrated for
  Chip 1 and Chip 3
- Flat spectrum
  for Chip 2 and 4
- Excellent
  agreement
  between Signal
  and Pedestal
- Coherent Noise
  level
  ~1 ADC Count
  in agreement
  with simple
  analysis
Channel Nr.
Chip

---
Incoherent Noise Level
Scan Point
Results for Scan 1
%sigma^2_{i}
Blue:Pedestals
Red: Signal
- Flat spectrum
  for all Chips 2
- Incoherent Noise
  level
~√20 ~4.5 ADC C.
- In agreement with
  G (see above)
  and rms
  (see earlier)
- Excellent
  agreement
  between Signal
  and Pedestal
color red {sqrt{%sigma^{2}_{ic}+%sigma^{2}_{cn}}approx sqrt{4.5^{2}+1} approx 4.6}
Channel Nr.
Chip

---
Incoherent Noise Level
Scan Point
Results for Scan 2
%sigma^2_{i}
Blue:Pedestals
Red: Signal
- Flat spectrum
  for all Chips 2
- Incoherent Noise
  level
~√20 ~4.5 ADC C.
- In agreement with
  G (see above)
  and rms
  (see earlier)
- Excellent
  agreement
  between Signal
  and Pedestal
color red {sqrt{%sigma^{2}_{ic}+%sigma^{2}_{cn}}approx sqrt{4.5^{2}+1} approx 4.6}
Channel Nr.
Chip

---
Incoherent Noise Level
Scan Point
Results for Scan 3
%sigma^2_{i}
Blue:Pedestals
Red: Signal
- Flat spectrum
  for all Chips 2
- Incoherent Noise
  level
~√20 ~4.5 ADC C.
- In agreement with
  G (see above)
  and rms
  (see earlier)
- Excellent
  agreement
  between Signal
  and Pedestal
color red {sqrt{%sigma^{2}_{ic}+%sigma^{2}_{cn}}approx sqrt{4.5^{2}+1} approx 4.6}
Channel Nr.
Chip

---
Incoherent Noise Level
Scan Point
Results for Scan 4
%sigma^2_{i}
Blue:Pedestals
Red: Signal
- Flat spectrum
  for all Chips 2
- Incoherent Noise
  level
~√20 ~4.5 ADC C.
- In agreement with
  G (see above)
  and rms
  (see earlier)
- Excellent
  agreement
  between Signal
  and Pedestal
color red {sqrt{%sigma^{2}_{ic}+%sigma^{2}_{cn}}approx sqrt{4.5^{2}+1} approx 4.6}
Channel Nr.
Chip

---
Matrix B'
Example for central impact Scan 1 – Signal Events
Diagonal: Prominent with value ~20 (ADC Counts)2
Off-Diagonal: Flat with value ~0

---
All matrices B' on request ;-)
        (39 more plots)

---
Spectrum of c-Parameter
Scan Point
Results for Scan 1
n/N
Black:Pedestals
Red: Signal
 - Excellent
   agreement
   between Signal
   and Pedestal
- In future
  application the
  values in these
  spectra can
  be used to
  subtract coherent
  noise!
- Here:
  Spectra used
  as input pdf
  for simulation
  of noise
c-Parameter
Chip

---
Spectrum of c-Parameter
Scan Point
Results for Scan 2
n/N
Black:Pedestals
Red: Signal
 - Excellent
   agreement
   between Signal
   and Pedestal
- In future
  application the
  values in these
  spectra can
  be used to
  subtract coherent
  noise!
- Here:
  Spectra used
  as input pdf
  for simulation
  of noise
c-Parameter
Chip

---
Spectrum of c-Parameter
Scan Point
Results for Scan 3
n/N
Black:Pedestals
Red: Signal
 - Excellent
   agreement
   between Signal
   and Pedestal
- In future
  application the
  values in these
  spectra can
  be used to
  subtract coherent
  noise!
- Here:
  Spectra used
  as input pdf
  for simulation
  of noise
c-Parameter
Chip

---
Spectrum of c-Parameter
Scan Point
Results for Scan 4
n/N
Black:Pedestals
Red: Signal
 - Excellent
   agreement
   between Signal
   and Pedestal
- In future
  application the
  values in these
  spectra can
  be used to
  subtract coherent
  noise!
- Here:
  Spectra used
  as input pdf
  for simulation
  of noise
c-Parameter
Chip

---
Comparison of noise spectra – Model ,-> Data (Pedestal)
Scan Point
Results for Scan 1
n/N
Black: Model
Red: Signal
c-Parameter
Chip

---
Comparison of noise spectra – Model ,-> Data (Pedestal)
Scan Point
Results for Scan 2
n/N
Black: Model
Red: Signal
c-Parameter
Chip

---
Comparison of noise spectra – Model ,-> Data (Pedestal)
Scan Point
Results for Scan 3
n/N
Black: Model
Red: Signal
c-Parameter
Chip

---
Comparison of noise spectra – Model ,-> Data (Pedestal)
Scan Point
Results for Scan 4
n/N
Black: Model
Red: Signal
c-Parameter
Chip

---
Calculation of upper Limits
- Aim: Upper Limits/Probabilities as a function of the Threshold
- Requires calculation of limits with underlying background
Probability Density Function (Frequentist Approach):
color red {f'(n;%lambda_S + %lambda_B)=f(n;%lambda_S+%lambda_B) / sum from{n_B = 0} to {k} f(n_B;%lambda_B ) " f, f' are Poissonnian Densities"}
Presence of Background via numerator (Approach á la Zech NIM A277)
Using this pdf the Confidence Limits/Upper Limits
can be calculated using regular statistics techniques
Here: S. Brandt, Datenanalyse, pp.183
Developed (“c++ fied”) program to calculate upper limits in the presence
of known background.
Background is noise which is present independent of all potential parasitic
effects from the beam

---
 Intermezzo I - χ2/ndf between Data and Model for 'Maïve' Model
Using mean and sigma of pedestal spectra – Positive Hits
Much worse agreement between data and 'naïve' model

---
Intermezzo II – Upper Limits from 'Naïve' Model for Pedestal Events
Using mean and sigma of pedestal spectra – Positive Hits
Much worse:
In particular
Chip 1

---
Intermezzo III – Upper Limits from 'Naïve' Model for Pedestal Events
Using mean and sigma of pedestal spectra – Negative Hits
Also worse
than developped
noise model