## Slide 1: Micromegas analysis results
On behalf of those involved

## Slide 2: Micromegas Modules for TPC
Resistive ink
~3 MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
2 Resistive Kapton
~3 MΩ/□
2

## Slide 3
From December 2008 to July 2010, we tested one module at a time.
December 2009: tested modules 4 and 5 without magnetic field.
March 2010: tested modules 2 (ink) and 3 (kapton) with 1T magnetic field.
June-July 2010: taken data in a high intensity hadron beam at CERN.

## Slide 4
Chart: Ed (V/cm)
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 215 | 230 | 250 | 270 | 290 | 310
Simulations (Magboltz) | 0 | 0.6796 | 1.544 | 2.486 | 3.438 | 4.342 | 5.151 | 5.844 | 6.425 | 6.879 | 7.236 | 7.434 | 7.595 | 7.745 | 7.831 | 7.867 | 7.867
Measurements | 0 | 0.709 | 1.589 | 2.521 | 3.4762 | 4.3892 | 5.2038 | 5.9406 | 6.5076 | 7.0175 | 7.335 | 7.5519 | 7.698 | 7.859 | 7.947 | 7.992 | 7.947
B=0 data : Drift velocity measurements
Vdrift = 7.698 +- 0.040 cm/µs at E=230 V/cm
(Magboltz : 7.583+-0.025(gas comp.))
The difference is 1.5+-0.6 %
Drift Velocity in T2K gas compared to Magboltz simulations for
- P=1035 hPa
- T=19°C
- 35 ppm H20
( T2K gas: Ar:CF4:iso=95:3:2)
Data analysis results (B=0T)

## Slide 5
B=0 data : Drift velocity measurements
Vdrift = 7.698 +- 0.040 cm/µs at E=230 V/cm
(Magboltz : 7.583+-0.025(gas comp.))
The difference is 1.5+-0.6 %
Drift Velocity in T2K gas compared to Magboltz simulations for
- P=1035 hPa
- T=19°C
- 35 ppm H20
( T2K gas: Ar:CF4:iso=95:3:2)
Data analysis results (B=0T)
Asian GEM preliminary results (WP114):
Vd = 7.557±0.001 [cm/μs]
Magboltz (v8.5) : Vd = 7.509±0.002 [cm/μs]
Temperature 290K
Pressure 1atm,
200ppm H2O
E field?

## Slide 6
PRF : Pad Response Function
a measure of signal size as a function of track position
relative to the pad
using pulse shape information to optimize the PRF
The PRF:
is not Gaussian.
can be characterized by its FWHM (z) & base Width (z).


Data analysis results

## Slide 7: PRF(Pad Response Functions) fits, z ~ 5 cm
B=1T data : comparison of resistive ink and Carbon-loaded Kapton
Data analysis results
Γ ~ 4 mm
δ ~ 14 mm
Γ ~ 2.6 mm
δ ~ 10 mm

## Slide 8: Bias (module ink)
Bias before
Bias after
Bias due to non-uniformity can be easily corrected.
±100µm
±100µm

## Slide 9
Position residuals xrow-xtrack
Data analysis results

## Slide 10
Z=5cm
Z=35cm
Z=50cm
MEAN RESIDUAL vs ROW number
Z-independent distortions
Distortions up to 50 microns for resistive paint
Rms 7 micron for CLP film
Uniformity

## Slide 11
Uniformity (B = 0T)
Total charge by row using cosmic-ray events
Using cosmic-ray
Preliminary

## Slide 12
Module 5
Module 4
Data analysis results (B = 0T)
χ2 : 10.6
Ndf: 10
χ2 : 13.9
Ndf: 10
Cd = 315.1 µm/√cm (Magboltz)

## Slide 13
Module_INK
Module_CLK
Data analysis results (B = 1T)
χ2 : 29.1
Ndf: 11
χ2 : 38.5
Ndf: 10
Cd = 94.2 µm/√cm (Magboltz)

## Slide 14: Neff measurement with Micromegas
Averaging B=0T data and B=1T data (excluding ink module):
  Neff = 38.0±0.2(stat) ±0.8 (Cd syst)
  σ0= 59 ± 3 µm
  Note that <1/N> = 47.1 from Heed for 5Gev electrons on 6.84 mm long pads.
  <1/N> = 34.9 for 5.4 mm pads.

## Slide 15
Dependence of resolution with data taking conditions
Chart: 
| 360 | 370 | 380 | 390 | 400
 | 79.7 | 69.2 | 61.5 | 58.5 | 54.6
Resolution at z=5cm (µm)
Vmesh (V)
Chart: Preamplifier Peaking Time(ns)
| 200 | 400 | 500 | 600 | 700 | 1000 | 1500 | 2000
 | 97 | 81.7 | 79.7 | 80.8 | 80.5 | 87.8 | 104 | 121.8
 | 126.6 | 91.8 | 91.4 | 91.7 | 92 | 91.7 | 94.8 | 98.7
Data analysis results (B = 1T)

## Slide 16
Total weight: ~20 kg
Radiation length: 40% (2×1.8 cm of aluminium)
27 cm
40 cm
35cm
11 cm
B field
Bottom
Top
High intensities beam test

## Slide 17
Data were taken with muons mostly at 1 kHz and with hadrons at intensities up to 180 kHz (over a 5 cm x 1cm region) and 150 GeV energy.
drift length: 28.8 mm
electric field: 240 V/cm
Gas mixture: T2K gas
The mesh voltage was 380 V, which corresponds to a gas gain of 2500
The detector peformed perfectly normally, as usual
We also tested a new, faster and multimodule DAQ. We obtained read-out rates of 40 Hz.

## Slide 19: Pad signals at 180 kHz hadrons
High intensity data

## Slide 20: Beam profile (run 565, 14 kHz pions)
High intensity data

## Slide 21
Thank you