## Slide 1: LC TPC 2008-2010
P. Colas for the LC TPC collaboration
PRC at DESY, Zeuthen

## Slide 2: A TPC for the LC
Higgs recoil ZH, Z->µµ
  d (1/PT) = 5. 10-5 GeV-1
Jets in a noisy environment
Continuous 3D tracking
High B required for vertex detector -> good for TPC
Wires have disadvantages at high B: ExB
Wires need to be tensioned -> MPGD
ILD concept

## Slide 3: LC TPC gathers all the actors in R&D for a TPC at a LC
25/38 institutes from 12 countries have signed the MoU
7 institutes are observer.
Most world specialists of TPCs, MPGD, front-end electronics, cooling, etc… are members

## Slide 4
After a decade of small prototype tests in various labs, all the member institutes joined their efforts and resources around the construction and exploitation of a beam test infrastructure in DESY, supported by the FP6 program EUDET. Links exist with RD51 (MPGD R&D).
LC TPC created a speaker’s bureau in 2009 and started a new working group for TPC engineering and integration.
Outline:
The EUDET infrastructure at DESY Hamburg
The prototypes
Results of operation in 2008-2010
Future
www.lctpc.org

## Slide 5: The EUDET facility at DESY Hamburg
SiPM Cosmic
Trigger Setup
LP : part of a
TPC endplate
PCMAG:
superconducting magnet, 1.2 T
e- test beam @DESY
(1GeV/c<p<6GeV/c)
Saclay
KEK
Moving frame
DESY

## Slide 6: The Large Prototype
Field cage:
extrapolable to LC
L=61 cm, f=72 cm
1.2% X°
Slow control:
T,P, O2, H2O
Gas system
Endplate
Sharing infrastructure:
- avoids duplication
- favours communication
HV system
DESY
DESY
Cornell
DESY
Laser calibration
U. Victoria

## Slide 7
S1
S2
Very
Two copper perforated foils separated by an insulator (50 mm). Multiplication takes place in the holes.
Usually used in 2 or 3 stages.
a micromesh supported by 50-100 mm - high insulating pillars. Multiplication takes place between the anode and the mesh
200 mm
GEM
Micromegas

## Slide 8
PLEASE ENTER…

## Slide 9: Beam tests at DESY
From October 2008 to September 2010 several GEM and Micromegas modules were tested in beam at the LP
Micromegas
GEM
Read out by T2K AFTER-based electronics (Saclay)
Read out by ALTRO electronics (EUDET, Lund,CERN)

## Slide 10: 5 Micromegas Modules for TPC
Resistive ink
~3 MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
2 Resistive Kapton
~3 MΩ/□
10
Bulk Micromegas: pillars hold the mesh on the whole surface: no need for frame
Resistive bulk: continuous 2D RC network to spread the charge
CERN
Saclay
Carleton

## Slide 11
24 rows x 72 pads, 2.7-3.2 mm wide, 7 mm long

## Slide 12
Test at CERN (July 2010) at 180 kHz (5 x 2 cm² beam) showed no charging up and stable operation
Peaking time of 200 ns is enough to obtain the best resolution -> 300 ns suffice to distinguish 2 tracks on the same pad
Time issues with the resistive foils?

## Slide 13: Asian GEM Modules for TPC
2-GEM (laser etched, with 100 µm gap, from SciEnergy, Japan), plus 1 gating grid (replaced by a field shaper in Sep. 2010 )
GEMs pegged down by the two arc-shaped stiffeners
KEK
Tsinghua
Saga + other Japan Univ.

## Slide 14
28 pad-rows of 176 -194 pads (pad size ~ 1.1 x 5.4 mm2
Total 5152 pads/modules
3 modules partially equipped (7616 channels)

## Slide 15
Micromegas, with P=1035 hPa, T=292 K, 35-50 ppm H20
Vdrift = 7.698 +- 0.040 cm/µs at E=230 V/cm (Magboltz : 7.583+-0.025(gas comp.))
GEM, with P=1013 hPa, T=290 K, 200 ppm H20
Vdrift = 7.563 +- 0.069 cm/µs at E=230 V/cm (Magboltz : 7.509+-0.024(gas comp.))
Both GEM and Micromegas used T2K gas (Ar:CF4:iso=95:3:2).
Drift velocity measurements
T2K Gas: B=1T
GEM

## Slide 16
Chart: Ed (V/cm)
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 215 | 230 | 250 | 270 | 290 | 310
Simulations (Magboltz) | 0 | 0.6796 | 1.544 | 2.486 | 3.438 | 4.342 | 5.151 | 5.844 | 6.425 | 6.879 | 7.236 | 7.434 | 7.595 | 7.745 | 7.831 | 7.867 | 7.867
Measurements | 0 | 0.709 | 1.589 | 2.521 | 3.4762 | 4.3892 | 5.2038 | 5.9406 | 6.5076 | 7.0175 | 7.335 | 7.5519 | 7.698 | 7.859 | 7.947 | 7.992 | 7.947
Velocity vs drift field with Micromegas
s2 (pad resp.) vs drift distance with GEM
CD = 95.4±0.1 µm/√cm
Magboltz predicts 94.3

## Slide 17
Position residuals xrow-xtrack
Micromegas residual distributions

## Slide 18: Bias inside a row vs track position
Bias before correction
Bias after
Bias due to non-uniformity can be easily corrected.
±50µm
±50µm
Bias after correction

## Slide 19
Uniformity (B = 0T)
Total charge by row using cosmic-ray events
from cosmic-ray tracks
Preliminary
Time of pulse max

## Slide 20
Z=5cm
Z=35cm
Z=50cm
MEAN RESIDUAL vs ROW number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film (red points)
Uniformity
Carbon loaded kapton is much more uniform than resistive ink

## Slide 21
Module 4
Micromegas results (B = 0T & 1T)
Carbon-loaded kapton resistive foil
B=0 T Cd = 315.1 µm/√cm (Magboltz)
Module 3
B=1 T Cd = 94.2 µm/√cm (Magboltz)
χ2/Ndof = 10.6/10
χ2/Ndof = 29.1/11
Averaging B=0T data and B=1T data (excluding ink module):
  Neff = 38.0±0.2(stat) ±0.8 (Cd syst)
  σ0= 59 ± 3 µm
80 µm resolution at 2m in B=3.5 T !

## Slide 22
Resolution with GEMs
3 modules allow a momentum measurement :
1/PT resolution extrapolated to z=0 obtained 0.083 GeV-1 (expected 0.081 GeV-1 )
Using MarlinTPC software

## Slide 23: Micromegas+pixels, GridPix
TimePix chip : 65 000 digital pixels (55 µm x 55 µm) with time and TOT measurement
Single electron capability
Octopuce : 8 chips bounded
on a LP panel.
Next steps within AIDA
Single electron efficiency vs gain determined by counting electrons from a source, assuming some analytic form for avalanche fluctuations
Nikhef Saclay Bonn CERN
e- content and width
of the escape peak

## Slide 24: GEM + Pixels
/cm
2 TimePix quads topped by 3 GEMs

## Slide 25: SOFTWARE
LC TPC developped a common software for reconstruction and simulation of test data: MarlinTPC (based on the ILC software).
This provides input for ILD design and benchmark studies
It includes reconstruction up to hit level (treatment of charge-spreading by resistive anodes to come)
Packages are available for track finding and fitting (Kalman filter, Hough transform, c2 and likelihood)
Calibration and correction methods (alignment, inhomogeneous fields) tools are being set up with the ILD collaboration
DESY, KEK, Bonn, Tsinghua, Victoria, Carleton…

## Slide 26: DESY GEM module
Present GEMs need improved flatness: a design with a thin ceramic support structure is under construction.
The GEMs are stretchless in this design, minimizing the dead space and flattening the gaps. This also allows to reach the dE/dx goal and provides robustness.
Previous studies with MediTPC showed that the ceramic grid (1 mm x 1 mm mullions) has a negligeable effect on single-point resolution.

## Slide 27
Effort to integrate the electronics flat behind the modules : cards with naked wire-bonded chips, special high density flat connectors, tailored protection
Expect noise reduction
Air cooling
“Power-pulsing ready”
Status: Backend and 2 prototype module cards operational, FECs under fabrication.
Test of 1 module soon, construc-tion in 2011 and full tests in 2012
Saclay Carleton
7-module electronics for Micromegas LP test

## Slide 28
Until now used PCA16 preamp and ALTRO filter+ADC
Full chain new S-ALTRO16 chip prototype submitted
Will be mounted on Multi-Channel Modules
Towards new chip 64 channels
CO2 Cooling and power pulsing foreseen (to be tested in a 5T magnet)
S-Altro electronics
The final electronics (could be SALTRO 64) will be usable for both GEM and Micromegas

## Slide 29
New Endplate under study at Cornell:
hybrid Al (for surfaces) and composite (for rigidity)
Or light space frame
Mechanical studies for the ILD TPC within AIDA (DESY-Saclay)
Mechanical engineered design
Deflexion O(150 µm) @ 3 mbar

## Slide 30
Space charge
Study of effects of primary ionisation (curlers and ‘snow’, mainly due to micro-curlers and X rays has started
Also effect of the ‘ion disk’ flowing back in the drift volume at each train crossing will be assessed
Gating is problematic : 50% transmission of gating GEM
  Work at low gain, wire grid?
Background from 150 bunch crossings overlapped with a ttbar event

## Slide 31: Towards the Detailed Baseline
The next milestone of LC TPC is to converge towards a Detailed Baseline Document answering all the open questions
New endplate and field cage designs with reduced material budget
S-ALTRO 16 chip in production
Add He compressors to PCMAG (AIDA-DESY + KEK-TOSHIBA) lowers operation cost and makes the magnet movable
Cooling and power pulsing will be tested (need 5T magnet)
Software developments towards corrections for space charge and field inhomogeneity
TimePix 2 and its readout