## Slide 1: Pions in the SiW ECAL using FNAL 2008 data (CAN-025)
Philippe Doublet
Roman Pöschl
François Richard
CALICE Analysis Meeting, November 8th, 2010

## Slide 2: Introduction
Interactions of pions in the SiW ECAL
Aim to use granularity and energy deposition to classify interactions
And have a look at differences between models in physics lists
CAN paper v2 submitted, now finalising answers to the questions of the EB

## Slide 3: Data samples
We study and compare interactions of pions (π-) with E = 2, 4, 6, 8 and 10 GeV
TB data were recorded at FNAL in 2008 and reconstructed (v0409)
MC data are simulated + digitised for 5 physics lists : QGSP_BERT, FTFP_BERT, LHEP, QGS_BIC and QGSP_BIC (Geant4 9.2)
Calice soft v02-00 is used for both TB and MC data

## Slide 4: Outline
The SiW ECAL (in 2008)
The test beam at FNAL (May & July 2008)
MC simulations
Finding the interaction point
Classification and optimisation
Observables
Ongoing work
Conclusions
Important slides for today’s meeting topic

## Slide 5: The SiW ECAL in 2008
Fully equipped ECAL
3 x 3 wafers of 6 x 6 pads
Sensors = Si pixels of 1 cm x 1 cm  tracking possibilities
Absorber = W
30 layers in 3 different stacks :
  1.4 mm of W
  2.8 mm
  3.6 mm
≈ 24 X0 ≈ 1 λI ≈ half of the hadrons interact inside the ECAL volume
9 Si wafers
Picture of the fully equiped SiW ECAL

## Slide 6: Test beam at FNAL in 2008
3 CALICE calorimeters installed : SiW ECAL, Analogue HCAL, TailCatcher (TCMT)
Triggers : scintillators, Cherenkov counters
Muon cuts added on the basis of simulated muons : < 0.6% remaining
Ask for only one primary track found with the MipFinder
Events left :
E (GeV) | 2 | 4 | 6 | 8 | 10
N evts | 212942 | 126222 | 73590 | 233820 | 454714
Beamline at FNAL

## Slide 7: Monte Carlo simulations
For comparisons, different physics lists were simulated in Geant4 9.2
QGSP BERT is used as reference for optimisation
E (GeV) | 2 | 4 | 6 | 8 | 10
QGSP BERT | BERT |  |  |  | BERT + LEP
QGS BIC | LEP (+ BIC for secondaries < 1.2 GeV) |  |  |  | 
QGSP BIC | LEP |  |  |  | 
LHEP | LEP |  |  |  | 
FTFP BERT | BERT |  | FTFP |  | 
Content of the physics lists for pions

## Slide 8: A look at interactions of hadrons
Picture of a generic interaction in the calorimeters :
  A primary track enters the detector (« MipFinder »)
  The interaction occurs
  Secondaries emerge from the interaction zone

## Slide 9: Visual examples (1/2)
2D profiles of an event at 10 GeV in the SiW ECAL
High energy deposition when the interaction starts
Interaction layer confirmed by visual inspection
Large number of secondaries created
Equation to be satisfied:
Ecut
TB data event at 10 GeV

## Slide 10: Visual examples (2/2)
Previous example not always valid, especially at low energies
Sometimes, slow increase in energy
Here, local energy deposition
Quantified by the relative increase in energy:
Secondary proton (from MC)
MC event at 2 GeV

## Slide 11: Classification
High energy deposition  « FireBall »
Increase continues + veto for backscattering  « FireBall »
Event view of the « FireBall » type at 10 GeV
Works here and meant for small energies

## Slide 12: Classification
High energy deposition  « FireBall »
Increase continues + veto for backscattering  « FireBall »
Local increase  « Pointlike »
Remark : delta rays are naturally included in « Pointlike » but contribute less than 4%
Event view of the « Pointlike » type at 2 GeV
Real TB data event at 2 GeV

## Slide 13: Classification
High energy deposition  « FireBall »
Increase continues + veto for backscattering  « FireBall »
Local increase  « Pointlike »
Others = non interacting
  « MIP »
  « Scattered »
Remark : delta rays are naturally included in « Pointlike » but contribute less than 4%
3 cm !
Event view of the « Scattered » type at 2 GeV
Real TB data event at 2 GeV

## Slide 14: Optimisation
Cuts need to be optimised (not discussed today, see my talk at CASABLANCA)
After optimisation 
Choice was made to merge all Fcut to one single value for simplicity
E (GeV) | Ecut | Fcut
2 | 3 | 4  6
4 | 8 | 5.5  6
6 | 10 | 6.5  6
8 | 13 | 7  6
10 | 10 | 6  6

## Slide 15: Efficiencies after optimisation
The efficiency to find the true interaction layer within ±1 and 2 layers is the result of the optimisation.
It is compared with another method.
E (GeV) | η (±1) | η (±2) | η (3-4, ±2)
2 | 56 % | 67 % | 28 %
4 | 60 % | 73 % | 61 %
6 | 62 % | 76 % | 69 %
8 | 64 % | 78 % | 71 %
10 | 72 % | 84 % | 76 %

## Slide 16: Rates of interactions
2 GeV
4 GeV
6 GeV
8 GeV
10 GeV
Small systematics with Ecut and Fcut in ±1
Interaction rates similar between physics lists

## Slide 17: Observables
The following results are still under discussion with the EB
We compare TB data and MC using
  Rates of interactions (previous slide)
  Mean shower radius (rms of transverse profile)
  Longitudinal profile (as defined in the CALICE pions in the SiW ECAL paper)

## Slide 18: Examples
Mean shower profile (log)
Longitudinale profile
Example of data vs QGSP_BERT simulation at 2 GeV

## Slide 19: Ongoing
Agreement with hadrons in SiW ECAL paper
Redoing style of the figures
Text improvement on comparison data – MC
Quantitative check of systematics of optimisation with physics lists
Write a new version of the note

## Slide 20: Conclusions
Interactions of hadrons in the SiW ECAL at energies from 2 GeV to 10 GeV are found and classified into 4 kinds, using energy deposition and high granularity
Efficiencies to reconstruct the interaction layer within ± 2 layers are > 67 %
Still answering to the EB (good progress)
Hope for a validation before the end of the year