## Slide 1
Laurent Royer, J. Bonnard, S. Manen, P. Gay
LPC Clermont-Ferrand
R&D activity @ pole MicRhAu
dedicated to High Granularity Si-W Ecal
The CALORIC chip

## Slide 2: Readout Electronics for High Granularity Ecal
2
Electrical specifications of the readout electronics:
  Dynamic range of the signal delivered by a Si-diode : from MIP (4 fC) to 2500 MIPs (10 pC)
  Level of noise limited to 1/10 MIP  SNR ≥ 10
  Error of Linearity:
    < 0.1 % up to 10 % of the dynamic range (1 pC)
    < 1% from 10 % and 100 % of the dynamic range
  Power budget limited to 25µW per channel
Axes of developments @ MicRhAu:
  Synchronous (with beam) analog signal processing: shaping with Gated Integrators, latched comparators
  Fully differential architecture, except for the Charge Sensitive Amplifier (CSA)
  One low-power ADC attached to each channel
  Use of a pure CMOS technology, no bipolar transistors

## Slide 3: First prototype channel
3
A VFE channel performing the amplification, the filtering, the memorization and the digitalization of the charge from Si detector has been designed and tested.
  Global Linearity better than 0.1 % (10 bits) up to 9.5 pC (2375 MIP).
  ENC = 1.8 fC (0.5 MIP) with a single gain stage
  Power consumption with power pulsing estimated to 25µW (no digital part).
Status report presented at Desy in July 2010

## Slide 4: The CALOrimetry Readout Integrated Circuit
4
Low noise CSA
Low-gain shaper
12-bits cyclic ADC
ADC
4
New chip designed and now ready to be sent to foundry (CMP run of 14th February)
Technology AMS CMOS 0.35 µm
Architecture of CALORIC based on the previous channel tested, with some improvements:
Reduction of the power consumption of the CSA
Reduction of the noise of the amplifier of the Gated Integrator
Increase of the analog memory depth to 16
Fully power pulsed
x16

## Slide 5: The CALOrimetry Readout Integragted Circuit
5
Low noise CSA
Low-gain shaper
12-bits cyclic ADC
ADC
High-gain shaper
4
Gain discri.
Threshold
A High-Gain (about x 20) channel added to reach the MIP-to-noise ratio of 10.
A discriminator indicates the dynamic range of the signal  select the signal to be converted
x16
x16

## Slide 6: The CALOrimetry Readout Integragted Circuit
6
Low noise CSA
Low-gain shaper
12-bits cyclic ADC
ADC
High-gain shaper
4
High-gain shaper
Amplifier
x5
Gain discri.
Trigger discri.
Analog part
x16
x16
A Trigger channel added to select events over the MIP
 The trigger signal determinates if the active memory cell is reset or the signal kept into memory

## Slide 7: The CALOrimeter Readout Integrated Circuit
7
Low noise CSA
Low-gain shaper
12-bits cyclic ADC
ADC
High-gain shaper
4
High-gain shaper
Amplifier
x5
Gain discri.
Trigger discri.
Digital Block
(State Machine)
12
Output
data
Control of the channel
Thresholds
Analog part
x16
x16
A digital block controls the chip

## Slide 8: Global State Machine
8
IDLE
Analog signal
processing
WAIT for 198 ms
No power
1 ms max.
Up to 16 events stored
< 1 ms
A/D conversion
x events stored
End of the beam train
DAQ
(not implemented)
All events converted
Bunch Crossing
Wake Up
Master clock of 20 MHz

## Slide 9
9
Timing of the analog processing
t = 0 ns: event synchronous w/ beam
+ 200 ns: decision of the trigger comparator
+ 250 ns: decision of gain comparator
+ 300 ns: end of integration: reset or memorization
+ 350 ns: ready to process next event
Output signal of the CSA
Output signal of the trigger channel
Output signal of high-gain channel
Output signal of the low-gain channel
Signal delivered by the Si-diode
Notes: Carge delivered

## Slide 10: Layout of CALORIC
10
Gated Integrator and the 32 memory cells
CSA, trigger channel and comparators
The cyclic ADC
The digital block

## Slide 11: Simulated performance
11
Gain-2 channel
Gain-20 channel
pC
LSB
LSB
pC
INL < 0.1%
INL < 1%
  ENC (rms value) = 0.4 fC = 2400 e- = MIP/10
  with the High-Gain channel and Cdetector = 30 pF

## Slide 12: Power consumption
12
Chart: 
| CSA | G.I.x20 | G.I.x2 | Amp. Trigger | Digital | Icc Amp.
 | 2.5 | 1.3365 | 1.3365 | 2.178 | 0.14 | 0.4356
 | 1 | 1.035 | 1.035 | 1.035 | 2 | 1.035
 | 12.5 | 6.9164 | 6.9164 | 11.2711 | 1.4 | 2.2542
 | 0.29296 | 0.1621 | 0.1621 | 0.26416 | 0.032812 | 0.052833
CSA
Trigger channel
Gain-2 channel
Gain-20 channel
Evaluation using power pulsing with the ILC duty cycle:
 45 µW per channel

## Slide 13: Conclusion and perspectives
The CALORIC chip is ready for fabrication.
Simulated performance is in agreement with the requirements of Calice, except power consumption.
The first measured performance is expected before summer.
A multi-channel chip should be submitted for fabrication before the end of 2011
 compatible with Calice DAQ
 compatible with pinout of FEV board for test