## Slide 1
D. Attié, P. Baron, D. Calvet, P. Colas, C. Coquelet, E. Delagnes,
R. Joannes, A. Le Coguie, S. Lhenoret, I. Mandjavidze, M. Riallot, E. Zonca
TPC Electronics: SALTRO Status & Evolution
May 10th, 2011
Status of AFTER
7 module integration for the Micromegas Large Prototype
Notes: I’m here to present a TPC review

## Slide 2: Overview of our roadmap
Detector
Baseline
Document
Large Prototype TPC
Resitive Micromegas
ILD-TPC

## Slide 3: T2K electronics
AFTER-based electronics (72 channels/chip) from T2K experiment:
  low-noise (700 e-) pre-amplifier-shaper
  100 ns to 2 μs tunable peaking time
  full wave sampling by SCA
  Zero Suppression capability
Bulk Micromegas detector: 1726 (24x72) pads of ~3x7 mm²
  frequency tunable from 1 to 100 MHz (most data at 25 MHz)
  12 bit ADC (rms pedestals 4 to 6 channels)
  pulser for calibration

## Slide 4
AFTER
511 cells
SCA
FILTER
100ns<tpeak<2us
CSA
1 channel
x72(76)
76 to 1
BUFFER
SCA MANAGER
SLOW CONTROL
Serial Interface
W / R
Mode
CK
CK
ADC
TEST
In Test
120fC<Cf<600fC
Power Supply
Reference Voltage
Reference Current
Asic Spy Mode
CSA;CR;SCAin (N°1)
Power
On
Reset
Design features:
72 channels x 511 analog memory cells; Fwrite: 1-50 MHz; Fread: 20 MHz
4 Charge Ranges (120 fC; 240 fC; 360 fC & 600 fC)
Supports positive or negative input signals
16 Peaking Time Values (100 ns to 2 µs)
Asic
For
Tpc
Electronic
Read-out

## Slide 5: Beam data sample
B = 1T
T2K gas
Peaking time: 100 ns
Frequency: 25 MHz
z = 5 cm

## Slide 6: Two detectors at B=1T, z ~ 5 cm
Resistive Kapton
Resistive Ink
RUN 310
vdrift = 230 cm/μs
Vmesh = 380 V
Peaking time: 500 ns
Frequency Sampling: 25 MHz
RUN 549
Vdrift = 230 cm/μs
Vmesh = 360 V
Peaking time: 500 ns
Frequency Sampling: 25 MHz

## Slide 7: Integrated electronics for 7 module project

## Slide 8: 7-module Micromegas project for the Large Prototype TPC

## Slide 9: Integrated electronics for 7 module project
Remove packaging and protection diodes
Wire –bonding on board for AFTER chips
Use 2 × 300 pins connector
Replace resistors SMC 0603 by 0402 (1 mm × 0.5 mm)
25 cm
14 cm
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
3,5 cm
3,5 cm
FEC
Chip

## Slide 10: Design of the integrated electronics

## Slide 11: Design of the integrated electronics

## Slide 12: Front-End Mezzanine (FEM)
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
30 pins
connector
FPGA
Xilinx V5
ADC
SRAM
Optical
connector
Test Pulser
Xilinx
Prom

## Slide 13: Front-End Card (FEC)
4 chips per FEC wire bonding on the 8-layer PCB
Protections: a resistor (0201 SMC) at each channel input
  A0: 0Ω
  A1: 3Ω
  A2: 5,1Ω
  A3: 10Ω
Temperature measurement device for each FEC

## Slide 14: First prototype of the electronics

## Slide 15: Back-end Hardware
ML523 development kit from Xilinx
  vc5vfx100t FPGA from Virtex-5 device family
    Embedded PowerPC
    16 Multi Gigabit Transceivers
    Embedded Ethernet MAC
  128 Mbyte DDR2 memory
  RS232 interface
Up to 3 4-channel SMA-SFP interface cards
  2 Gbit/s optical transceivers for FE links (×12)
  RJ45 Ethernet transceiver for the DAQ link
Trigger – Clock – Fast Control link mezzanine card
  To be developed according to the link specifications

## Slide 16: Temperature during switching on
Chart: Temperature (°c)
| 2 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 135
FEC 0 | 29 | 34 | 39 | 41 | 43 | 44 | 44 | 45 | 45 | 45 | 45 | 46 | 46 | 46 | 46
FEC 1 | 30 | 36 | 43 | 46 | 49 | 50 | 51 | 51 | 51 | 51 | 51 | 52 | 52 | 52 | 53
FEC 2 | 30 | 37 | 44 | 48 | 50 | 52 | 52 | 53 | 53 | 53 | 53 | 54 | 54 | 54 | 54
FEC 3 | 30 | 37 | 45 | 49 | 51 | 52 | 53 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 55
FEC 4 | 30 | 37 | 44 | 47 | 49 | 51 | 51 | 52 | 52 | 52 | 52 | 52 | 53 | 53 | 53
FEC 5 | 29 | 34 | 39 | 41 | 43 | 44 | 44 | 44 | 45 | 45 | 45 | 45 | 45 | 45 | 46
FEMI | 30 | 37 | 42 | 45 | 47 | 47 | 48 | 48 | 49 | 49 | 49 | 49 | 49 | 49 | 49
Temperature in the hall

## Slide 17: Temperature after cooling
Chart: Temperature (°c)
| 1 | 5 | 10 | 15 | 20 | 25 | 30 | 31 | 33 | 35 | 40 | 45 | 46 | 48 | 50 | 55 | 60 | 70
FEC 0 | 45 | 43 | 42 | 41 | 41 | 40 | 40 | 40 | 39 | 39 | 38 | 38 | 38 | 38 | 38 | 37 | 37 | 37
FEC 1 | 52 | 49 | 47 | 46 | 46 | 46 | 45 | 45 | 44 | 43 | 43 | 42 | 42 | 42 | 41 | 41 | 41 | 41
FEC 2 | 54 | 52 | 50 | 48 | 48 | 48 | 48 | 47 | 47 | 46 | 45 | 45 | 44 | 44 | 44 | 43 | 43 | 43
FEC 3 | 54 | 53 | 51 | 49 | 49 | 49 | 48 | 48 | 47 | 47 | 46 | 45 | 45 | 44 | 44 | 44 | 43 | 43
FEC 4 | 53 | 51 | 49 | 48 | 48 | 47 | 47 | 46 | 46 | 45 | 44 | 44 | 43 | 43 | 43 | 42 | 42 | 42
FEC 5 | 46 | 45 | 44 | 43 | 42 | 42 | 42 | 41 | 41 | 40 | 40 | 39 | 39 | 38 | 38 | 38 | 38 | 38
FEMI | 47 | 44 | 42 | 41 | 41 | 41 | 40 | 40 | 39 | 38 | 37 | 37 | 37 | 36 | 36 | 36 | 35 | 35
Increasing of the Nitrogen flow
Temperature in the hall

## Slide 18: Event samples in B=1T
Commissioning last week in 5 GeV electron beam at DESY:

## Slide 19: Conclusion
The first module is currently testing in DESY we should definetly validate the integrated AFTER-based electronics
New concepts have been used and validated: flat high-density, zero-extraction-strength connectors, naked chips on board, and many improvements to the T2K readout: latest ADCs, FPGAs
Now entering the production phase for 7 modules (+ 2 spares) to equip the Large Prototype TPC endplate. This production will also be a semi-industrial production and a proof of feasability, meeting the LOI specs