## Slide 1: Drive Beam Injector RF Structures
Hamed Shaker
School of Particles and Accelerators, Institute for Research in Fundamental Sciences, Iran ; CERN , Switzerland
“Hayy Ibn Yaqzân”
by “Ibn Tufail” from Granada region
Translated by Simon Ockley

## Slide 2: CLIC Drive Beam Injector Layout
Gun
Bucking coil
PB
Buncher
SHB 1-2-3
Acc. Structures
Quadrupoles
Magnetic chicane
Slit
Solenoids
Energy = 140 KeV
Energy = 53 MeV
Energy = 26 MeV
CLIC DB Injector (CDR) | Field (MV/m) | Length (cm) | Voltage (KV)
Gun |  |  | 140 (β=0.62)
SHB - I | 0.224 | 15.6 | 35
SHB - II | 0.234 | 15.6 | 36.5
SHB - III | 0.249 | 15.6 | 38.8
PB | 1.2 | 6 | 72
Buncher | 4.2 | 168.1 | 
Acc Cavity - I | 4.6 (Average) | 99.98 | 
The values was found by S. Bettoni et al. [1] during CLIC DB Injector design and optimization.
The accelerating structures are designed and optimized for 4.2 A beam current after the magnetic chicane but the beam current is 6 A before the magnetic chicane. Then to keep the same structure and the same input power we should change the input phase.
Initial design of RF structures was started with these numbers. But these values should be corrected afterward depend on the structure and the power source restrictions.

## Slide 3: Powering Layout
PB
Buncher
Accelerating cavity
SHB-I
SHB-II
SHB-III
Gun
PB - II
15 MW
15 MW
?
?
?
15 MW
The power source for the accelerating structure was chosen by Erk Jensen (his presentation in the evening) and the accelerating structure is designed and optimized based on that by Rolf Wegner.
S. Bettoni et al. assumed a constant gradient structure for the buncher with 4.2 MV/m axial electric field with beam loading. By a raw calculation we can see about 27 MW input power is needed for 6 A beam current and 1 m structure length. This calculation comes from this fact that about 90% percent of the input power is consumed by beam. The electric field could not keep constant anymore at the end of buncher and the structure length should be shortened to 1 m instead of 1.68 m. And the rest power (about 3 MW) can be used for one or two prebunchers.
 | Field (MV/m) | Length (cm) | Voltage (KV) | Input Power (CTF3 rescaling)
Gun |  |  | 140 | 
SHB - I | 0.224 | 15.6 | 35 | 1.1 MW
SHB - II | 0.234 | 15.6 | 36.5 | 1.2 MW
SHB - III | 0.249 | 15.6 | 38.8 | 1.4 MW
PB | 1.2 | 6 | 72 | 686 KW
Scaling from the CTF3
The SHBs structures should be changed to reduce the input power and this talk is more focused on this topic. to scale, using this fact that The CTF SHBs have the same length and their voltages are 20 KV with 40KW input power[2,3].
To scale the prebuncher, I used the CTF3 data (27.5 KV voltage with 100 KW input power).

## Slide 4: Accelerating Structure
gapn
RBP
E0T(n)
Vacc
Ncells
Pout
Pin
Pb
Pb
SICA structure with constant aperture
η= ΔPb/Pin
tfill
mode spectrum
constant free parameter
vgr,n tapering
Ra,n
φn=120⁰
Borrowed from Rolf Wegner [4]

## Slide 5: Baseline structure, 19 cells, RB=49 mm
Pin = 15 MW RB = 49 mm, N = 19 cells
Borrowed from Rolf Wegner [4]
Energy gain =3.4 MeV
Length = 1.8996m
Average electric field≈1.8 MV/m.
These numbers are different from S. Bettoni et al. model then the model should be corrected.

## Slide 6: SICA – GdfidL simulations
input
output
SiC dampers
nose cones
Input and output coupler design finished
Correct match, input reflection < 30 dB.
(red and green: two different geometries; red is final)
beam
Rolf Wegner
Borrowed from Erk Jensen [5]

## Slide 7: Sub Harmonic Bunchers
Phase coding
180 phase switch
Acceleration n0
Deflection n0 / 2
Sub-harmonic bunching n0 / 2
odd buckets
even
buckets
  RF deflector n0 / 2
Gap creation and combination
Sub Harmonic Bunchers (SHBs) works at 499.75 MHz that is half of the frequency of the rest structures (999.5 MHz). The main challenge for SHBs is the fast phase switching capability of these structures (about 10ns).

## Slide 8: Filling time choosing
Borrowed from Oleksiy Kononenko [6]
In the normal case the time interval between phase switching is constant (243.7 ns). In the Oleksiy model these intervals are not constant to have better energy dispersion at the end of main beam linac. It also give us an idea that how much the filling time should be. The result shows us it should be less than 18ns. In this talk I use 10ns as the filling time similar to CTF3 SHBs.

## Slide 9: Fundamental Equation
Standing Wave Structure
Travelling Wave Structure
P
Load
V , τ
P
Load
V , τ
Forward Travelling Wave structure
Backward Travelling Wave structure
For the known gap voltage and filling time our goal is to increase R/Q to reduce the input power.
τ=10ns
V=36.5 KV
Pd : Power disappears on surface.
β : Coupling coefficient
Qe = ωτ : External quality factor
τ : Filling time
R : Effective shunt impedance
R’: Effective shunt impedance per length
Q : Unloaded quality factor
P: Source power
V : Gap voltage
W’ : Stored energy per length
L: Structure length
vg : Group velocity
n : Cell numbers
…
P
P/n V/n , τ
P/n V/n , τ
P/n V/n , τ
Load

## Slide 10: Phase Switching Model and the Power Source Bandwidth
C
B
A
At f0fs (499.75  50 MHz) frequencies the amplitude is half of f0 frequency. By this fact that the bandwidth is measured from the frequencies that power consumption is half , the BW is about 57.7 MHz or 11.5%.
The BW of CTF3 SHBs sources - that are TWT structures -are about 160 MHz (10.7 %) then they have capability of phase switching at less than 4 ns.

## Slide 11: Effective filling time in a SW structure
To see what is the behaviour of a single cell SW structure I used a simple RF circuit [7] with the input from last slide. τ=10 ns and Q=ωτ=10π. It is about 39 ns between two 80% electric field level after phase switching.
It can be introduced by this fact that the BW/f0 is equal to 1/Q then the BW is equal to 15.9 MHz. By the fact that 57.7 MHz bandwidth is needed for 10ns phase switching, the phase switch for this SW structure should be around 36 ns – close to 39 ns - .

## Slide 12: Effective filling time in a TW structure-I
In a TW structure with n cells and the total filling time(τ) defined by length/group velocity, the filling time of each cell is equal to τ/n. Then the external Q for one cell is equal to ωτ/n. It means that the BW for this structure is n times more than a single cell SW structure. The pass band is about two times more than the BW for these structure. Now if we use 4 cells structure with 10ns filling time the BW is equal to 63.7 MHz and the pass band is equal to 127.3 MHz. It means this structure accept all the frequencies are needed for 10ns phase switching or less but still it takes 10ns to fill the whole structure. It is a description why for a TW structure, effective filling time is more or less equal to standard filling time.
I haven’t modeled a TW structure during phase switching but we have data from CTF3 SHBs at the moment. The filling time is about 11ns for CTF SHBs. In these structures, group velocity and phase velocity are 4.8% and ~62% of light speed, respectively and in the same direction. It means the beam sees 10ns for the phase switching.
For CTF3 SHBs with 6 cells the structure pass-band is equal to 173.6 MHz and the BW is equal to 86.8 MHz (75.5±(20,22.5)°). A raw calculation – but not exactly correct - gives us about 6.6 ns for the transient time for the phase switching that is close to streak camera measurement that you can see in the next slide.

## Slide 13: Effective filling time in a TW structure-II
The streak camera measurement at the end of the CTF3 linac shows transient time less than 10 ns(~ 6 ns).
There is one description by Roberto Corsini from the sensitivity studies done by A. Vivoli [8] . This graph shows the final phase variation (end of the linac) around 0° and 180° SHBs input phase. This graph shows it takes at least 40° less for the final phase switching then it is about 7.7 ns.
With similar filling time for a single cell SW structure and a TW structure, it seems the effective filling time for the SW case is about four times more. Then a TW structure should be our choose.

## Slide 14: Pill Box Model – TM010 mode
a
g
Chart: Phase advance per cell (deg)
Chart: Phase advance per cell (deg)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
 | 0 | 0.0871 | 0.17321 | 0.25734 | 0.33856 | 0.41596 | 0.48868 | 0.55596 | 0.6171 | 0.6715 | 0.71865 | 0.75815 | 0.78972 | 0.81318 | 0.82847 | 0.83564 | 0.83486 | 0.82638 | 0.81057 | 0.78789 | 0.75887 | 0.72411 | 0.68428 | 0.64009 | 0.59229 | 0.54164 | 0.48891 | 0.43487 | 0.38027 | 0.32584 | 0.27226 | 0.22017 | 0.17015 | 0.12271 | 0.078302 | 0.0373 | 1.0755e-06
Maximum at 133.5°
Maximum at 77°

## Slide 15: CTF3 case – Forward TW structure
It means the minimum input power needs using the fundamental equation is around 1.11MW for CLIC DB injector.
Related to pill-box model and by attention to the disk thickness, the maximum R/Q is at 85° phase advance but 75.5° was chosen for CTF3 SHBs before detuning for beam loading compensation.
The best thing was done for the CTF3 SHBs with Forward TW structure and it can not be reduced so much then we should look for another structure type.
Chart: R/Q per cell for 75.5° phase advance per cell
| 0.13 | 0.78 | 2.09 | 2.94 | 3.8 | 4.9000000000000004 | 5.95 | 6.74 | 7.99 | 8.9500000000000028 | 9.9
HFSS simulation | 73.28 | 55.45 | 38.64 | 31.53 | 26 | 20.33 | 16.02 | 13.47 | 9.99 | 7.79 | 6.08
Pill Box model | 88.7
Chart: Total R/Q for 75.5° phase advance per cell
| 0.13 | 0.78 | 2.09 | 2.94 | 3.8 | 4.9000000000000004 | 5.95 | 6.74 | 7.99 | 8.9500000000000028 | 9.9
HFSS simulation | 3.6615 | 16.6235 | 31.0391 | 35.6285 | 37.9737 | 38.2877 | 36.6358 | 34.8942 | 30.6788 | 26.797 | 23.1348
Pill Box model | 0
Maximum is around 4.8% that was chosen for CTF3 SHBs.
From L. Thorndahl presentation [2] for 4 cells model. Finally 6 cells structure was chosen.
The group velocity is increased by increasing the iris radius. The iris radius is about 10cm for 4.8% group velocity.

## Slide 16: Backward TW structure
l
g
g
rb
rn
θ1
θ2
r1
r2
t/2
rc
lc
θc
g/l | ≈0.51
rb | 25 mm
rn | 5 mm
θ1 | 30°
θ2 | 24°
t (disk thickness) | 18 mm
This design is based on the LEP cavity [9].

## Slide 17: R/Q and Vg vs. Coupling angle
Frequency | 499.75 MHz
l (for 75.5° phase advance per cell) | 78mm
r1 | 176 mm
rc | 171 mm
lc | 45 mm
r2 is changed to keep resonant frequency constant.
Chart: Group velocity vs. Coupling angle
| 90 | 80 | 70 | 60 | 50 | 40 | 30
 | 16.89 | 12.23 | 7.97 | 4.9 | 2.74 | 1.34 | 0.52
Chart: R/Q per cell vs. Group velocity
| 16.89 | 12.23 | 7.9700000000000024 | 4.9000000000000004 | 2.74 | 1.34 | 0.52
 | 87.08 | 90.28 | 90.93 | 90.05 | 88.42 | 86.63 | 84.34
Chart: R/Q vs. Group velocity
| 16.89 | 12.23 | 7.9700000000000024 | 4.9000000000000004 | 2.74 | 1.34 | 0.52
 | 565.41 | 424.46 | 278.6 | 169.55 | 93.01 | 44.63 | 16.83
R/Q per cell is weakly depend on the magnetic coupling angle. It means that total R/Q is linear vs. group velocity because the cell numbers is linearly dependent on group velocity.
We can keep the beam hole radius as small as possible(rb) to have higher R/Q per cell. Then we can increase the group velocity by using magnetic coupling holes and it means more cell numbers.

## Slide 18: Optimization
number of cells | Phase advance per cell (deg) | Vg/c(%) | R/Q - cell (Ω) | R'/Q (Ω/m) | R/Q (Ω) | Input power (KW) | r1 (mm) | r2 (mm) | rc (mm)
3 | 122 | 12.79 | 149.15 | 1183.3 | 453.71 | 93.46 | 159 | 174 | 154
4 | 110 | 15.17 | 131.82 | 1160.21 | 527.73 | 80.34 | 163 | 173 | 158
5 | 98 | 16.74 | 117.59 | 1161.44 | 582.93 | 72.74 | 166 | 177.7 | 161
6 | 86 | 17.79 | 99.91 | 1124.49 | 599.61 | 70.79 | 173 | 178.8 | 167.8
7 | 62 | 15.02 | 66.33 | 1035.47 | 466.31 | 90.98 | 187 | 191 | 182
The maximum R/Q was found with HFSS for each cell numbers for θc=90°
Chart: Number of cells
| 3 | 4 | 5 | 6 | 7
 | 93.46 | 80.34 | 72.74 | 70.79 | 90.98
Chart: Number of cells
| 3 | 4 | 5 | 6 | 7
 | 453.71 | 527.73 | 582.93 | 599.61 | 466.31
Chart: Number of cells
| 3 | 4 | 5 | 6 | 7
 | 1183.3 | 1160.21 | 1161.44 | 1124.49 | 1035.47
R’/Q seems to be constant then we can imagine that the maximum R/Q is close to 90° phase advance because the group velocity is maximum.
I think the best option to have limited cell numbers is the 4 cells structure with 110° phase advance that needs 80 KW input power.
If we have allowed to increase filling time, then by using 4 and 5(6) cells for 122° and 110° structures, respectively, we can reach to 52.6 KW and 51.2(35.6) KW power.

## Slide 19: Optimization - II
number of cells | phase(deg) | vg/c(%) | R/Q - cell (Ω) | R'/Q (Ω/m) | R/Q (Ω) | Input power (KW) | r1(mm) | r2(mm) | rc(mm) | θc(deg) | lc(mm) | rn(mm) | t(mm) | g/l | phase velocity/c
3 | 105 | 10.86 | 142.76 | 1337.61 | 428.28 | 100.79 | 169.8 | 186.35 | 164.9 | 75 | 49.04 | 6.13 | 12.26 | 0.45 | 0.61
3 | 120 | 12.2 | 163 | 1336.35 | 489 | 86.81 | 152.9 | 167.8 | 148.49 | 89 | 44.16 | 5.52 | 11.04 | 0.44 | 0.61
4 | 105 | 14.34 | 142.16 | 1331.96 | 568.64 | 75.04 | 159.55 | 175.1 | 154.94 | 87 | 46.08 | 5.76 | 11.52 | 0.46 | 0.61
5 | 105 | 16.14 | 126.89 | 1314.05 | 634.45 | 67.07 | 162.88 | 178.75 | 158.17 | 95 | 47.04 | 5.88 | 11.76 | 0.54 | 0.61
another HFSS models with a little better R/Q
It is possible to reduce the power a little. For example to 75 KW from 80 KW in last slide.
After choosing the structure we can work to optimize cells depend on all parameters affect the design like beam loading, HOMs, minimum wall thickness for cooling water pipe holes and ...
It is the definition of drain time as was introduce by L. Thorndahl et al.[2] . This time is used to find the number of bunches passages during phase switching. For FTW case it is about 8% less (τ’≈9ns) and for BTW case it is about 20 % more than filling time(τ’≈12ns).

## Slide 20: Standing Wave structure
Chart: Phase advance per cell (deg) = kg/β
| 122 | 110 | 98 | 86 | 62
BTW cells | 149.15 | 131.82 | 117.59 | 99.91 | 66.33
SW cells | 173.68 | 186.09 | 193.21 | 209.06 | 219.44 | 226.68 | 223.62 | 212.45
Maximum is around 230°
Chart: Number of cells
| 3 | 4 | 5 | 6 | 7
BTW cells | 453.71 | 527.73 | 582.93 | 599.61 | 466.31
SW cells | 453.36
Chart: Number of cells
| 3 | 4 | 5 | 6 | 7
BTW cells | 93.46 | 80.34 | 72.74 | 70.79 | 90.98
SW cells | 93.5516
As mentioned briefly, most power is reflected because of low external Q (≈ 31.4 for τ=10ns) to have small filling time. In the case of beam loading the external Q can be increased to use a fraction part of reflected power to compensate beam loading then we have not need more input power except the beam loading consuming power exceeds the input power. Maximum 13.3 (16.5) KV beam voltage gain for 80(100) KW input power.
As another options , we can use the SW structure with two single cells with two power coupling like a TW structure.
By using two single cells at 230° phase advance we just need 93.5 KW that it is 17% more than 80KW for the 110° four cells BTW structure. If we want to keep drain time at 10ns for BTW structure then it needs about 120KW input power that it is about 30% more than SW case.
…
P
P/n V/n , τ
P/n V/n , τ
P/n V/n , τ
Load
The main idea from Alexej

## Slide 21
Borrowed from L. Thorndahl [2]
It is the fundamental theorem of beam loading. This equation is based on circuit convention then we need to divide it by two for our convention.
At CTF3, the SHBs are detuned to turn more than 360° between bunch passage to compensate negative real phasor but with the negative group velocity, this number should be smaller than 360° .

## Slide 22: Beam Loading Compensation
Chart: Detuning angle vs. Input power for 10ns filling time
| 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190 | 195 | 200
 | 31.3852 | 27.8979 | 25.1081 | 22.8256 | 20.9234 | 19.3139 | 17.9344 | 16.7388 | 15.6926 | 14.7695 | 13.949 | 13.2148 | 12.5541 | 11.9563 | 11.4128 | 10.9166 | 10.4617 | 10.0433 | 9.657 | 9.2993 | 8.9672 | 8.658 | 8.3694 | 8.0994 | 7.8463 | 7.6085 | 7.3847 | 7.1738 | 6.9745 | 6.786 | 6.6074 | 6.438 | 6.277
I= 6 A
V= 36.5 KV
τ = 10 ns
ω = 2π x 499.75 MHz
F= bunch form factor = 1 (maximum)
Historically, the problem was discovered after building the structure then they try to detune it to compensate the negative beam loading but we can just change the phase advance by changing the length then we doesn't need to detune the structures.
Maximum 15.7° for 80KW and 12.6° for 100KW input power. The bunch form factor in CTF3 for the third SHB is around 0.6 and if assume the same for CLIC the detuning angles are around 9.3° and 7.6° for 80KW and 100KW input power, respectively.
This is valid for a Gaussian charge distribution that σ is the time width and Δφ is the phase width of one bunch .
For SW structures this concept is not useful. As mentioned previously, we just need to increase external Q for the beam loading compensation.
The detuning angle could be decreased by decreasing the gap voltage and filling time or by increasing the filling time if we keep the total length constant by decreasing the group velocity.

## Slide 23
For our case (BTW) the sign should be positive.
Borrowed from L. Thorndahl presentation [10]
Using this equation, vph will be 0.72c (0.71c) for the 110° four cells (122° three cells ) BTW structures for F=0.6 in comparison with ve=0.62c.

## Slide 24: Alternatives to remove satellites
PB
Buncher
Accelerating cavity
SHB-I
SHB-II
SHB-III
PB - II
Gun
PB
Buncher
Accelerating cavity
SHB-I
SHB-II
Passive
cavity
PB - II
Gun
New prebuncher (PB – II) is added to reduce the satellite – the idea from P. Urschütz- . In this case, the SHB – III should be operated at non-zero crossing.
Another Option – The idea from Steffen and Roberto : Using a RF chopper but the energy location is still unknown and also we need phase switching.
Another raw idea – from Steffen and me – is to using a passive cavity instead of SHB-III. It means we doesn’t need any power source.
Borrowed from S. Bettoni et al. [1]
CDR version
Modified version

## Slide 25: Power source requirement
80 KW (114 KW) output power for 10(8) ns filling time
499.75 MHz with 60(75) MHz bandwidth.
140 μs pulse length
50 Hz repetition rate
Looking for the power source.
Any suggestions?
8 ns is chosen to have effective filling time close to 10 ns (group velocity and phase velocity in the opposite direction).

## Slide 26: Summary
BTW structure with 4 cells seems the best case for SHBs.
A power source with about 120 KW output power and 75 MHz bandwidth is needed.
Need to study more on the transient behavior for the BTW structure with and without beam.
Work on passive cavity and RF chopper to remove satellites.
Input/output couplers with strong coupling is needed. Using an electrical coupling waveguide is an option.

## Slide 27: References
CLIC drive beam injector design, S. Bettoni, R. Corsini, A. Vivoli , 2010
Sub harmonic buncher at 1.5 GHz for CTF3, H. Braun, G. Carron, A. Millich, L. Thorndahl, A. Yeremian , CLIC Note 580 , 2003
Parameter list of the CTF3 Linac and the CT line , P. Urschütz , CTF3 Note 071 , 2006
Drive Beam Accelerating Structures , R. Wegner , 21 October 2010
Drive Beam linac structures and RF power sources , E. Jensen , 6th CLIC advisory committee, 3 Feb 2011
Advanced model to compensate transient beam-loading in CLIC main linac , O. Kononenko, not published yet
Physics and Technology of Linear Accelerators, Lecture 4 : RF Structures (Design) , H. Henke
Status of the Drive Beam Injector Study , A. Vivoli, 31 August 2011 , CLIC Beam Physics meeting
The LEP accelerating cavity, H. Henke, LEP note 143, 1979
From documents I got from L. Thorndahl.

## Slide 28: Thanks for your attention