## Slide 1: L-band power sources for drive beam
E. Jensen, CERN

## Slide 2: CLIC scheme at 3 TeV
e+ main linac
e- main linac , 12 GHz, 100 MV/m, 21.1 km
BC2
BC2
decelerator, 24 sectors of 878 m
IP
BDS
2.75 km
BDS
2.75 km
48.4 km
drive beam accelerator
2.38 GeV, 1.0 GHz
combiner rings
Circumferences
delay loop 72.4 m
CR1 144.8 m
CR2 434.3 m
CR1
CR2
delay
loop
326 klystrons
33 MW, 139 ms
1 km
CR2
delay
loop
drive beam accelerator
2.38 GeV, 1.0 GHz
326 klystrons
33 MW, 139 ms
1 km
CR1
TA
R=120m
TA
R=120m
245m
245m
booster linac,
9 GeV
BC1
e+ DR
365m
e+ PDR
365m
e- DR
365m
e- PDR
365m
linac,
2.2 GeV
e+ injector, 0.2 GeV
e- injector, 0.2 GeV
11 GW
11 GW

## Slide 3: CLIC 3 TeV
28 MW
MB+DB production & transport, services, infrastructure
and detector
Dumps
Main
linac
PETS
Drive beam
acceleration
266 MW
173.0 MW
140 MW
109 MW
23.8 MW
cosφs = .94
hTRS = .98
hT = .96
F(s) = .97  .96
hD = .84
Drive beam
power extr.
Power supplies
klystrons
hKlys→ struct→beam = .86
hRF = .277
102 MW
(2 x 101 kJ x 50 Hz)
Main beam
+5% network losses
594 MW
Modulator
337 MW
256 MW
hMOD = 0.9
hrise = 0.875
650 MVA
622 MW
1/’cosφi’
‘wall plug’
Wall plug | 100%
To DB-RF | 57%
To DECEL | 41%
To PETS_out | 73%
To Main Beam | 28%
Overall η | 4.7%
From B. Jeanneret – PRELIMINARY!
ηK = 0.65

## Slide 4: CLIC power consumption
Anticipating from B. Jeanneret’s talk later today, the actual numbers are:
  CLIC 3 TeV: 582 MW
  CLIC 1.5 TeV: 361 MW
  CLIC 0.5 TeV: 271 MW
I think: This is too high!
What can we do about it?

## Slide 5: CLIC power generation scheme
Drive Beam Accelerator
efficient acceleration in fully loaded linac
140 ms total length - 24  24 sub-pulses - 4.2 A
2.4 GeV - 60 cm between bunches
240 ns
Drive beam time structure - initial
24 pulses – 100 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - final
Power Extraction
Drive Beam Decelerator Sector (24 in total)
Combiner ring  3
Combiner ring  4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay loop  2
gap creation, pulse compression & frequency multiplication
Transverse RF Deflectors

## Slide 6: Full beam-loading acceleration
RF in
“short” structure - low Ohmic losses
RF to load
most of RF power
(≥ 95%) to the beam
High current
beam
No
No beam

## Slide 7: Full beam-loading acceleration
Measured RF-to-beam efficiency
95.3 %
Theory
96% (~ 4 % ohmic losses)
At 1 GHz, this will be even higher!
RF pulse at structure output
RF pulse at structure input
analog signal
1.5 µs beam pulse
3 GHz 2p/3 TW constant aperture
Slotted-iris damping + detuning with nose cones
Up to 4 A – 1.4 ms beam pulse accelerated – no sign of BBU

## Slide 8: Optimum aperture found!
ηRF ≥ 97.5 %
|tfill – 245 ns| ≤ 5 ns
Pin = 15 MW
Beam dynamic (Avni Aksoy): RB = 49 mm, N = 19 cells
Rolf Wegner

## Slide 9: Damping and detuning
Reduction of transverse wakefields by damping and detuning
Alexej Grudiev’s idea: dampers in web (~18 mm tick)
acc. mode Q0= 2.2 ∙104, Qext= 3.7∙107
distorted, 0.1° <=> 0.1 mm @ nose Qext= 1.5 ∙106 Pext,peak= 110 W, Pext,avg= 0.83 W
Ø≈ 250 mm
Rolf Wegner

## Slide 10: SICA: Slotted Iris – Constant Aperture
input
output
SiC dampers
nose cones
beam
Rolf Wegner

## Slide 11: SICA design finished:
Results for field distribution, phase advance per cell,
bead pull result simulation (Ez2)
GdfidL time domain simulations to verify dipole mode damping and detuning are ongoing.
Rolf Wegner
numerical error < 10-9

## Slide 12: Typical average power ranges (commercially available)
Chart: f [MHz]
| 10 | 352 | 1000 | 3000
Transistors | 1.2 | 0.33 | 0.12 | 0.02
SSPA (x32) | 38.4 | 10.56 | 3.84 | 0.64
Klystrons | 1300 | 1200 | 1000 | 500 | 250 | 2.5
Grid tubes | 6000 | 2800 | 1000 | 18
IOTs | 80 | 31 | 15
CCTWT | 100 | 40 | 15
UHF
State of the art
ESS/SPL: 704 MHz
SNS: 805 MHz
CLIC: 1 GHz
ILC/P-X: 1.3 GHz

## Slide 13: Optimum peak power for an MBK?
Chart: peak power [MW]
| 0.15000000000000011 | 1.5 | 10 | 20 | 30 | 36
present state of the art | 0.4 | 0.17 | 0.1 | 0.1 | 0.115 | 0.128
Chart: peak power [MW]
| 0.15000000000000016 | 1.5 | 10 | 20 | 30 | 36
after dedicated R&D | 0.39 | 0.165 | 0.095 | 0.089 | 0.105 | 0.12
The used model may be wrong, but there is an optimum which justifies the R&D.

## Slide 14: UHF: State of the art: X-FEL/ILC MBK’s
CPI: VKL-8301B (6 beam): 1.3 GHz, 10.2 MW, 10 Hz, 66.3 %, 49.3 dB gain
Thales: TH 1801 (7 beam): 1.3 GHz, 10.1 MW, 10 Hz, 63 %, 48 dB gain
Toshiba: E3736 (6 beam): 1.3 GHz, 10.4 MW, 10 Hz, 66 %, 49 dB gain
1.
2.
3.

## Slide 15: X-FEL MBK’s: horizontal test
CPI VKL 8301 B
Thales TH 1802
Toshiba E3736 H

## Slide 16: Power needs for future Linacs:
 | ESS | SPL II | ILC .5 TeV | CLIC .5 TeV | CLIC 3 TeV
Frequency | 704 MHz | 704 MHz | 1300 MHz | 1000 MHz | 1000 MHz
Technology | klystrons | klystrons | MBK | MBK | MBK
Total AC power | 38 MW | 40 MW | 230 MW | 249 MW | 594 MW
Modulator output | 17.8 MW | 26.5 MW | 135 MW | 64 MW | 266 MW
Power source output | 8.9 MW | 10.7 MW | 88 MW | 41.6 MW | 173 MW
Drive beam power |  |  |  | 33.6 MW | 140 MW
Acc. structure input | 6.5 MW | 7.8 MW | 67 MW | 24.6 MW | 102 MW
Total beam(s) power | 5 MW | 4 MW | 21.6 MW | 9.75 MW | 28 MW
Efficiency | 13.5 % | 10 % | 9.4 % | 3.9 % | 4.7 %
Table from Linac10 talk “TH103”, CLIC numbers adjusted to present preliminary numbers.

## Slide 17: Synergies
Energy efficient systems are in high demand to make these large projects sustainable and compatible with environmental and ecological requirements
The “EuCARD 2” proposal includes a “Network” activity “EnEfficient” – please take part!

## Slide 18: Announcement EuCARD2
From the EuCARD 2 draft proposal:
Task 3. higher electronic efficiency RF power generation (Erk Jensen, CERN)
The power conversion efficiency of a typical accelerator facility is a product of many individual efficiencies (mains to DC, DC to RF, RF to beam). One of the important contributors to the relatively low overall efficiency is the RF power generation, which for present day high power klystrons reaches 65% (ILC 10 MW klystrons) – the main purpose of task 6.3 is to create a network of interested and competent partners to facilitate and foster work on possible technologies and strategies to increase the RF power generation efficiency.
topics for task 3 include:
Possibilities to increase the efficiency of conventional, sheet-beam and multi-beam klystrons, including the use of higher harmonic cavities, smaller perveance and/or techniques for multi-stage depressed collectors,
the investigation of alternative sources with potentially higher efficiency compatible with large scale accelerator facilities including SSPA, IOTs, magnetrons and CFAs, or even more exotic devices like the magnicon,
possible techniques to increase the efficiency of klystrons that have to work with a non-zero differential gain (normally the maximum efficiency is obtained in saturation),
optimizing the design of power distribution systems and of the accelerating structures for maximum efficiency.

## Slide 19: Announcement ESS Workshop

## Slide 20: Klystron efficiency
100 % η would mean that all electrons will be slowed down to zero by the self-induced field in the output cavity. This is impossible!
For a maximum η, one needs:
  Dirac-delta like bunches through output cavity
    needs harmonic cavities,
    space charge forces counteract (small current helps)
  small ratio energy spread/voltage
    large voltage helps
  correct output cavity impedance! (Tolerances!)

## Slide 21: Increase klystron efficiency?
Good ideas are needed!
Some ingredients:
  small perveance
  higher harmonics
  travelling wave output structures?
  …
CERN and U Lancaster have started to jointly work on this, in the view of the needs of both ESS and CLIC! First results: 83% simulated!

## Slide 22: Sheet beam klystron
Courtesy CPI
Instead of many beams, also flat beams would reduce the effect of space charge forces and thus potentially increase η.
Potential advantage: Fabrication techniques may be better suited for cost-effective mass production.
Courtesy CPI
SLAC design of a 1.3 GHz, 10 MW SBK

## Slide 23: Multi-stage depressed collector?
Idea:
The collector consists of a number of electrodes with different potential.
the spent electron beam drifts against a potential and is intercepted at lower energy.
more energetic electrons drift further and their energy is recuperated.

## Slide 24: Magnetrons
Magnetrons have potentially very high η.
They have a good ratio MW/$.
But they are oscillators, not amplifiers!
Pulsed operation requires settling time – this effectively reduces efficiency.
They make a lot of phase noise!
If you run an accelerator with more than one magnetron, you need to phase-lock them! This can be done to about 1° precision (dixit Amos Dexter) – this is not good enough for the CLIC drive beam

## Slide 25
Thank you!