## Slide 1
Fully featured accelerating structure
engineering design
G. Riddone on behalf of the eng. design team
(great contribution from A. Solodko)
28.09.2011
LCWS11 WG4

## Slide 2: Contents
Introduction
Mechanical Design of Copper Discs and Compact Couplers
Mechanical Design of Vacuum Manifolds
Wake Field Monitor Design
Interconnection Design
Alignment Features
Super Structure Main Assembly Steps
Dedicated Tests
Conclusions

## Slide 3: Introduction
LSAS=502.5mm (1/4LMODULE)
1. Each Accelerating Structure consists of:
26 regular cells with four damping waveguides
2 compact coupler cells with two damping waveguides and other two opposite waveguides for WR90 connections
2. 4 WFMs are integrated in the first cell of the second AS
COMPACT COUPLER
WR90
WFM
BEAM
DIRECTION
1st AS
2nd AS

## Slide 4: Engineering Design Overview
BEAM
DIRECTION
1st AS
2nd AS
243.701 mm
502.5 mm
COOLING TUBE
VACUUM MANIFOLD
& COOLING SYSTEM
COOLING FITTING
WAVEGUIDE
INTERCONNECTION
WFM WAVEGUIDE
VACUUM FLANGE
BONDED DISC STACK
RF FLANGE
ALIGNMENT
VACUUM PORT
VACUUM PORT
BEAM
DIRECTION
Compact coupler design (already in TD26 CC);
The body of an AS formed by high-precision copper discs joint by diffusion bonding at 1040 °C;
Two AS are brazed together to form a superstructure (SAS);
The SAS has 8 vacuum manifolds and 4 Wakefield Monitor (WFM) waveguides;
The cooling system is integrated into the vacuum manifolds in order to provide a more compact technical solution.

## Slide 5: Mechanical Design of Copper Discs and Compact Couplers
Compact Coupler Cell
Cell with Alignment Features
Regular Cell

## Slide 6: Mechanical Design of Copper Discs and Compact Couplers
• Cell shape accuracy 0.005 mm • Flatness accuracy 0.001 mm • Cell shape roughness Ra 0.025 μm

## Slide 7: Mechanical Design of Vacuum Manifolds
Type 1
Type 2
Type 3
Type 4
Type 5
Type 6
Interface for WFM WG
Interface for supporting system
Type 1
Type 2
Interface for WFM WG
Interface for WG
Type 3
Interface for WG (x2)
Type 4
Interface for WFM WG
Interface for WG
Pumping the SAS
Type 5
Interface for WG (x2)
Pumping the SAS
Type 6

## Slide 8: Mechanical Design of Vacuum Manifolds
• Waveguide shape accuracy 0.02 mm
• Waveguide surface roughness Ra 0.1 μm

## Slide 9: Mechanical Design of Vacuum Manifolds
The vacuum manifolds combine a number of functions:
Damping. Silicon carbide absorbers are fixed inside each manifold for effective damping of HOMs.
Vacuum pumping. Two of the eight vacuum manifolds are equipped with vacuum flanges.
Cooling. Two internal cooling channels for the water flow are presented in each manifold.
DAMPING MATERIAL
CORNER SUPPORT
VENTED SCREW
VACUUM PORT
VACUUM PORT
COOLING TUBE
COOLING
FITTING
COOLING
CHANNEL

## Slide 10: Wakefield Monitor Design
Required tolerances
Waveguide shape tolerance ±10 μm
Waveguide surface roughness Ra 0.1 μm
WFM: accuracy of 5 μm;
Four WFM are integrated in the first cell of the second AS.
DAMPING MATERIAL
WFM WAVEGUIDE
TM-LIKE
MODE PICK-UP
TE-LIKE
MODE PICK-UP
Custom design of feedthrough
ST.STEEL ADAPTER
FLANGE

## Slide 11: Interconnection Design
Requirements
Keeping low pressure 10-9mbar;
Electrical continuity with low impedance;
Damping material must be used to avoid wakefields;
Be flexible;
Be compact.
SAS (N+1)
EDGE WELDED
BELLOWS
QUICK CF CLAMP CHAIN
XS40 VACOM
SAS (N)
DAMPING
MATERIAL
QUICK CF FLANGE
Stretched length ~+30%
Press formed length ~-70%
* Agreed with Vacuum Group

## Slide 12: Alignment Features
ST.STEEL INSERT
TUNING STUD
REFERENCE CONICAL BORE
Placed on the external reference surface of AS;
Stainless steel inserts are brazed to the tuning holes;
8 stainless steel inserts per one AS;
Conical bore on the insert top to provide a reference for the measuring arm;
The recorded coordinates of all points help to determine the AS beam axis and to align the AS properly.

## Slide 13
Super Structure Main Assembly Steps
1a. Brazing of the vacuum manifold bodies, cooling adapters and cooling caps
1b. Brazing of the WFM waveguides
x 8
x 4
1c. Brazing of the waveguides
1e. Brazing of the waveguides and RF flanges
x 8
1d. Machining of the waveguides
2. Brazing of the pre-assemblies to the vacuum manifolds
x 8

## Slide 14
Super Structure Main Assembly Steps
4. Brazing of the vacuum manifolds and interconnection bellows to the bonded disc’s stack
5. Brazing of the two equipped stacks to form a superstructure
6. Installation of the silicon carbide damping loads
3. Diffusion bonding of 2 disc’s stacks

## Slide 15
Super Structure Main Assembly Steps
8. Installation of cooling fittings and tubes
7. EBW of the vacuum manifold covers, vacuum flanges, feedthroughs
Intermediate leak tests and alignment verifications

## Slide 16: Test Program. Bonding
Option 1:
- 2 sets of regular discs
Option 2:
2 sets of special discs
Option 3:
2 sets of special discs
Could be the problem regions for bonding
This will be done before for TD26 CC

## Slide 17: Test Program. Brazing
Option 1: (hard to realize in a real structure)
Ni, Cu, Au
Option 2: (hard to realize in a real structure)
Ag 10 microns
Option 3: (hard to realize in a real structure)
Ag 15 microns
Disk copper
Disk copper
Silver 10 um on one disk
Disk copper
Disk copper
Silver 15 um on one disk
Disk Copper
Nickel 4 um
Copper 15 um
Gold 15 um
Disk Copper
* Courtesy of Serge Lebet
Could be a critical
region for brazing
Could be a critical
region for brazing
Option 4: (already validated for couplers and cooling circuits)
Au/Cu 50/50 foil, h=0.05mm
Disk copper
Disk copper
Au/Cu foil

## Slide 18: Conclusions
Engineering design under completion
It is foreseen to order fully equipped SASs to be tested in CLEX modules (June 2012)
A “version” for the stand-alone test stand will also be needed
First time we develop a fully equipped accelerating structure: main assembly steps under validation with mock-ups to be installed in dedicated modules

## Slide 19
Workpackage