## Slide 1: Beam test of a new integrated Micromegas module
Saclay Carleton Bruxelles

## Slide 2: Completely new setup aimed at 7-module operation
New detector : new routing to adapt to new connectors, lower anode resistivity, new res. foil grounding on the edge of the PCB.
New 300 points flat connectors
New front end: keep naked AFTER chips and remove double diodes (count on RF to protect against sparks)
New Front End Mezzanine (FEMI)
New backend ready for up to 12 modules
New DAQ, 7-module ready and more compact format
New trigger discriminator and logic.

## Slide 3: Beam Test
Started Monday May 2
Up and running in 24 hours, but 2 days for debugging monitoring, mapping, tuning HV, etc…
All the initial program has been done (150 good runs of 5000 evts, + lots of cosmics).
Plan to dismount on Friday night and Saturday morning May 14.
Small problem yesterday with magnet -> solved

## Slide 4: Beam size, Vdrift
Fitted rms 1.3 bins -> 3.9 mm
Vdrift checked OK

## Slide 5: Integrated electronics for 7 module project

## Slide 6: Integrated electronics for 7 module project
Remove packaging and protection diodes
Wire –bonding on board for AFTER chips
Use 2 × 300 pins connector
Replace resistors SMC 0603 by 0402 (1 mm × 0.5 mm)
25 cm
14 cm
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
3,5 cm
3,5 cm
FEC
Chip

## Slide 7: Design of the integrated electronics

## Slide 8: Front-End Card (FEC)
4 chips per FEC wire bonding on the 8-layer PCB
Protections: a resistor (0201 SMC) at each channel input
  A0: 0Ω
  A1: 3Ω
  A2: 5,1Ω
  A3: 10Ω
Temperature measurement device for each FEC

## Slide 9: First prototype of the electronics

## Slide 10: Temperature during switching on
Chart: Temperature (°c)
| 2.0 | 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0 | 55.0 | 60.0 | 65.0 | 135.0
FEC 0 | 29 | 34 | 39 | 41 | 43 | 44 | 44 | 45 | 45 | 45 | 45 | 46 | 46 | 46 | 46
FEC 1 | 30 | 36 | 43 | 46 | 49 | 50 | 51 | 51 | 51 | 51 | 51 | 52 | 52 | 52 | 53
FEC 2 | 30 | 37 | 44 | 48 | 50 | 52 | 52 | 53 | 53 | 53 | 53 | 54 | 54 | 54 | 54
FEC 3 | 30 | 37 | 45 | 49 | 51 | 52 | 53 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 55
FEC 4 | 30 | 37 | 44 | 47 | 49 | 51 | 51 | 52 | 52 | 52 | 52 | 52 | 53 | 53 | 53
FEC 5 | 29 | 34 | 39 | 41 | 43 | 44 | 44 | 44 | 45 | 45 | 45 | 45 | 45 | 45 | 46
FEMI | 30 | 37 | 42 | 45 | 47 | 47 | 48 | 48 | 49 | 49 | 49 | 49 | 49 | 49 | 49
Temperature in the hall

## Slide 11: Temperature after cooling
Chart: Temperature (°c)
| 1.0 | 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 31.0 | 33.0 | 35.0 | 40.0 | 45.0 | 46.0 | 48.0 | 50.0 | 55.0 | 60.0 | 70.0
FEC 0 | 45 | 43 | 42 | 41 | 41 | 40 | 40 | 40 | 39 | 39 | 38 | 38 | 38 | 38 | 38 | 37 | 37 | 37
FEC 1 | 52 | 49 | 47 | 46 | 46 | 46 | 45 | 45 | 44 | 43 | 43 | 42 | 42 | 42 | 41 | 41 | 41 | 41
FEC 2 | 54 | 52 | 50 | 48 | 48 | 48 | 48 | 47 | 47 | 46 | 45 | 45 | 44 | 44 | 44 | 43 | 43 | 43
FEC 3 | 54 | 53 | 51 | 49 | 49 | 49 | 48 | 48 | 47 | 47 | 46 | 45 | 45 | 44 | 44 | 44 | 43 | 43
FEC 4 | 53 | 51 | 49 | 48 | 48 | 47 | 47 | 46 | 46 | 45 | 44 | 44 | 43 | 43 | 43 | 42 | 42 | 42
FEC 5 | 46 | 45 | 44 | 43 | 42 | 42 | 42 | 41 | 41 | 40 | 40 | 39 | 39 | 38 | 38 | 38 | 38 | 38
FEMI | 47 | 44 | 42 | 41 | 41 | 41 | 40 | 40 | 39 | 38 | 37 | 37 | 37 | 36 | 36 | 36 | 35 | 35
Increasing of the Nitrogen flow
Temperature in the hall

## Slide 12: Event samples in B=1T

## Slide 13: Are we loosing ASICs?
May 6
May 10
May 12
Mainly ASICs 1 and 2 tend to be missing
-not especially where the beam is
Pedestal fluctuations?
Bad contacts?
Investigate…