LCTPC Collaboration Meeting 18. May 2011
Status LP – PCMAG Modification – Testbeams
(on behalf of Ralf Diener)
Software and Simulation Status

---
Large Prototype Field Cage
- Based on experience with small prototypes
  - Made of composite materials
  - Ø 72cm, ↔ 61cm
- Due to fabrication imperfection:
  - 2nd field cage planned
  - Mandrel worked over and measured

---
T24/1 Test Beam Setup
- Built inside EUDET
- Set up in DESY II test beam, area T24/1
  (e+/e- from 1 to 6 GeV/c)
- Comprises:
  - PCMAG magnet mounted on movable
    lifting stage (3 axis):
    Control and safety system being worked
    on in last 2 weeks of May
  - HV and gas system including slow control system
    (constantly under extension)
  - Cosmic and beam trigger (just updated)
  - Laser calibration system
- Outer silicon detector for reference - work in progress (based on ZEUS vertex parts):
  - Helix driver card missing, could be rebuild (plans available) and integrated with EUDAQ, but building & programming needs manpower
    (@DESY: both people working on it dropped out)

---
Past Test Beams
- 2008:
  - Nov-Dec Micromegas module w/ resistive anode
    (T2K electronics)
- 2009:
  - Feb-Apr 3 Asian GEM Modules w/o Gating GEM (3,000ch ALTRO electronics)
  - Apr TDC electronics with an Asian GEM Module
  - Apr-May Maintenance of PCMAG
  - May-Jun Micromegas w/ two different resistive anodes (New T2K electronics)
    Setup and test of laser–cathode calibration
  - Jun	GEM+Timepix (Bonn)
  - Jun	Installation of PCMAG moving stage and SiTR support
  - July	TDC electronics with an Asian GEM module
    ALTRO electronics study w/ Asian GEM
  - July-Aug Full installation of PCMAG moving stage
  - Aug	Micromegas w/o resistive anode with laser-cathode calibration
  - Sept	Bonn GEM module ( A small aria GEM with
    ALTRO electronics)
  - Nov	Micromegas with SiTR
- 2010:
  - March	Micromegas using PCMAG movable table.
  - March and Sept
    3 Asian GEM modules w/ gating GEM or a
    field shaper using the PCMAG movable table	(7616ch ALTRO electronic)
  - Dec	Octpuce (8 Ingrids) test on LP with 1T
    (Saclay/Nikhef)
- 2011:
  - Apr	First test of DESY GridGEM module (B=0T)
  - May	New AFTER electronics for Micromegas
    Installation of new cosmic trigger logic

---
Test Beam Schedule – Near Future
- - 29.05: T24 used by other group → no beam in T24/1
- 30.05-05.06:	Mounting of DESY module and measurements with
  cosmics (no beam available)
- 06.06-14.06: Beam measurements with DESY module
- 16.06-08.07: Asian module measurements
- 11.07- :	Shutdown of test beams at DESY till mid August
  Warm up of PCMAG
- End July: packing of PCMAG, shipping to Japan

---
Test Beam Schedule – Farer Future
- Late 2011/early 2012:
  - 7 Micromegas modules w. AFTER electronics
    (without magnetic field)
  - Tests with S-Altro 16 electronics
- 2012:
  - Continuation of LP1 tests (with magnetic field)
  - LP2 (advanced endplate) tests at test beam
- Late 2012/2013: Move to hadron test beam for some months

---
PCMAG
- PCMAG (designed for airborne experiments)
  - Persistent Current, superconducting MAGnet
  - Thin coil and wall (0.2X0), no return yoke
  - Liquid Helium reservoir
  - Moved to DESY in Dec 2006
  - Tested and mapped in 2006-2007
    (cooperation of DESY, KEK and CERN)
    Accuracy of 10-4
- Dimensions and data:
  - Coil: Ø 1.0 m, ↔ 1.3 m, weight: 460 kg
  - Central magnetic field: up to 1.2T
  - Liquid He capacity: 240L (max. 10 days)
  - Operational current: 430A (1T)

---
PCMAG Modification
- Up to now: filling manually with liquid He
  - Expert work, many steps to be taken carefully → error-prone
- Magnet modification inside AIDA project (+contrib. by KEK+DESY)
  - No filling, but using closed
    circuit with cryo modules
  - Safe, easy and efficient operation
    + Portability
  - No persistent current mode,
    PSU always connected
- Schedule:
  - Test beam end: 10.July 2011 → warm up of magnet, End of July: shipping to Japan, Ready in the beginning of 2012 (March?)
  - Might be pushed a few weeks back, due to delays with Toshiba
- Status: Preparations ongoing
  - Details of installation being planned (cable/tube lengths, packaging, etc.)
  - Open question: cooling water for the compressors
    (search for water chiller ongoing)
cryo modules will be installed
reservoir will be removed
2
- Up to now: filling manually with liquid He
  - Expert work, many steps to be taken carefully
    → error-prone
- Magnet modification inside AIDA project:
  - No filling, but using closed circuit
    with cryo modules
  - Safe, easy and efficient operation + Portability
- Schedule:
  - Test beam end: 10.July 2011 → warm up of magnet
  - End of July: shipping to Japan
  - Ready in the beginning of 2012
- Status: Preparations ongoing
  - Details of installation being planned
    (cable/tube lengths, packaging, etc.)
  - Close contact to Japan
  - Open question: cooling water
    for the compressors

---
Example of Modified System with similar Coil
2 cryo coolers (50K, 4K) mounted on chimney
Magnet chimney with the 2 coolers on the side
Helium gas compressors
for the 2 cryo coolers
Water Chiller behind
the two compressors

---
Software: MarlinTPC
- Working reconstruction chain from raw data (LCIO input) to track finding
- For pad based data:
  - Pulse Finding (single channel data)
  - Hit Building (space point reco)
- Pixel data:
  - Cluster Finding (from TOT/time measurement)
  - Hit Building (space points)
- Pattern recognition works, three options
- Within/Uses Marlin framework:
  - Geometry description (GEAR)
  - Data format/Persistency (LCIO)
  - Conditions Data (LCCD)
- In use (at least started) for all types of modules that were tested

---
Software: Current workplan and Needs
- Information management improvement
  - Data location on grid
  - Converter programs for ALTRO, AFTER electronics (and pixel?)
  - Geometry and pad mapping info
- Conditions data access and usage (almost done)
- Reconstruction – Fitting:
  - Currently no fitter truly works in MarlinTPC
  - KalTest is a good option, but extra effort is needed (e.g. geometry description)
  - Other option is still work in progress (possibly with direct connection to alignment)
- Reconstruction – Alignment and Calibration
  - Very important but no common tools so far
  - Makes little sense without a working fitter

---
Simulation status
- Several different approaches existing in MarlinTPC
  - Simple Geant Hit smearing (used e.g. for ILD simulation)
  - Charge cloud approximation (used e.g. for the Likelihood fitter technique)
  - Detailled ionisation and drifting & (fixed) parametrised amplification
- None that fit exactly our needs:
  - Possible single electron level from ionisation to readout plane
  - Different amplification structures
  - Ion backdrift studies
- (Possible) Solution: Garfield++ by Rob Veenhof and Heinrich Schindler in collaboration with RD51
  - Some experience already there
  - PhD candidate + C.R. will start to work on/with it
- Other parts also there
  - Ion Backdrift studies (Torsten Krautscheid)
  - Photo dots for calibration (Jason Abernathy)

---
Summary Slides by Ralf for easier digestion

---
Testbeam Setup
- Field cage:
  - Due to fabrication imperfection:
    2nd field cage planned
  - Status: Mandrel worked over
    and measured
- Setup at T24/1:
  - PCMAG magnet mounted on movable lifting stage (3 axis):
    Control and saftey systems currently being completed
  - Cosmics trigger logic just updated
  - HV and gas system including slow control
  - Laser calibration system
  - Outer silicon reference detector in progress,
    some problems due to missing parts

---
PCMAG Modification
cryo modules will be installed
- Up to now: filling manually with liquid He
  - Expert work, many steps to be taken carefully
    → error-prone
- Magnet modification:
  - Inside AIDA (+ contrib. by KEK, DESY)
  - No filling, but using closed Helium
    circuit with cryo modules
  - Safe, easy and efficient operation + Portability
- Schedule:
  - Test beam end: 10.July 2011 → warm up of magnet
  - End of July: shipping to Japan
  - Ready in the beginning of 2012
- Status: Preparations ongoing
  - Details of installation being planned:
    cable/tube lengths, packaging,
    cooling water, etc.
reservoir will be removed
2
- Up to now: filling manually with liquid He
  - Expert work, many steps to be taken carefully
    → error-prone
- Magnet modification inside AIDA project:
  - No filling, but using closed circuit
    with cryo modules
  - Safe, easy and efficient operation + Portability
- Schedule:
  - Test beam end: 10.July 2011 → warm up of magnet
  - End of July: shipping to Japan
  - Ready in the beginning of 2012
- Status: Preparations ongoing
  - Details of installation being planned
    (cable/tube lengths, packaging, etc.)
  - Close contact to Japan
  - Open question: cooling water
    for the compressors

---
Test Beam Planning
- Near future (2011)
  - June: DESY GridGEM module with ALTRO electronics
  - June/July: Asian GEM modules with ALTRO electronics
  - From mid July to beginning 2012: PCMAG modification
- Farer Future
  - Late 2011/early 2012:
    - 7 Micromegas modules w. AFTER electronics (without magnetic field)
    - Tests with S-Altro 16 electronics
  - 2012:
    - Continuation of LP1 tests (with magnetic field)
    - LP2 (advanced endplate) tests at test beam
  - Late 2012/2013: Move to hadron test beam for some months