## Slide 1: FONT Shifts June 2011

## Slide 2
CABLE
MAP
28 June
2011

## Slide 3: 28 June 2011 – Shift Log
Usual preamble:
  Locate beam (set big trig delay = 117)
  Load trim DACs
  Phase LOs
  Set scan delays
Had to tweak generated 357 MHz
  Match to 1.428 GHz master signal

## Slide 4: 28 June 2011 – Shift Log
ACCESS
  replaced grey intermediate amplifier unit on x with NEW MiniCircuits unit
  N.B. atten. P1: 6dB, P2: 6dB, P3: 5dB (y, sum atten. was 3dB on all channels)
Result: reduced noise on x channels

## Slide 5: 28 June 2011 – Shift Log
Before useful data obtained, linac cooling water system failed.
Extended ACCESS
  Phil, Colin examined IP region
  Rob, Mikey repaired damaged RG58 cables

## Slide 6: 28 June 2011 – Shift Log
Beam returned @ ~7pm
Took LO phase sensitivity scans
Noticed DR instability causing huge y excursions; corrected using sextupoles
More LO phase scans + BPM calibrations
Large residuals cast doubt on P1
ACCESS to check P1, set up for next shift

## Slide 7
P1X = 1
-0.00129

## Slide 8
P2X = 2
-0.00089

## Slide 9
P3X = 4
-0.00060

## Slide 10
P1Y = 5
-0.00236

## Slide 11
P2Y = 7
-0.00246

## Slide 12
P3Y = 8
-0.00198

## Slide 13: Note on these calibrations
X calibrations look “correct”, but actual constants are out
Possible causes:
  2-3 dB extra attenuation on XDIF
  XDIF, YSUM not aligned in time well enough (effect of this misalignment is scale factor)
These two effects could account for poor calibration constants yet lack of obvious deficiency with data

## Slide 14
P1X
P2X
P3X
P1Y
P2Y
P3Y

## Slide 15
CABLE
MAP
29 June
2011

## Slide 16: 29 June 2011 – Shift Log
Running with both FONT5 boards
P2 outputs split 4-ways (spare terminated)
Channel assignments:
Channel no. | #1 (Y) | #2 (X)
2 | YDIF (5) | XDIF (1)
3 | YSUM (5) | XSUM (1)
5 | YDIF (7) | XDIF (2)
6 | YSUM (7) | XSUM (2)
8 | YDIF (8) | XDIF (4)
9 | YSUM (8) | XSUM (4)

## Slide 17: 29 June 2011 – Shift Log
New 3-channel MiniCircuits intermediate amplifiers used on X (3 dB atten. on all)
Amplifier on FONT rack provides +20 dB for 357 MHz (split in tunnel)
Routine: BPM calibrations, LO phase scan
Single BPM resolution runs
Rob’s resolution vs. position study
ACCESS to change setup back to 3 BPM

## Slide 18: 29 June 2011
P2X = 1
0.00236

## Slide 19
P2X = 2
0.00218

## Slide 20
P2X = 4
0.00222

## Slide 21
P2Y = 5
-0.00239

## Slide 22
P2Y = 7
-0.00239

## Slide 23
P2Y = 8
-0.00215

## Slide 25
CABLE
MAP
30 June
2011

## Slide 26: 30 June 2011 – Shift Log
New FONT data cables put on ATF local
Routine: BPM calibrations, LO phase scan
Three BPM resolution runs
Kicker “calibrations”
ACCESS to collect equipment
  Almost all FONT kit now in Oxford

## Slide 27
P1X = 1
0.00246

## Slide 28
P2X = 2
0.00268

## Slide 29
P3X = 4
0.00193

## Slide 30
P1Y = 5
-0.00238

## Slide 31
P2Y = 7
-0.00246

## Slide 32
P3Y = 8
-0.00221

## Slide 34
170 µm
K1 in P2

## Slide 35: Summary
250 µm
K2 in P3

## Slide 36: Summary
BPM calibrations within normal range
LO phase scans baffling
  Susceptibility to LO phase appears to vary wildly depending on BPM used
Kicker calibrations consistent