Muon Collider Detector Simulation
and Calorimetry
Alexander Conway
Analysis of mcd00, an ideal depth-segmented
muon collider detector model.

---
Muon Collider Detector v.0.0
(mcd00)
Norman Graf

---
Calorimeter Properties
NUM LAYERS	EM	Hadron	Muon
Material	Tungsten	Steel 235*	Iron
Z	74	---	26
Density / {g/cm^3}	19.3	7.87	7.85
Cell size {cm^3}	1	2	10
Detector Depth {cm}	10	80	300
Radiation Length	6.76g/cm^2 0.35 cm	13.9g/cm^2 1.76 cm	13.8g/cm^2 1.76 cm
Nuclear Interaction Length	185 g/cm^2 / 9.58 cm	132.1 g/cm^2 / 16.8 cm	131.9 g/cm^2 / 16.8 cm
Data from http://pdg.lbl.gov/2010/AtomicNuclearProperties
*http://iopscience.iop.org/1748-0221/5/05/P05004/pdf/1748-0221_5_05_P05004.pdf

---
Beam's-eye view of a single 10GeV pion event

---
Bernd Surrow
http://physics.bu.edu/neppsr/2006/TALKS-2006/Calorimetry_Surrow.pdf

---
Studying the Detector
- Simplistic model:
  - Single particle events
  - No noise
- Calorimeter properties:
  - Total absorption
  - Homogeneous
  - Sensitive
- Establish baseline properties

---
Studying the Detector
- Energy resolution
  - How much can we detect?
  - How much does signal vary?
  - Can we characterize particles?
- Constraints to add
  - Timing cuts
  - Energy deposition threshold
  - Clustering

---
Establishing a Baseline: Timing cuts
- Simulated 10GeV electrons and pions
- How fast do showers develop?

---
Energy Response with varying time cutoffs from 0 to 1000ns
electrons
pions

---
Time Cutoff Comparisons
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.95	8.25	0.02	0.58	0.6%	18%
100ns	9.95	7.76	0.03	0.72	1%	23.7%
10ns	9.94	7.48	0.04	0.86	1.3%	27%

---
Pion energy response with
100 ns and 1000 ns cutoffs
	Mean (GeV)	RMS (GeV)
1000ns	8.25	0.58
100ns	7.76	0.72
1000ns
100ns
GeV

---
Time Cutoff Comparisons
RMS for electrons and pions
2D Histogram of energy responses for pions

---
Time Cutoff Comparisons
- Electrons:
  - Characteristically fast shower development and high resolution.
- Pions:
  - Slower shower development
  - Lower energy response that varies widely
  - Will have to use other aspects of the detector to characterize these and other particles;
    - EM cal vs H cal response, shower shape, tracking, cherenkov, etc

---
Minimum Ionizing Particle
(MIP)
- Relativistic muons approximate MIPs
  - Little interaction with detector but with characteristic energy
  - Want to see this MIP trail
    - Energy threshold must be lower than MIP energy
  - Use muons to measure the MIP energy specific to each type of calorimeter

---
Minimum Ionizing Particle
(MIP)
10 GeV Muon

---
Minimum Ionizing Particle
(MIP)

---
Minimum Ionizing Particle
(MIP): EM and H Cals
EM Cal cell response
H Cal cell response
MIP
MIP
GeV ->
GeV ->

---
Minimum Ionizing Particle
(MIP): Muon Cal

---
Minimum Ionizing Particle
(MIP)
Minimum ionization is very clear in all detectors
- Muon cal's MIP energy is about five times that of the other cals
  - Muon cal cells are 5X bigger but otherwise very similar to H cal
  - Hcal cells are 2X bigger than EM but EM has approximately twice the density
Use arbitrary value less than one MIP for energy cutoff, 1/5 MIP for preliminary studies.

---
Energy Cuts: 1/5MIP
Before Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.95	8.25	0.02	0.58	0.6%	18%
100ns	9.95	7.76	0.03	0.72	1%	23.7%
10ns	9.94	7.48	0.04	0.86	1.3%	27%
After Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.520	7.05	0.059	0.75	1.9%	24%
100ns	9.513	6.85	0.064	0.82	2.0%	26%
10ns	9.510	6.74	0.067	0.88	2.1%	27.8%

---
Energy Cuts: 1/5MIP
Pion response is drastically changed
  - Especially for longer time windows
  - 'Splashes'?
  - Will this be lost by clustering anyway?
Look at clusters first, then combine with energy cuts

---
Clustering
- Must remove hits that can't be traced to particle
- Can test different algorithms,
  - Fixed-cone clustering
  - Nearest neighbor clustering
Fixed-cone:
  - Clusters of hits that fit within cone
Nearest neighbor:
  - Clusters hits adjacent within x number of cells

---
Clustering: Fixed-cone
Before Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.95	8.25	0.02	0.58	0.6%	18%
100ns	9.95	7.76	0.03	0.72	1%	23.7%
10ns	9.94	7.48	0.04	0.86	1.3%	27%
After Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.54	7.90	0.083	0.771	2.6%	24.4%
100ns	9.94	7.57	0.052	0.83	1.6%	26.2%
10ns	9.93	7.34	0.087	0.91	2.8%	28.8%

---
Clustering: Nearest Neighbor
Before Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.95	8.25	0.02	0.58	0.6%	18%
100ns	9.95	7.76	0.03	0.72	1%	23.7%
10ns	9.94	7.48	0.04	0.86	1.3%	27%
After Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.96	5.86	0.924	1.62	29.2%	51.2%
100ns	9.95	5.71	0.924	1.62	29.2%	51.2%
10ns	9.55	5.60	0.923	1.64	29.2%	52.9%

---
Thoughts
- Fixed-cone clustering provides better resolution across the board
- Nearest-neighbor parameters should change
- Ways to improve energy resolution:
  - Change nearest-neighbor parameters
  - Combine nearest-neighbor clusters that fall with in fixed cone
  - Perform nearest-neighbor on fixed cone clusters

---
Clustering/threshold: Fixed-cone
Before Cuts (fixed-cone clustering):
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.54	7.90	0.083	0.77	2.6%	24.4%
100ns	9.94	7.57	0.052	0.83	1.6%	26.2%
10ns	9.93	7.34	0.087	0.91	2.8%	28.8%
After MIP Cuts:
	Mean energy response (GeV)		RMS / (GeV)		RMS/sqrt(E)
	Electrons	Pions	Electrons	Pions	Electrons	Pions
1000ns	9.95	7.90	0.053	0.77	2.6%	24.4%
100ns	9.94	7.57	0.058	0.83	1.6%	26.2%
10ns	9.93	7.34	0.061	0.91	2.8%	28.8%