## Slide 1: H->gg,WW Analysis for Detector Optimization
Ron Cassell
11/16/11

## Slide 2: Outline
Envisioned procedure
Simulation/Reconstruction
Analysis

## Slide 3: Envisioned procedure
Develop an analysis package to measure the e+e- -> nunuH, H->gg,WW sigma*br error at 1 TeV in the sidloi3 detector, using full simulation/reconstruction, following the lead of Tim’s analysis using fast MC.
Create new detectors varying the Hcal (# interaction lengths, absorber?).
Calibrate, simulate, reconstruct and analyze in the new detectors.

## Slide 4: Simulation
Slic, Geant4, and lcio have all changed recently.
Various problems with each, being worked out.
Currently have a “compatible path”: SLIC – “special” – from Jeremy – new slic, old geant, old lcio: requires using old lcsim and old slicPandora.
This is the sim/reco path I’m using.

## Slide 5: Simulation: Data samples
For 80% e-(L) 20% e+(R), ½ inverse ab:
nunuH: 214,787 events, H->WW,gg 25,745 events.
e+e- -> enuW: 2,789,166 events
e+-A -> enuW: 10,882,230 events

## Slide 6: Simulation: Data samples
Not practical to process 14 million events for each detector.
Looking for cuts at the generator level to reduce number.
Currently processing 100,000 nunuH events, and 1,362,000 enuW (~10%) events.
Initial processing neglected beam crossing angle, => large # of enuW events passing cuts.

## Slide 7: Analysis variables
From Tim’s analysis: variables used
Event energy, Event Pt, Event Mass, cos(Θthrust), # charged tracks, # “large impact parameter” tracks, # jets, # isolated leptons.
To use these variables, we need to define:
Jet clusterer
Isolated lepton criteria
Large impact parameter track criteria

## Slide 8: Jet clusterers
Tried using the Durham clusterer with a variety of y cuts.
Separation of WW* and gluongluon events not as good as hoped.
Tried jet clustering in the event CM system.
Compared to clustering with “perfect” particles, results nearly identical.
For now, using Durham clusterer in the CM system with a ycut = .0075

## Slide 10: Isolated lepton criteria
Have previously observed isolated leptons (mainly electrons) being reconstructed as 2 or more particles.
Current criteria:
Jet contains an electron or muon > 5 GeV
Elepton/Ejet > 0.6

## Slide 11: Large impact parameter criteria
Track parameters D0 and Z0: errors appear to be too small
Check with sid02
Match tracks to MCParticle
Require MCParticle origin => magnitude < 1 micron.

## Slide 14: Large impact parameter criteria
Correct for errors, and define ipsig2 = (D0**2/eD0**2 + Z0**2/eZ0**2)/2
Define ipsig = sqrt(ipsig2)
Look at # of tracks with E > 2 Gev and ipsig > 3 per event

## Slide 16: Current cuts for gg + WW*had
100 < Evis < 500
20 < Pt < 400
cos(Θthrust) < 0.95
# isolated leptons = 0
10 <= # Tracks <= 48
# large ip tracks < 4
2 <= #jets <= 5
102 < Mvis < 132
All subject to change when studying SM background

## Slide 17: Signal efficiency for cuts
CUT | WW* eff | gg eff | WW* + gg eff | WW* + gg pur wrt other H decays
visE + visPt + cosΘthr + # iso leptons | 79.3% | 80.7% | 80.0% | 13.8%
+ # tracks + # jets + # large impact tracks | 72.9% | 75.8% | 74.6% | 42.3%
+ Mass | 66.6% | 68.9% | 67.6% | 48.7%

## Slide 18: Comparison
Estimates from Tim’s paper:
# WW* hadronic events ~ 37000
After WW cuts: eff = 49.5%, pur wrtH = 44.4%, pur = 31.6%
After NN: eff = 32.2%, pur wrtH = 67.0%, pur = 52.2%
If I cut on > 3 jets:
Eff = 48.0%, pur wrtH = 56.0%