## Slide 1
Dampimg
Ring
Surface

## Slide 2
Helium compressor / cryogenics
Loading area
Detector services
Main access tunnel

## Slide 3: Access tunnel
ILD
SiD
A trailer with lower deck height
would reduce the tunnel size

## Slide 4: Solenoid transport
Trailer truck
  225t/5axles450t with 2 trailers
  Capability of ~7% slope
Gear track (Abt system) is also suggested

## Slide 5: ILD Detector assembly
Solenoid
  Wound, assembled, and tested on surface
  Carried into the cavern as a whole
Return yoke
  Pre-assembled on surface as relatively small blocks ~200 tons
  Each ~200 ton block is carried into the cavern one by one and assembled into one barrel
  No gap in the barrel yoke  Less leakage field
Large assembly hall on surface is necessary

## Slide 6: Detector assembly
Barrel assembly
Endcap (+) assembly
Endcap (-) assembly
Solenoid installation
QD0 support tube (-) assembly
QD0 support tube (+) assembly
Sub-detector installation
1
6
5
3
4
2