## Slide 1: ILC-SCRF Test Facilities considerations
H. Hayano 01062012

## Slide 2
SCRF Test Procedure to be considered;
(1) Cavity (total 15,764 in RDR) : will be treated by Cavity
Surface treatment, jacketing, 2K-field-test are required.
(2) Coupler (total 15,764 in RDR)
RF process in Room-Temperature is required.
(3) Cryomodule (total 1,824 in RDR)
coupler RF process in R.T. , cool-down, 2K (coupler+cavity) RF process are required.
in-situ process in tunnel is also required.
(4) Klystron (total 646 in RDR) : will be treated by HLRF
HV-DC apply, RF process are required.

## Slide 3
Coupler Fabrication
clean-up
pair assembly
pumping/120C baking
RF power process (RoomTemperature)
disassembly
in clean room
assembly into cavities
in clean room
RF power process
(Room Temperature)
RF power process with cavity (2K)
20hrs for two
Coupler Procedure
Cryomodule Procedure
cryomodule assembly
cryomodule test facility
in tunnel
RF power process
(Room Temperature)
RF power process with cavity (2K)
Accelerator Operation
reflection mode
through mode
reflection mode
through mode
Coupler test facility
2x peak RF power process
Move to Tunnel and install into Accelerator
cavities
couplers

## Slide 4
Marc’s Questions
Only 30% will be tested before installation, the other will be done in-situ, in RDR estimate.
However, 2x peak power in-situ is not streightforward. Need WG re-configuration.
(1) power coupler test
(2) Cryomodule test
Only 30% will be tested before installation. The other will be installed without cold-test.
2x peak power process is strongly recommended for ceramics window process,
whisker process and out-gass process.
not good for in-situ process to avoid contamination into cavity.
120C baking is also required for surface water removal,
not good for in-situ baking to avoid contamination into cavity.
So that, automated Coupler Test Facility for 100% coupler process should be considered.
Cryomodule cold-test can be skipped after resolving initial installation issues
and after getting stable performance.
30% test ( 547 cryomodules ) looks reasonable,
it corresponds to 2-years production out of 5 years production.
Cavity performance degradation issue should be addressed and solved before production.
(such as coupler inner surface inspection & rinsing, beam-pipe bellows inspection & rinsing, ..)

## Slide 5
Cavity Test Procedure consideration
(He tank-on test)
Cavity Fabrication
Inspections/
optical inspection
Bulk-EP (150µm)
800C heat treatment
optical inspection
cell RF tuning
surface repair 2
fine EP (20µm)
120C baking
He tank welding
pick-up antenna inst.,
HOM tuning
2K field test
OK
if defect found
surface repair 1
if defect found
4 Cavities Test
in one cool-down
> 28MV/m
< 28MV/m
2nd pass
remove pick-up antenna
with He Tank
in 2nd pass
with He Tank
in 2nd pass
skip
in 2nd pass
to cryomodule
Cavity test facility

## Slide 6
He tank-on testing
(1) cavity fabrication and treatment can be separated from cavity test facility
with costy cryogenics.
-> companies cover fabrication and treatment, deliver treated tank-on cavity.
(2) If it fail into <28MV/m, 2-nd pass process will be complicated.
tank-on EP, tank-on baking, etc are required, and the cavity is put back to companies.
mixture of tank-off EP and tank-on EP make the process and jigs complicate.
-> transport cost + tank-on process cost
(3) The model; lab. takes care the 2-nd pass process.
The lab facility for 20% cavity is required. -> facility cost
He tank-off testing
(1) cavity move back from cavity test facility to fabrication factory, and then deliver again.
-> transport cost
(2) If cavity fail into <28MV/m, 2-nd pass process will be the same as the 1-st pass,
however, cavity is put back to companies.
-> transport cost
(3) The model; lab. takes care the 2-nd pass process. -> the same above.

## Slide 7
End of slides