## Slide 1: PandoraPFA: Status for ILD
ILD Analysis/Software Meeting, 18/04/2012
J.S. Marshall, University of Cambridge

## Slide 2: Overview
Recent IlcSoft changes are likely to have an impact on the particle flow reconstruction.
Pandora algorithms are isolated from these changes by the MarlinPandora client application.
MarlinPandora is responsible for performing the following software/detector-specific tasks:
  Providing calibrated energy values for each calorimeter cell,
  Making quality cuts for all input inner-detector tracks and calorimeter cells,
  Specifying information about inner-detector tracks and their relationships (kinks, prongs, etc.).
Now need to review these operations...
Pandora Client Application
Pandora Framework
ILD/Marlin
SiD/org.lcsim
Run registered algorithms/tools and perform book-keeping
Algorithm Manager
CaloHit Manager
Cluster Manager, etc.
Isolate specific detector and software details, creating self-describing hits, tracks, etc.
API

## Slide 3: Calibration
With any important change to simulation or reconstruction, need to perform calibration.
PandoraAnalysis package contains Marlin processors and simple binaries to ease this process.
  Ensure that Mokka hits are calibrated, using following MC samples:
      10,000 10GeV photons at cos() = 0.02, with random  values,
      5,000 10GeV KL at cos() = 0.02, with random  values,
      5,000 10GeV muons at cos() = 0.02, with random  values.
  Determine PandoraPFA MIP calibration constants, using the muon sample.
  Identify the PandoraPFA constants (below). We might expect these to just be 1.0, but need to account for mip cuts applied in MarlinPandora and also for PandoraPFA isolation cuts.
      ECAL_To_EM_GeV
      ECAL_To_HAD_GeV
      HCAL_To_EM_GeV
      HCAL_To_HAD_GeV
      MUON_To_GeV
  Aim to optimise jet energy reconstruction: quantify using Zuds events, RMS90(E)/Mean90(E).

## Slide 4: ECAL Calibration
ECAL calibration rather straightforward.
Change CalibrECAL from 40.91, 81.81 to 42.91, 85.82
          Pandora constants: ECAL_To_EM_GeV=1.00
                HCAL_To_EM_GeV=1.00
HCAL To EM constant not too important

## Slide 5: HCAL Calibration
HCAL calibration difficult: non-Gaussian, energy corrections, KL energy divided between ECAL/HCAL
Use MINUIT to optimise for jet energy reconstruction: change CalibrHCAL from 34.80 to 58.60
          Pandora constants: ECAL_To_HAD_GeV=1.05
                HCAL_To_HAD_GeV=1.00
Further increases distort distribution

## Slide 6: MIP Calibration
ECAL
HCAL
MUON
MIP constants: ECAL_To_MIP=160.0 HCAL_To_MIP=34.8 MUON_To_MIP=10.0
Need to change product of CalibrMUON and MUON_To_MIP from 100,000 to 465.
Choose to keep MUON_To_MIP unchanged (for now), intermediate MUON_To_GeV untested.

## Slide 7: Zuds Simulation
Assess performance using Zs at different energies decaying at rest into light quarks, producing two back-to-back jets. Backgrounds not included and no jet finding performed.
For most interesting comparison, use IlcSoft v01-13-05 version of Mokka to process same stdhep files for both ILD_00 and ILD_O1_v02. Same physics lists, etc. Change only detector model.
Reconstruct events with IlcSoft v01-13-05, using old tracking/calibration (previously validated steering file) and new tracking/calibration (new steering file from ILDConfig repository).
Event 1
Same 91GeV Zuds stdhep file
Same physics list and Mokka version
IlcSoft v01-13-05
Same PandoraPFA
ILD_00
Old Tracking/Calibration
ILD_O1_v02 New Tracking/Calibration

## Slide 8: Tracking Changes
Tracking reconstruction has changed significantly. Can no longer assume that the many track quality checks in MarlinPandora are appropriate.
  For first tests, continue to apply “sensible” track quality cuts, but nothing directed at specific pathologies in either the old or the new tracking software.
Cannot assume that track-relationship information, provided by KinkFinder and V0Finder processors, can be used safely.
  For first tests, do not feed track-relationship information to Pandora algorithms.
Preliminary plots, with rather low stats: 1,000 91GeV Zuds events

## Slide 9: Tracking Changes
MarlinPandora chooses not to pass tracks to Pandora if have only a small number of tracker hits (accounts for different tracking detectors in decision).
However, this is not full story. MarlinPandora also specifies a number of important properties, which tell Pandora algorithms how to use tracks they receive:
  CanFormPfo flag
  CanFormClusterlessPfo flag

## Slide 10: Zuds Results
Ez (= 2 * Ej) | 91GeV | 500GeV
ILD_00, RMS90(Ej)/mean90(Ej) [%] | 3.69 ± 0.05 | 3.40 ± 0.05
ILD_O1_v02, RMS90(Ej)/mean90(Ej) [%] | 4.15 ± 0.05 | 3.48 ± 0.05
Jet energy reconstruction results indicate problems. Sizeable at EZ=91GeV, decrease at EZ=500GeV.

## Slide 11: Next Steps...
Have reported first quick studies of performance with new detector model and reconstruction. Now need to understand the observed degradation in jet energy resolution:
  New track reconstruction?
  Calibration problems?
  Simulation issues?
If calibration is a problem, not as simple to solve as might first think: MINUIT-controlled variation of calibration parameters cannot improve present jet energy resolution results.
Have so far examined ILD_00 with old tracking reconstruction, plus ILD_O1_v02 with new tracking. Would be helpful to test old detector model with new reconstruction software.
A “TruthTracker” that is fully functional for Zuds events would also help to narrow search.
Suggestions very welcome!
 | ILD_00 | ILD_O1_v02
Old Tracking | ✓ | ?
New Tracking | ? | ✗
Must distinguish between these