## Slide 1: A TPC for the Linear Collider
P. Colas
on behalf of LCTPC

## Slide 2: 2 detector concepts : ILD and SiD
SiD: all-silicon
ILD: TPC for the central tracking
Both based on the ‘particle flow’ paradigm
Benchmark process: e+e- -> HZ, Z->µµ
Requirements:
Momentum resolution
d(1/pT) <2.10-5 GeV/c with vertex constraint
d(1/pT) <9.10-5 GeV/c TPC only
(200 points with 100 µ resolution in Rf)
2-track separation: 2 mm in Rf and 6 mm in z in a high density background
Material budget: <5% X° in the barrel region, <25% X° in the endcap region
B=3.5 T

## Slide 3: All the R&D is gathered in LCTPC
38(*) member + 7 observer institutes from 12 countries
(*) 25 signed the MOA

## Slide 4: The EUDET test setup at DESY
The EUDET (FP6) setup at DESY is operational since 2008
Being upgraded within AIDA (FP7): autonomous magnet with internal He compressors
SiPM trigger
Field cage

## Slide 5: Beam tests at DESY : 5 technologies
Laser-etched Double GEMs 100 µ thick (‘asian GEMs’)
Micromegas with charge disper-sion by resistive anode
GEM + pixel readout
InGrid (integrated Micromegas grid with pixel readout)
Wet-etched triple GEMs (‘European GEMs’)

## Slide 6: Advantages of MPGDs

## Slide 10: Charge spreading by resistive foil
Resistive coating on top of an insulator: Continuous RC network which spreads the charge: improves position sensitivity
Various resistive coatings have been tried: Carbon-loaded Kapton (CLK),
3 and 5 Mohm/square, resistive ink.
M. Dixit, A. Rankin, NIM A 566 (2006) 28

## Slide 11: Pad response
Z=20cm, 200 ns shaping
Relative fraction of ‘charge’ seen by the pad, vs x(pad)-x(track)
24 rows x 72 columns of 3 x 6.8 mm² pads
x(pad) – x(track) (mm)

## Slide 12
Z=5cm
Z=35cm
Z=50cm
MEAN RESIDUAL vs ROW number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film (red points)
-> select CLK
Uniformity (B=1T data)
Row number

## Slide 13
Uniformity
Average charge by row
Using cosmic-ray events
B=OT
Excellent uniformity up to the edge of the module, thanks to the ‘bulk’ technology.
Average charge by row
Using 5 GeV e-
B=1T
0 5 10 15 20
0 5 10 15 20
z distribution

## Slide 14
Module 4
Data analysis results (B = 0T & 1T)
Carbon-loaded kapton resistive foil
χ2 : 10.6
Ndf: 10
B=0 T Cd = 315.1 µm/√cm (Magboltz)
Module 3
χ2 : 29.1
Ndf: 11
B=1 T Cd = 94.2 µm/√cm (Magboltz)
Cd : diffusion constant
Gas: Ar/CF4/Iso 95/3/2

## Slide 15: Neff measurement with Micromegas
Averaging B=0T and B=1T data, modules 4, 5 and 3 (excluding ink module):
  Neff = 38.0±0.2(stat) (systematics difficult to assess)
  σ0= 59 ± 3 µm
  Note that 1/<1/N> = 47.1 from Heed for 5 Gev electrons on 6.84mm long pads.
  Thus Neff has to be between 23.5 (for exponential gain fluctuations) and 47.1 if there are no gain fluctuations.
  1/<1/N> = 34.9 for 5.4 mm pads (GEM case).
D. Arogancia et al., NIM A 602 (2009) 403

## Slide 16: Dependence of resolution with peaking time
Z=5cm
CLK 5 MW/sq
Chart: 
| 200 | 400 | 500 | 600 | 700 | 1000 | 1500 | 2000
 | 97 | 81.7 | 79.7 | 80.8 | 80.5 | 87.8 | 104 | 121.8
Optimum resolution for 500 ns peaking time -> try to lower resistivity to lower this peaking time (faster charge spreading)

## Slide 17
27 cm
40 cm
35cm
B field
Top
Test in a high intensity p beam
Bottom
11 cm

## Slide 18
Test at CERN (July 2010) at 180 kHz (5 x 2 cm² beam) showed no charging up and stable operation
Peaking time of 200 ns is enough to obtain the best resolution -> 300 ns suffice to distinguish 2 tracks on the same pad
4µs
Time (in 40 ns bins)

## Slide 20: 7 module project – Micromegas electronic integration

## Slide 21: Integration and cooling
New detector : new routing to adapt to new connectors, lower anode resistivity (3 MW/sq), new res. foil grounding on the edge of the PCB.
New 300 points flat connectors
New front end: keep naked AFTER chips and remove double diodes (count on resistive foil to protect against sparks)
New Front End Mezzanine (FEMI)
New backend ready for up to 12 modules
New DAQ, 7-module ready and more compact format
New trigger discriminator and logic (FPGA).

## Slide 22: Integrated electronics for 7-module project
Remove packaging and protection diodes
Wire –bond AFTER chips
Use 2 × 300 pins connector
Use tiniest resistors (1 mm × 0.5 mm) from O to 10W
25 cm
14 cm
0,78 cm
0,74 cm
4,5 cm
12,5 cm
2,8 cm
3,5 cm
3,5 cm
FEC
Chip
after 2 weeks of operation: no ASIC lost:
  The resistive foil protects against sparks

## Slide 23: First prototype of the electronics

## Slide 25
Thermal studies. IR camera shows hot spots (regulators, ADC). T-probes on every component.
2-phase CO2 cooling under study (KEK, Nikhef)
Nitrogen cooling
Onset of the electronics

## Slide 26
Tends to confirm previous measurements
(excluding lines with ASICs in bad contact).
Optimum resolution now obtained for peaking time below 200 ns
Preliminary results : resolution (B=1T data)
Resolution vs z for various peaking times.

## Slide 28: Ion disk and gating

## Slide 29: Preparation for future electronics
Design and optimization work in progress for a new chip GdSP, evolution from SALTRO16:
  64 or 128 channels
  130 nm technology
  Very low noise
  Integrated ADC
  6 different power regions for power cycling
  High level filtering (baseline subtraction, spike removal)

## Slide 30: CONCLUSIONS
MPGDs have been shown to fulfill the requirements for the readout of a TPC for the LC.
Integration work (electronics and cooling) is going on, and practical production issues are addressed for the pad readout.
Pixel readout needs more development to gain in reliability and operability in large surfaces.