## Slide 1: Preparation for Sept 9mA studies: Follow-up items from February J. Carwardine, 22 May 2012

## Slide 2: List of follow-up tasks from Feb 9mA studies
Implement the gradient soft limiters on all cavities in ACC4-7
Determine suitable thresholds for the hard and soft limiters, develop procedures on how to use them
Revisit methodology for robust quench detection (the quench server acting at the end of the pulse)
Integrate and improve exception handling for the various interconnected servers (QL server, quench detect, piezo server, gradient flattening algorithm,...)
Various refinements to the Loaded-Q server
Implement an 'operations quality' version of my iterative gradient flattening algorithm
Better (more complete) ways of doing off-line testing of new scripts, servers, automation, etc to reduce the requiring amount of dedicated machine time
Implement Fermilab piezo tuner algorithm at CMTB

## Slide 3: Follow-ups
Quench threshold identification
  Revisit methodology for more robust quench identification
Pre-limiter
  Principle works very well, we now need more experience with it
  Where to set the thresholds…?
  How/when to use it, procedures,
Testing automation and operations tools without beam time?
  Real-time (pulse to pulse?) online simulator with DOOCS front-end
Automation
  Implement ‘operations-quality’ gradient flattening algorithm
  Cross-linkages between automation tools – integration
  Need better exception handling, better uniformity
DAQ
  Propose new DAQ specifications (AMTF, XFEL ?)

## Slide 4: Automation: new servers
Piezo / Quench / Ql
  All worked well
  All can be improved
  Need for uniformity among servers
    A centralized / unique QL measurement
    A centralized / unique detuning measurement
    Uniformity in various threshold definitions (i.e. low gradients, limiters, pre-limiters, etc…)
  Need for priority among servers
    Sequence of action (sequencer ? state machine ?)
      i.e. wait for cavity tuner before adjusting piezo
      adjust cavity frequency before adjusting QLs
      etc…
    Exception handling (e.g. motor moving, don’t change Ql)
      communication & coordination between automatic servers

## Slide 5: Automation: QL Server
Auto Ql
  all ON / all OFF ability  DONE
  settings Save/Restore (add to existing sequencer)
  one-click return to default value (part of Save/Restore)
  performance assessment (speed, accuracy)
  automatic tuning strategy  flatten cavity tilts (9mA) with exception handling  other algorithms ?
  getting a reliable QL measurement server is key

## Slide 6: Automation: Quench Server
Quench detection
  issues with time stamp (quenches detected after 3-4 quenches)  is it OK ?
  some false alarms  why ?
  still problems with changing RF flat top length
  improve operator notification in case of quench
  getting a reliable QL measurement server is key

## Slide 7: Automation: Piezo server
Auto piezo server
  could propose tuning action when DC bias is max
  settings Save/Restore (add to existing sequencer)
  needs to include pulse shortening  in the works
  ability to selectively turn auto piezo ON / OFF
  better detect ‘run-away’ situation and exception handling in general
  getting a reliable detuning measurement is key

## Slide 8
Highest priority items for the Sept 9mA studies?
Who will do the work?
Then there are some machine issues needing follow-up
  We want 800us pulses with at least 6mA