## Slide 1: Developing a program for 9mA studies shifts in Sept 2012
John Carwardine
5th June 2012

## Slide 2
It would be natural to develop a program that builds on what was achieved in February
  Klystron saturation studies
  Operation close to quench
Need to consider that the Sept studies will be the last chance to collect results for the ILC TDR
  Are there things missing from our accomplishments?

## Slide 3: 9mA studies (Feb 2012)
Study topics
  How well can we flatten the individual cavity gradients
  How close to quench can we run the cavities with beam
  How close to saturation can we run the klystron
  How to ramp up to the maximum current, pulse length, and gradient without quenching
Machine conditions used
  800us bunch-trains (2400 bunches)
  Average current over 800us: ~4.5mA (1.5nC/3MHz)
  Beam energy: 1GeV
  Energy gain on ACC67: 380MeV with 13 cavities
  Operating gradients on ACC67: 29MV/m average, four cavities running above 31MV/m

## Slide 4: Key Results
Beam operation with 800us/4.5mA bunch trains, and…
  Gradients of all cavities in vector sum flat within +/-0.3%,
  All cavities in vector sum operating within 5-10% of quench
First experience of ‘high gradient operations management’
  Quench detection / exception handling
  Gradient ‘soft limiter’ to dynamically prevent quenching
  Data-point of running machine into quench with 800us/4.5mA
Beam operation with 800us/4.5mA bunch trains, and..
  RF forward power within ~7% of klystron saturation
Ramp-up from ~zero to 800us/4.5mA pulses without quenching
Rapid recovery to 800us/4.5mA after trip (‘crash test’)

## Slide 5: TD Phase R&D results (updated mid 2012): System Tests with Beam at FLASH
High beam power and long bunch-trains (Sept 2009) |  | 
Metric | ILC Goal | Achieved
Macro-pulse current | 9mA (5.8mA) | 9mA
Bunches per pulse | 2400 x 3nC (3MHz) | 1800 x 3nC 2400 x 2nC
Cavities operating at high gradients, close to quench | 31.5MV/m +/-20% | 4 cavities > 30MV/m
Gradient operating margins (updated following Feb 2012 studies) |  | 
Metric | ILC Goal | Achieved
Cavity gradient flatness (all cavities in vector sum) | 2% DV/V (800ms, 5.8mA) (800ms, 9mA) | <0.3% DV/V (800ms, 4.5mA) First tests of automation for Pk/Ql control
Gradient operating margin | All cavities operating within 3% of quench limits | Some cavities within ~5% of quench (800us, 4.5mA) First tests of operations strategies for gradients close to quench
Energy Stability | 0.1% rms at 250GeV | <0.15% p-p (0.4ms) <0.02% rms (5Hz)

## Slide 6: Check-list of TD Phase accomplishments
Long bunch trains, heavy beam loading demonstration
  6mA / 800us demonstrated ( TDR Baseline)
  9mA / 800us marginally achieved (luminosity upgrade)
Vector Sum control of RF unit
  Operation of RF units comprising 16 and 24 cavities
  Intra- and inter-pulse stability better than 0.02%
Operating gradients
  Operation up to average of 29MV/m (24MV/m to 33MV/m)
  Lorentz-force detuning compensation on all cavities simultaneously
Pk/Ql control for optimizing gradient profile
  Demonstrated flat gradient solutions to +/-0.3%
  ILC baseline has more knobs (power ratios), so easier

## Slide 7: Check-list of TD Phase accomplishments
Klystron overhead
  First results: beam operation within 7% of saturation
  (Need to evaluate effect on energy stability)
Operation close to quench
  Several cavities within 5-10% of quench at 4.5mA, 800us
Operation close to quench (operability)
  Ramp-up to 4.5mA, 800us within 10% of quench demonstrated without quenching
  Rapid recovery after quench
  Quench detection / prevention with beam loading
HOM coupler
  Beam tests during high power 9mA/800us tests in 2009
  Excellent agreement between model and measured data
Strengthen these results

## Slide 8
9mA Studies: evaluating rf power overhead requirements
(4.5mA/800us bunch trains)
Klystron high voltage was reduced from 108KV to 86.5KV so that the rf output just saturated during the fill
The required beam-on power ended up being ~7% below saturation
Response to step up is slower because the klystron cannot deliver the power demanded

## Slide 9: Klystron saturation studies at TDR low-power baseline parameters
Klystron saturation studies
  In Feb, we didn’t have enough beam current to run in saturation during beam-on period
In Sept, should perform klystron saturation studies at the new TDR ‘low power’ baseline parameters. Parameters relative to RDR…
  Average current goes from 9mA to 6mA
  Ql goes from 3e6 to 5e6
  Fill time goes from 600us to 900us
  Pulse length goes from 1ms to 700us

## Slide 10: Pushing closer to quench
In Feb, we didn’t go as far up in gradients as we could have done – we have further to go
Gradient ‘pre-limiter’ was working only on ACC6 cavities, and we only barely got started on learning how to set up and use the pre-limiters
  In Sept, we need pre-limiters on all the ACC6/7 cavities
  Work on setting up the limiter and pre-limiter thresholds
Another possible gradient related study (FEL not ILC)
  Pushing for higher total linac energies at lower charge
  Would need pre-limiters on ACC4/5 as well as ACC6/7
  Wouldn’t be able to detune cavities as we do for ILC study
  How significant would this study be?

## Slide 11: Gradient operations management: ‘Soft-limiter’ dynamically prevents quenches
If any cavity gradient reaches a defined threshold, the Klystron is automatically ramped down within the rf pulse. Prevents quench without initiating an rf trip

## Slide 12
Main study items
  Klystron saturation studies at ILC/TDR low-power baseline
  Push more cavities closer to quench
  Other high priority items…?
It would also be good to work on the exception handling, eg
  Implement ‘operations-quality’ gradient flattening algorithm
  Cross-linkages between automation tools – integration
  Need better exception handling, better uniformity
Preparation tasks – see Julien’s slide from earlier