## Slide 1: 9mA webex meeting 3rd July 2012
Updates on FLASH activities
‘Missing Measurements’ for Sept 9mA program

## Slide 2: ‘Missing Measurements’: studies program for Sept 9mA shifts
Context
  ILC Global Design Effort formally coming the end
  Technical Design Report is being written
  Sept 9mA studies will be the last before formal completion of the ILC Global Design Effort
  The most important ILC studies – shows that an ILC can be built and actually work
What should we try to accomplish in Sept…?

## Slide 3: Key Results
Beam operation with 800us/4.5mA bunch trains, and…
  Gradients of all cavities in vector sum flat within +/-0.3%,
  All cavities in vector sum operating within 5-10% of quench
First experience of ‘high gradient operations management’
  Quench detection / exception handling
  Gradient ‘soft limiter’ to dynamically prevent quenching
  Data-point of running machine into quench with 800us/4.5mA
Beam operation with 800us/4.5mA bunch trains, and..
  RF forward power within ~7% of klystron saturation
Ramp-up from ~zero to 800us/4.5mA pulses without quenching
Rapid recovery (‘crash test’): 800us/4.5mA -> trip -> 800us/4.5mA

## Slide 4: if we stopped now… System Tests with Beam at FLASH
High beam power and long bunch-trains (Sept 2009) |  | 
Metric | ILC Goal | Achieved
Macro-pulse current | 9mA (5.8mA) | 9mA
Bunches per pulse | 2400 x 3nC (3MHz) | 1800 x 3nC 2400 x 2nC
Cavities operating at high gradients, close to quench | 31.5MV/m +/-20% | 4 cavities > 30MV/m
Gradient operating margins (updated following Feb 2012 studies) |  | 
Metric | ILC Goal | Achieved
Cavity gradient flatness (all cavities in vector sum) | 2% DV/V (800ms, 5.8mA) (800ms, 9mA) | <0.3% DV/V (800ms, 4.5mA) First tests of automation for Pk/Ql control
Gradient operating margin | All cavities operating within 3% of quench limits | Some cavities within ~5% of quench (800us, 4.5mA) First tests of operations strategies for gradients close to quench
Energy Stability | 0.1% rms at 250GeV | <0.15% p-p (0.4ms) <0.02% rms (5Hz)
Already a compelling demonstration that we could run an ILC at the specified parameters

## Slide 5: Pushing the parameters beyond what we already have achieved (A yet stronger demo)
We’re not quite there with the demo that we can operate within ILC gradient margins
  Gradient margins themselves
  Running at the ILC current (now 5.8mA)
  Definitely want to spend some time understanding how to use the soft limiters wrt quench limits
  Can we dynamically recover from marginally starting to quench
We also not quite there demonstrating operation with minimal klystron power overhead
  Only one datapoint so far
Conclusion: demo context, we should push further with what we did in Feb
What about any tests related to Klystron Cluster Scheme..?

## Slide 6: Characterization context
What can we do now that we’d want to include in the 9mA journal article(s)…?
(My view) – we would want to show an understanding of the issues and limitations
  Characterize operation close to gradient margins
  Characterize operation close to power limits

## Slide 7
Evaluating rf power overhead requirements
(4.5mA/800us bunch trains)
Klystron high voltage was reduced from 108KV to 86.5KV so that the rf output just saturated during the fill
The required beam-on power ended up being ~7% below saturation
Response to step up is slower because the klystron cannot deliver the power demanded

## Slide 8: TTF/FLASH layout 9mA Experiment
An issue for studying gradient margins: not all cavities reach their quench limits at the same time (impact of being close to quench may not be visible on VS)

## Slide 9: How to characterize operation close to quench…?
Questions (still) to be answered
  How does stability change as we get closer to quench limits
  Is there a knee or a hard threshold on how close we can run?
  …
Conditions
  Reduce number of cavities in VS to get some number of cavities all very close to the quench limits (VS dominated by cavities close to quench)

## Slide 10: How to characterize operation close to klystron saturation…?
Questions (still) to be answered
  How does stability change as we get closer to quench limits
  Is there a knee or a hard threshold on how close we can run?
  How much benefit do we get from klystron linearization?
Conditions
  Beam-on power as high as possible (above the fill power)
  Run klystron down till we can no longer reach the VS setpoint with the beam power
  Use Klystron linearization function in LLRF controller?

## Slide 11
What else…?
Proposals for additional measurements to strengthen material for 9mA journal article(s)
….discussion