## Slide 1: 9mA webex meeting on 17th July Notes (1)
General Updates
John: 9mA studies are confirmed for KW38 (week of Sept 17) but actual dates not yet fixed. Julien: FYI, there is a big event at DESY on Sept 19th
Valeri: new gun has been working well so far
Christian: will be doing studies with uTCA LLRF test system weekend. Electronics racks are located in the FLASH tunnel to mimic radiation environment they will see at XFEL
New quench server has been implemented that should be more robust against false trips than in Feb
John: please consider whether there are specific studies that we’d want to do for inclusion in the planned 9mA Journal article

## Slide 2: Notes (2)
Klystron saturation studies
Shin: increasing beam current would be the desired option for increasing klystron power during flat-top. Also needed for gradient operation study with beam loading. We need an update from Siggi on gun/transport
Valeri: it could be quite difficult to increase beam current due to transport issues (even if gun delivers the charge). Experience from Feb shows this
Valeri: yes, it would be possible to lengthen the fill time to >700us to reduce fill power (we used 660us in Feb) while maintaining flat-top power
Brian: we should measure transfer function LLRF drive to klystron o/p
Brian: is drive amplifier saturation a problem? In Feb, we avoided this situation by reducing the attenuation in the klystron drive chain
Christian: observed drift in stability during Feb saturation study (Shin’s slide) – was this due to some automation scripts? Christian will check daq data (needs timestamps for daq)
Other options for having higher relative klystron power during flat-top than during fill time?

## Slide 3: Notes (2)
John: could we do the study on ACC45 instead of ACC67 and then increase the average loaded Qs? (gradient spread is lower)
Julien: ACC45 has stub tuners not motorized couplers, so much more difficult to change the Qls
John: could we increase the flat-top power by running all the cavities off resonance during the flat-top?
Other items
Julien: during Sept study, we should measure the increased rf power required to flattening the gradients with Pk/Ql control
Shin: propose to study what happens operationally if we dynamically lose a piezo on a single cavity and hence lose LFD compensation
For next meeting (31 July)
Gustavo will show results of additional analysis from Feb saturation study
Julien will look at the proposal to use detuning to increase flat-top power