## Slide 1: 9mA meeting, 17th July 2012
Klystron saturation studies planning

## Slide 2: Update on studies dates for Sept
~15 shifts are expected
Studies are confirmed for KW38 (week of Sept 17th)
Exact dates within KW38 are not yet determined (when..?)

## Slide 3: ‘Missing Measurements’: studies program for Sept 9mA shifts
Context
  ILC Global Design Effort formally coming the end
  Technical Design Report is being written
  Sept 9mA studies will be the last before formal completion of the ILC Global Design Effort
  The most important ILC studies – shows that an ILC can be built and actually work
What should we try to accomplish in Sept…?

## Slide 4: Pushing the parameters beyond what we already have achieved (A yet stronger demo)
We’re not quite there with the demo that we can operate within ILC gradient margins
  Gradient margins themselves
  Running at the ILC current (now 5.8mA)
  Definitely want to spend some time understanding how to use the soft limiters wrt quench limits
  Can we dynamically recover from marginally starting to quench
We also not quite there demonstrating operation with minimal klystron power overhead
  Few datapoints so far
What about any tests related to Klystron Cluster Scheme..?

## Slide 5: Characterization context
What can we do now that we’d want to include in the 9mA journal article(s)…?
(My view) – we would want to show an understanding of the issues and limitations
  Characterize operation close to gradient margins
  Characterize operation close to power limits

## Slide 6
Evaluating rf power overhead requirements
(4.5mA/800us bunch trains)
Klystron high voltage was reduced from 108KV to 86.5KV so that the rf output just saturated during the fill
The required beam-on power ended up being ~7% below saturation
Response to step up is slower because the klystron cannot deliver the power demanded

## Slide 7: How to characterize operation close to klystron saturation…?
Questions (still) to be answered
  How does stability change as we get closer to klystron saturation
  Is there a knee or a hard threshold on how close we can run?
  How much benefit do we get from klystron linearization?
Conditions
  Beam-on power as high as possible (above the fill power)
  Run klystron down till we can no longer reach the VS setpoint with the beam power
  Use Klystron linearization function in LLRF controller?