## Slide 1: Klystron saturation studies: Options for changing relative fill and flat-top power..?
John Carwardine

## Slide 2: Some ideas for changing parameters for increasing relative flat-top power (ACC67)
Option | Pro | Con
Increase beam current | It’s the obvious one – we’d need ~5.5mA | Gun conditioning? Beam transport issues
Increase fill time | Reduces fill power | Already did that in Feb – ran out of room with the timing configuration (NO)
Lower the average QL | Lower Ql = shorter fill time for same gradient, or lower fill power for same fill time | Still need to use spread of QLs to maintain flat gradients with beam loading so we don’t hit quench limits Matched current scales with 1/QL, so we need proportionately more flat-top power
Dynamically detune the cavities at end of fill the piezos (or don’t compensate LFD) | Needs more flat-top power (what we want) | Practical? Can we dynamically change the Ql fast enough using piezos??

## Slide 3: Operational gradients
Chart: 
| ACC1-1 | ACC1-2 | ACC1-3 | ACC1-4 | ACC1-5 | ACC1-6 | ACC1-7 | ACC1-8 | ACC2-1 | ACC2-2 | ACC2-3 | ACC2-4 | ACC2-5 | ACC2-6 | ACC2-7 | ACC2-8 | ACC3-1 | ACC3-2 | ACC3-3 | ACC3-4 | ACC3-5 | ACC3-6 | ACC3-7 | ACC3-8 | ACC4-1 | ACC4-2 | ACC4-3 | ACC4-4 | ACC4-5 | ACC4-6 | ACC4-7 | ACC4-8 | ACC5-1 | ACC5-2 | ACC5-3 | ACC5-4 | ACC5-5 | ACC5-6 | ACC5-7 | ACC5-8 | ACC6-1 | ACC6-2 | ACC6-3 | ACC6-4 | ACC6-5 | ACC6-6 | ACC6-7 | ACC6-8 | ACC7-1 | ACC7-2 | ACC7-3 | ACC7-4 | ACC7-5 | ACC7-6 | ACC7-7 | ACC7-8
Operation | 19.7682 | 19.9971 | 19.7682 | 19.7682 | 24.5883 | 24.5883 | 23.7535 | 24.3068 | 20.2035 | 16.0482 | 22.6687 | 22.6687 | 22.6687 | 18.0064 | 22.6687 | 22.6687 | 25.9819 | 25.6219 | 25.7619 | 25.572 | 25.4783 | 24.7854 | 24.9903 | 24.9696 | 22.4337 | 23.9917 | 23.9917 | 23.9917 | 23.9917 | 23.9917 | 23.9917 | 23.9917 | 26.6682 | 26.7604 | 26.853 | 27.1015 | 27.7009 | 27.669 | 27.5736 | 27.5419 | 30.9002 | 31.981 | 29.7189 | 29.2486 | 18.5154 | 19.0592 | 23.2981 | 23.0731 | 25.8373 | 25.8373 | 26.7282 | 26.7282 | 31.1829 | 31.1829 | 23.1644 | 23.1644
Margin | 0.23176 | 0.0028518 | 0.23176 | 0.23176 | 0.41175 | 0.41175 | 1.2465 | 0.69321 | 1.7965 | 1.9518 | 2.3313 | 4.3313 | 2.3313 | 0.99359 | 2.3313 | 1.3313 | 2.0181 | 4.3781 | 3.2381 | 4.428 | 4.5217 | 0.21464 | 0.0096645 | 3.0304 | 0.56628 | -0.9917 | -0.9917 | -0.9917 | -0.9917 | -0.9917 | -0.9917 | -0.9917 | 2.3318 | 0.23955 | 1.147 | 0.8985 | 1.2991 | 0.33101 | 0.42641 | -1.5419 | 3.0998 | 0.019039 | 4.2811 | 2.7514 | 2.4846 | 1.9408 | 5.7019 | 2.9269 | 3.1627 | 5.1627 | 7.2718 | 3.2718 | 3.8171 | 7.8171 | 3.8356 | 2.8356

## Slide 4: Options (cont)
Option | Pro | Con
Raise average QL | Matched current scales with 1/Ql, so flat-top power goes up even though gradients are lower | Fill time becomes longer for same gradient or gradient is less for same fill power Still need spread of Qls to avoid gradient tilts
Use ACC45 instead of ACC67 | ACC4 cavities on run at identical gradients, so no spread of QLs needed, ACC5 cavities have lower spread then can lower average Ql to reduce fill time | Can we reach klystron saturation? Operational issues? Do we gain enough? Problem – stub tuners not motorized couplers on ACC45