## Slide 1: STF Quantum-Beam Accelerator commissioning status
H. Hayano, KEK, 05292012

## Slide 2
KEK-STF
Quantum-Beam Accelerator
STF Quantum-Beam experiment
2012. Feb : cool-down started,
April : beam acceleration
experiment: June run,
October run
High-flux X-ray by Inverse-Compton scattering
10mA electron beam （40MeV, 1ms, 5Hz)
4-mirror laser resonator cavity
head-on collision with beam
Target: 1.3 x 1010 photons/sec 1%bandwidth
30KeV X-ray
Capture cryomodule ( 2 SC cavities )
collision point
(Laser, electron beam)
photocathode RFgun

## Slide 3
Plan of X-ray generation by Inverse-compton scattering
40MeV, head-on collision
 | Electron | Laser
Energy | 40MeV | 1.17eV (λ=1064nm)
Energy spread | 0.1% (rms) | 
Beam size(rms) | 10μm | 10μm
Pulse width(FWHM) | 12ps | 12ps
Intensity | 61.5 pC/bunch | 50mJ/pulse
Number of bunches | 162500 | ----
Emittance | 0.5π mm mrad | 
Collision angle | 0deg (Head on) | 
Rep. Rate | 5Hz | 
4-mirror laser accumulation, head-on with e-beam
target: 1.3x1010 photons/sec/1%bw
max. 28 keV X-ray
X-ray
X-ray Energy
X-ray Energy
X-ray angle

## Slide 4
STF Photo-cathode RF-gun
RFgun cavity
Cs2Te photocathode
Preparation chamber
Cs2Te
Photocathode
Preparation
Chamber
Molybdenum cathode-block
1ms beam was extracted
from Gun
Quantum efficiency of photo-cathode
0.5 – 1.5%
dark-current (peak)
~300µA
emittance:
reliable measurement was not yet done

## Slide 5
Accelerated beam (April 13,2012)
Energy：40MeV、
Beam charge：41pC/bunch、28bunches
repition：5Hz
RFgun cavity power：2.2MW
(34.6MV/m cathode field）
Beam energy from RFgun：3.3MeV/c
SC cavity voltage；
MHI-012:20.15MV/m (40MV/m in VT)
MHI-013:21.5 MV/m (33MV/m in VT)
Accelerated Beam bunch
Accelerated Beam profile
Beam orbit
Blue：BPM signal: exit of Rfgun
Purple：WCM signal: downstream of cryomodule
green：beam-loss-monitor signal
Yellow：beam gate timing
X orbit
Y orbit
Beam profile at collision point：
1mm(FWHM)

## Slide 6
162.5MHz 10,000 bunches (61.5µsec) acceleration
61.5µsec beam
4% of Design maximum Beam Power

## Slide 7
Radiaiton leakage to STF surface buliding (4% of design beam power)
EP room
non-control area
(<0.2µSv/h)
Klystron gallery
control area
(<20µSv/h)
Tunnel
underground
beam dump
concrete shield
Need to reduce 1/14 for controlled-area
1/28 for non-controlled area,
by putting more lead-shield, concrete,...
scale to
(control area)
(non-control area)
Waveguide hole
STF Building cross-section

## Slide 8
Waveguide access hole between tunnel
and Klystron gallery.
(looking up from tunnel)
lead-shield were installed in the WG-hole
lead-block were placed in front of dump
STF accelerator beam dump.
Beam goes from left to right.
More shield were installed

## Slide 9
April 2012
Sun
Mon
Tue
Wed
Thu
Fri
Sat
KILC12
G.W. shutdown
GV open
cool-down
cool-down
cool-down
cool-down
radiation survey by 4% beam power
beam to dump, beam monitor tuning
beam commissioning start

## Slide 10
May 2012
Sun
Mon
Tue
Wed
Thu
Fri
Sat
radiation survey by 4% beam power
cryomodule cool-down
cryomodule cool-down
cool-down
Beam Operation re-start
4 mirror
Laser
Accumulation
cavity
Lead block
shield
RFgun
Cooling
System
improvement
SC-cavity process
SC-cavity
process
Schedule

## Slide 11
June 2012
Sun
Mon
Tue
Wed
Thu
Fri
Sat
cool-down
cool-down
cool-down
cool-down
beam focus operation
beam focus operation
beam focus / BG reduction
beam focus / BG reduction
Operation target: Reduce beam emittance, then focus the beam down to 10µm size.

## Slide 12
July 2012
Sun
Mon
Tue
Wed
Thu
Fri
Sat
Beam-laser collision trial
cool-down
cool-down
radiation shield examination
Operation target: Try to collide electron beam with Laser beam.
Summer shutdown