## Slide 1: Mechanical studies for a TPC at the ILC
I-DEAS for the ILD-TPC
Ties Behnke, Volker Prahl
DESY Hamburg

## Slide 2: The mechanical model
Detector components inside the magnet
  VTX
  Silicon
  TPC
  Calorimeters
Current model:
TPC supported from Coil
Inner detectors supported from TPC

## Slide 3: Design studies: mechanical properties
Light weight Endplate
by D.Peterson
PRC report 2010
FEM Calculations by CEA Saclay:
Deflection O(150 µm) @ 3 mbar
We still do not have a very good understanding of the beviour of the system.

## Slide 4: Details of TPC design
Infrastructure ( Cables, Gaslines, Cooling, Alignment ) C.Clerc
Boudaries for a design have been defined

## Slide 5: Material distribution
40%X0 spike in the middle of the detector:
Caused by the cathode support

## Slide 6: Support Rings
Current model:
Massive Carbon-fiber support ring
Proposed alternative model
Support ring from composite materials:
Cathode foil
Support rings carbon – foam - carbon
1mm Carbon (0.35%)
28mm Carbon Foam (0.5%)
1 mm Carbon (0.35%)
About 2% X0 (instead of 40%) for two rings

## Slide 7: Cathode design and support
STAR TPC
Typical cathode design:
Tensioned foil (mylar, CFC, …) supported by inner and outer ring
Design goals and problems:
Light weight, thin
Mechanically stable and robust (inaccessible)
Supply of HV non trivial
Studies in laboratory support this design: load is about 2kg/10cm outer radius
HV supply through special HV cable, OF about 14mm for 100 kV

## Slide 8: Field Cage Design
Wallstructure Large Prototype TPC: HV stable up to 30 kV
→ extrapolate to ILD-TPC (O(100 kV))
Estimate: Outer field cage 60mm, inner field cage 30mm