## Slide 1
STF accelerator status
(RFgun + capture cryomodule operation)
H. Hayano, 07032012

## Slide 2
KEK-STF
Quantum-Beam Accelerator
STF Quantum-Beam experiment
2012. Feb : cool-down started,
April-June : beam acceleration
High-flux X-ray by Inverse-Comton scattering
10mA electron beam （40MeV, １ｍｓ, ５Ｈｚ）
4-mirror laser resonator cavity
head-on collision with beam
Target: 1.3 x 1010 photons/sec 1%bandwidth
Capture cryomodule ( 2 SC cavities )
collision point
(Laser, electron beam)
photocathode RFgun

## Slide 3
20% of full-beam power operation
40MeV, 15pC/bunch, 162500bunches
（June, 2012）
ー＞ILC beam （1ms length） acceleration
ILC beam intensity （6.6mA)
1ms
Accelerator commissioning for beam extraction, acceleration, and 1ms beam
beam acceleration
40MeV, 41pC/bunch, 28bunches（April, 2012）
Fiber Beam loss monitor
Beam on gate
BPM signal
PIN Beam loss monitor
1ms
STF QB accelerator commissioning (April-June 2012)
1ms Beam extraction from RF-gun (Mar.22,2012)
Accelerated Beam bunches
Beam extraction

## Slide 4
Swap
Beam emittance of STF accelerator
εx, εy ：0.8 – 1.3 x 10-6 @ 15-25pC/bunch, 39MeV（close to the design）

## Slide 5: Beam size measurement June 21,2012
First Wire scanner:
σx：22.8 µm
σy：21.3 µm
Second wire scanner
σx：56.5 µm
σy：52.6 µm
RF gun 3.5 MW, SC cav 14.5 & 25.5 MV/m
40 MeV, 35 - 40 pC, 40 bunches
Still beam line Tuning is necessary
collision point

## Slide 6
Plan of X-ray generation by Inverse-compton scattering
40MeV, head-on collision
 | Electron | Laser
Energy | 40MeV | 1.17eV (λ=1064nm)
Energy spread | 0.1% (rms) | 
Beam size(rms) | 10μm | 10μm
Pulse width(FWHM) | 12ps | 12ps
Intensity | 61.5 pC/bunch | 50mJ/pulse
Number of bunches | 162500 | ----
Emittance | 0.5π mm mrad | 
Collision angle | 0deg (Head on) | 
Rep. Rate | 5Hz | 
4-mirror laser accumulation, head-on with e-beam
target: 1.3x1010 photons/sec/1%bw
max. 28 keV X-ray
collision will be started in September