DBD SiD Higgs
Branching Ratio Analysis
Presented by
H. Neal (SLAC)
@
The August 2012 SiD Workshop
@
Analysis work in progress by
A. Grohsjean, M. Stanitzki & H. Neal
and much support from
T. Barklow, N. Graf,
C. Grefe, J. McCormick, S.Poss, P. Rollof & J. Strube

---
Motivation for using e+e- → nnH
Goal is to measure BR errors for gg,WW* using e+e- → nnH
@ 1 TeV
WW fusion cross-section rises with ECOM
WW fusion
s grows
as ln(s)
Higgstralung
SLAC-R-570

---
Elements of the nnH Benchmark
  - flavor/anti-flavor tagging using LCFI+
  - Include extra background
  - Full simulation using SLIC
  - Mixed stdhep from Whizard with various polarizations (+80%,-20%),(-80%,+20%)
  - Beam spot simulation
  - Pandora PFA
    Continuing the work of Ron and Tim

---
Production Steps
Use of the GRID tools has been productive as well as fun.
Thanks to Jan and Philipp for development of recoChain
Initial orientation from
Jeremy and Norman was extremely useful in getting started.

---
Signal Samples
The following signal samples were generated thanks to Tim Barklow:
/nfs/slac/g/lcd/ilc_data4/DBD/ILC1000/higgs_ffh_nomu/stdhep/
Uploaded to:
 /ilc/user/j/jstrube/SID_DBD/ILC1000/mixed/higgs_ffh_nomu/stdhep/:
500 Event samples
#Files Filename prefix
   3089 higgs_ffh_nomu_+80e-_-20e
   3089 higgs_ffh_nomu_-80e-_+20e

---
Analyzable nnH Data
MC truth
lcsim reco
tracks
MC truth
MC truth
By H. Neal
From running recoChain on /ilc/user/j/jstrube/SID_DBD/ILC1000/mixed/higgs_ffh_nomu/stdhep/higgs_ffh_nomu_+80e-_-20e+_007.stdhep and then analyzing using JAS3

---
Higgs event selection
PreSelection:
- no isolated electron or muon
- |cos qthrust| < 0.95,
- 100 < E(visible) < 400 GeV
- 20 < pT (visible) < 500 GeV
Previously used selection variables with cuts depending on the mode: (see arXiv:hep-ph/0312268)
- visible mass M(visible)
- N(chg)
- N(imp) - # large impact parameter tracks
- N(jet) as determined by the PYCLUS algorithm of PYTHIA with parameters MSTU(46)=1 and PARU(44)=5.

---
Mode Specific Selection Cuts
h → bb
	6<N(chg)<19	7<N(imp)<19	2<N(jet)<3	Mh-10 GeV<M(vis)<Mh+6 GeV
h →gg
	N(chg)=0	N(imp)=0	N(jet)=2	Mh-2 GeV<M(vis)<Mh+1 GeV
h →WW
	16<N(chg)<44	N(imp)<6	4<N(jet)<5	Mh-10 GeV<M(vis)<Mh+6 GeV
h →gg
	11<N(chg)<49	N(imp)<6	2<N(jet)<4	Mh-10 GeV<M(vis)<Mh+6 GeV
N(imp) will be replaced with LCFI+ flavor/anti-flavor tagging and the other cuts will need to be
retuned due to new backgrounds.
based on arXiv:hep-ph/0312268

---
Higgs Production Mode
from M. Stanitzki
and A.Grohsjean
Fusion includes ZH + Interference
WW Fusion
ZZ Fusion
ZH nunu
ZH ll
ZH qq
Higgs to gg and WW*

---
Decay Modes
from M. Stanitzki
and A.Grohsjean
bb
WW
gg
ττ
ZZ
cc
γγ
ss
Zγ

---
Recoil Mass and Higgs Angle
in WW Fusion and ZH Events
from M. Stanitzki
and A.Grohsjean
ZH
WW Fusion

---
From Simulation
- Durham
- Select Events > 9 Tracks
- Force into two jets
- Works most of the time
- They are getting with an adhoc-fit
  - 121.9 +/- 5.1 GeV
  - Tail pulls it downwards
from M. Stanitzki
and A.Grohsjean

---
Known work to be done
- Add backgrounds
- Validate DSTs
- train flavor/anti-flavor taggers and apply to DSTs
- Apply improved electron ID
- Handle overlap between bb, cc, gg and WW
- Exactly define what is the signal
  (ZH included or not?)
- Alexander is working on the gluon tagging

---
Signal Production in Progress
bash-3.2$ dirac-dms-get-file /ilc/prod/ilc/sid/1000_p80m20/higgs_ffh_nomu/sidloi3/SIM/00001729/004/higgs_ffh_nomu_p80m20_sim_1729_4002.slcio
{'Failed': {},
 'Successful': {'/ilc/prod/ilc/sid/1000_p80m20/higgs_ffh_nomu/sidloi3/SIM/00001729/004/higgs_ffh_nomu_p80m20_sim_1729_4002.slcio': '/afs/slac.stanford.edu/u/ey/homer/sid/grid_vvh/higgs_ffh_nomu_p80m20_sim_1729_4002.slcio'}}

---
Summary
- Preparing to expediently complete the DBD Higgs BR Benchmark with updated simulation and flavor/anti-flavor tagging
- Production output of signals and backgrounds soon becoming available
- Analysis tools and data reduction being exercised
- Looking forward to having preliminary results soon.
- Many thanks to the help of the production experts

---
LCSIM output from running on
Current Sim. Production Output

---
Tracks