## Slide 1: Future Accelerators
Marc Ross, SLAC - ILC
Higg’s factories and beyond:
ILC and alternate schemes

## Slide 2: Outline
International Linear Collider (ILC)
  Parameters
  Superconducting RF and Nano-beams
  Staging: 250 GeV to 1 TeV
e+/e- Ring Colliders
  Parameters
  AC Power Consumption and Construction Cost
  Tunneling near CERN
μ+/μ- Colliders
  Staging and Parameters
  R & D

## Slide 3: ILC in a Nutshell
Damping Rings
Polarised electron source
Polarised positron source
Ring to Main Linac (RTML)
(inc. bunch compressors)
e- Main Linac
Beam Delivery System (BDS) & physics detectors
e+ Main Linac
Beam dump
not too scale
310 x football pitch
Total site length (500 GeV CM) | 30.5 km
SCRF Main Linacs | 22.2 km
RTML (bunch compressors) | 2.8 km
Positron source | 1.1 km
BDS / IR | 4.5 km
Damping Rings (circumference) | 3.2 km

## Slide 4
ILC Parameters

## Slide 5: ILC Overview
Designed and optimized for 500 GeV Ecm; upgradeable to 1 TeV
L500 ~ 1.8e34 with 162 MW wall plug
  L1000 ~ 5e34 with 300 MW wall plug
R & D program completed: Detailed Design
  Technology Demonstrated (SCRF)
  8%-scale Demonstration ‘E-XFEL’ (DESY) in 2015
  IR optics & tuning Demonstration ‘ATF-II’ (KEK) 
Physics Studies, Detector / Machine Design Report completed 02.2013
  Culmination of 6 year design study

## Slide 7: Fermilab – Niowave SCRF Cavity Team

## Slide 8: ILC Cavity Assembly (Helium tank, mag. shield, tuner and coupler)
Graphics by Rey. Hori

## Slide 9: Linac building block: the Cryomodule:
Graphics by Rey. Hori

## Slide 10: 12 GeV cavities: overall performance
CEBAF 12 GeV upgrade
72/85 @ admin limit (85%)
Cavities made by RI (Germany); Followed ILC Process
Reported 11.2012 by F. Pilat
Vertical Test; 1500 MHz 7 cell; 10% gradient correction

## Slide 11: Global Progress in ILC Cavity Gradient Yield
(94+/-6)% acceptable for ILC mass production

## Slide 12: IT optics and tuning beam demonstration
ATF-II at KEK
Model Final-Focus optics system
Beam from ultra-low emittance damping ring

## Slide 13: KEK - ATF2 Facility Layout
120 m

## Slide 14: ATF-2 achieves 72.8 nm
1994
2012

## Slide 15: Outline
International Linear Collider (ILC)
  Parameters
  Superconducting RF and Nano-beams
  Staging: 250 GeV to 1 TeV
e+/e- Ring Colliders
  Parameters
  AC Power Consumption and Construction Cost
  Tunneling near CERN
μ+/μ- Colliders
  Staging and Parameters
  R & D

## Slide 16: Luminosity Upgrade
Concept: increase nb from 1312 → 2625
  Reduce linac bunch spacing 554 ns → 336 ns
  Increase pulse current 5.8 → 8.8 mA
  Increase number of klystrons by ~50%
Doubles beam power  ×2 L (3.6×1034cm-2s-1)
Damping ring:
  Electron ring doubles current (389mA  778mA)
  Positron ring: possible 2nd (stacked) ring (e-cloud limit)
AC power: 161 MW  204 MW (est.)
  AC power increased by ×1.5
  shorter fill time and longer beam pulse results in higher RF-beam efficiency (44%  61%)

## Slide 17: TeV upgrade: Construction Scenario
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
BDS
Main Linac
e+ src
IP
BC
start civil construction
500GeV operations
500GeV operations
Installation/upgrade shutdown
civil construction + installation
final installation/connection
removal/relocation of BC
Removal of turnaround etc.
Installation of addition magnets etc.
Commissioning / operation at 1TeV
Notes: An obvious possible approach to minimizing downtime for physics.
Assume something like a total of 5 year construction with perhaps 12-18 months with no physics??

## Slide 18: TeV Upgrade
2.2 km
1.3 km
10.8 km
1.1 km
BDS
Main Linac
e+ src
bunch comp.
<26 km ?
(site length <52 km ?)
Main Linac
<Gcavity> = 31.5 MV/m
Geff ≈ 22.7 MV/m
(fill fact. = 0.72)
IP
central region
<10.8 km ?
Snowmass 2005 baseline recommendation for TeV upgrade:
Gcavity = 36 MV/m ⇒ 9.6 km
(VT ≥ 40 MV/m)
Based on use of low-loss or re-entrant cavity shapes
Assume Higher Gradient

## Slide 19: 250 GeV – Staged ILC
5.1 km
1.1 km
Main Linac
bunch comp.
2.2 km
1.3 km
BDS
e+ src
IP
central region
15.4 km
125 GeV transport
Half the linac
Full-length BDS tunnel & vacuum (TeV)
½ BDS magnets (instrumentation, CF etc)
1 RTML LTL
5km 125 GeV transport line
Extended tunnel/CFS already 500 GeV stage

## Slide 20: ILC at low/high Ecm
Low Ecm operation of upgraded ILC:
  L250 ~ 3e34; Wall plug 200 MW
  Possible Higgs Factory
High Ecm ~ 1.5 TeV
  L1500 ~ 6e34; Wall plug 340 MW
Chart: Luminosity vs Energy
| 250 | 500 | 1000 | 1500 | 240 | 350
ILC | 3 | 3.6 | 4.9 | 6
TLEP | 4.9 | 0.65
ILC - nominal
ILC - upgraded
80 km ring; per IP

## Slide 21
ILC Parameters

## Slide 22: Two Alternatives to ILC (1):
e+/ e- storage ring-based colliders
  Low Energy ‘factories’
  Assume substantial injection complex
  Enormous tunnel complex (step toward VLHC)
  Based on extrapolation of established technology
  R & D needed
Only 2 parameters:
  Ring Size and
  Site Power consumption
Civil engineering cost and strategy 

## Slide 23
From K. Yokoya

## Slide 24
From K. Yokoya:

## Slide 25
From K. Yokoya
Low emittance operation planned for Super KEK-B

## Slide 26: Collider ‘Wall Plug’ AC Power use:
ILC and 80 km ring: | ILC -H | ILC-nom | Ring - H | Ring - t
E_cm (GeV) | 250 | 500 | 240 | 350
SRF Power to Beam (MW) | 5.2 | 10.5 | 100 | 100
Eff. RF Length (m) | 7,837 | 15,674 | 600 | 1200
RF klystron peak efficiency (%) | 65 | 65 | 65 | 65
klystron operating margin, HVPS, Klystron Aux and klystron water cooling (% inefficiency) |  |  | 20* | 20
Overall system RF efficiency (%) | 10 | 14 | 45 | 45
Cryo (MW) | 16 | 32 | 20 | 40
Normal Conducting (exc. Injector complex) (MW) | 6 | 10 | 120** | 120
Injector complex | 32 | 32 | 16*** | 16
Conventional (Air, lighting, ..) | 6 | 6**** | 18 | 18
Total (exc. detector) | 112 | 153 | 396 | 416
* 5% for operating margin, 2% for auxiliaries, 3% for HVPS and 10% for water cooling
** assume 1.5 kW / m tunnel inclusive (ILC avg. 3 kW / m)
*** from SSC / Fermilab injector (linac + LEB + MEB); assumes LHC not needed
**** 6 MW for 30 km beam tunnel complex; ~3x more for 80 ring

## Slide 27: ILC AC Power loads:

## Slide 28: Questions asked for ‘Snowmass’:
CSS2013 / P5 planning process:
What the required parameters and key characteristics of lepton / gamma colliders in the Higg's factory range? with physics capabilities far beyond the LHC? at what cost? How does a Higgs factory scale cost-wise to a TeV scale linear collider?
Cost comparisons with concepts can only be done parametrically.

## Slide 29: ILC ‘value’ estimate:
‘Value’ is the direct cost of goods and services
Appropriate for in-kind projects
ILC: 7.8 B ILCU + 23 million labor person-hours

## Slide 30: Parametric ‘value’ costing for TeV–class machines (KILCU)*:
Civil Construction: 35 / m
Utilities: 5000 / MW
Superconducting RF 180 / m (inclusive)**
‘Conventional Acc.’ 35 / m
 |  | TLEP-t quantity | MILCU | ILC quantity | MILCU
Civil Construction | km | 80 | 3000 | 34 | 1200
Power and cooling | MW | 416 | 2000 | 162 | 800
SRF (incl. packing) | km | 1.2 / .7 | 250 | 22 | 4000
‘Conventional’ | km | 160 | 5500 *** | 12 | 800
Installation | km | 80 | 100 | 34 | 100
Total |  |  | 11000 |  | 7800**
* 1 ILCU = USD 01.2012
** cryogenics not included – reuse LHC assumed; 900 MILCU included for ILC
*** Conventional Acc. (Magnets, vacuum, etc) cost – scale reduced 2x for ring
Institutional Labor is part of the project cost and must also be analyzed.

## Slide 31: Outline
International Linear Collider (ILC)
  Parameters
  Superconducting RF and Nano-beams
  Staging: 250 GeV to 1 TeV
e+/e- Ring Colliders
  Parameters
  AC Power Consumption and Construction Cost
  Tunneling near CERN
μ+/μ- Colliders
  Staging and Parameters
  R & D

## Slide 32
European Strategy Submission – Krakow 08.2012 by CERN Civil Engineering: John Osborne
Presented at:

## Slide 33: Jura & Salève: Karst Geology
Tunneling risk
Karst (green):
  “Dissolution by layers of soluble bedrock, typically limestone”
  “rocky ground, caves, sinkholes, underground rivers, and the absence of surface streams and lakes”
  France; Kwangsi in China; Yucatán Peninsula; Florida in the United States

## Slide 34: Karst geology:
Florida US 03.2013

## Slide 35: CE considerations Tunneling
  Mountain area consists of Limestones and evaporates
    For 10% of tunnel
    Difficult tunneling conditions
      Local and unpredictable karst features
        Water conduits
        High flow rates (600L/sec)
      Water transports silt-clay sediments
        Difficult to drawing off water through
        pressure relief holes
        Increase of water inflow over time
        Difficulties in removal of the water
        Risk of aquifer pollution & depletion
      Anhydrites -> ‘badrock’ causes swelling
        Heaving of the tunnel invert
        Structural instabilities
        Probably low risk for 80km Lakeside option
        but high risk for 80km Jura option
LEP tunnel collapse
Geneva plain
Underneath Lake Geneva
Through Jura and Salève Mountains
Example of tunnel invert heave Chienberg tunnel, Switzerland

## Slide 36: Potential locations
Pre-feasibility study performed by CERN and the specialized firm ARUP.
  Focused on
    geology & hydrogeology,
    tunneling & construction,
    environmental impacts
  Result: for the 80km long tunnel location 2 ‘80km Lakeside’ is most feasible.
High
Low
Feasibility
Risk |  |  |  |  |  |  |  |  |  |  | 
 | water ingress | heaving ground | weak marls | hydro carbons | support & lining | ground response & convergence | hydrostatic pressure & drainage | Pollution of aquifers | effect of shafts on nature | effects of shafts on urban areas | Total
Jura 80 | 5 | 3 | 0 | 0 | 5 | 4 | 5 | 5 | 4 | 2 | 33
Lake 80 | 2 | 0 | 3 | 3 | 3 | 3 | 2 | 2 | 3 | 2 | 23
Lake 47 | 1 | 0 | 2 | 2 | 2 | 2 | 1 | 1 | 2 | 5 | 18

## Slide 37: CE considerations Optimization
Optimization studies for the project configuration have been started
  Bypass tunnel in geological and environmental sensitive area
  Inclined access tunnel in urban area
More optimization studies needed
  Incline tunnel?
  More bypass tunnels?

## Slide 38: Ring Collider R & D items:
Much related beam physics will be studied at Super KEK-B (2015 )
  IR optics and vertical emittance will be checked. SuperKEKB will try to x10 smaller vert emittance (than LEP) with full beam-beam.
CERN-region ring ‘optimization’ work
  Avoiding Karst geology (conclusion of 21.02 meeting)
Large ring cost is not substantially smaller than ILC
  Energy consumption is excessive

## Slide 39: Two Alternatives to ILC (2):
Muon colliders
  Very High energy without enormous tunneling
Basic R & D needed in four technical areas
  Normal Conducting RF
  Superconducting RF
  High Field magnets
  Targeting
System demonstrations:
  beam cooling and
  high power-on-target

## Slide 40: The U.S. Muon Accelerator Program
Mark Palmer
Frontier Facilities Meeting University of Chicago
February 25, 2013

## Slide 41: Muon Accelerators
Program Baselines

## Slide 42: The Muon Accelerator Program Timeline
 | 2010 |  | ~2020 |  | ~2030 | 
Muon Accelerator R&D Phase |  |  |  |  |  | 
Proton Driver Implementation (Project X @ FNAL) |  |  |  |  |  | 
Intensity Frontier |  |  |  |  |  | 
Energy Frontier |  |  |  |  |  | 
MAP Feasibility Assessment
Advanced Systems R&D
Muon Ionization Cooling Experiment (MICE)
IDS-NF RDR
Proposed Muon Storage Ring Facility (nSTORM)
Evolution to Full Spec n Factory
Collider Conceptual  Technical Design
Collider Construction  Physics Program
Proj X Ph I
Proj X Ph II
Proj X Ph III & IV
Indicates a date when an informed decision should be possible
Notes: Yellow diamonds indicate potential start of DOE CD process

## Slide 43: Muon Collider Concept
Proton source:
For example PROJECT X at 4 MW, with 2±1 ns long bunches
Goal: Produce a high intensity m beam whose 6D phase space is reduced by a factor of ~106-107 from its value at the production target
Collider: √s = 3 TeV
Circumference 4.5km L = 3×1034 cm-2s-1 m/bunch = 2x1012
s(p)/p = 0.1%
eN = 25 mm, e||N=70 mm
b* = 5mm
Rep. Rate = 12 Hz
Muon Collider Block Diagram

## Slide 44: Muon Collider Parameters
3-4 MeV CoM Energy Spread

## Slide 45: 126 GeV Higgs Factory
Major advantage for Physics of a + Higgs Factory: possibility of direct measurement of the Higgs boson width (~4MeV FWHM expected)
Reduced cooling:
N =0.3mmrad,
||N =1mmrad
s-channel coupling of Muons to HIGGS with high cross sections:
Muon Collider of with L = 1032 cm-2s-1 @ 63 GeV/beam (50000 Higgs/year)
Competitive with e+/e- Linear Collider with L = 2. 1034 cm-2s-1 @ 126 GeV/beam
Sharp resonance: momentum spread ~ 4 × 10-5
Han and Liu
hep-ph 1210.7803
~30 T HTS Final Cooling Solenoids

## Slide 46: Overview of R&D Areas
Design Studies
  Proton Driver
  Front End
  Cooling
  Acceleration and Storage
  Collider
  Machine-Detector Interface
  Work closely with physics and detector efforts
Major System Demonstration
  The Muon Ionization Cooling Experiment – MICE
    Major U.S. effort to provide key hardware: RF Cavities and couplers, Spectrometer Solenoids, Coupling Coils
    Experimental and Operations Support
Technology R&D
  Normal Conducting RF
    Vacuum RF Cavities with reduced breakdown rates in high magnetic fields
    Cavity Materials
    RF Cavities filled with high pressure gas
  Superconducting RF
    Demonstrating good Q0 performance with Niobium on Copper cavities
      Performance
      Fabrication techniques
  Magnets
    High field solenoids for cooling channel application
    10T dipole design (synergistic with LHC upgrade activities)
    Rapid cycling magnets for high energy hybrid synchrotron
    Shielded magnets for m decay in rings
  Target and Absorbers
    Liquid jet targets capable
    Capture solenoid technology

## Slide 47: MAP Technology Highlights
Successful Operation of 805 MHz “All Seasons” Cavity in 3T Magnetic Field under Vacuum
MuCool Test Area/Muons Inc
World Record HTS-only Coil 15T on-axis field 16T on coil
PBL/BNL
Demonstration of High Pressure RF Cavity in 3T Magnetic Field with Beam
Extrapolates to m-Collider Parameters
MuCool Test Area
Breakthrough in HTS Cable Performance with Cables Matching Strand Performance
FNAL-Tech Div T. Shen-Early Career Award
The Path to a Viable Muon Ionization Cooling Channel
Pure GH2
1% Dry Air (0.2% O2) in GH2
E0 = 25 MV/m
~50X reduction in
RF power dissipation
1% Dry Air
(0.2 % O2)
in GH2 at
B = 3T

## Slide 48: Muon collider R & D

## Slide 49: Summary: