## Slide 1: Status and update plan of the ATF DR
Nobuhiro Terunuma, KEK
European Linear Collider Workshop ECFA LC2013, May 28, 2013

## Slide 2: ATF DR status
Present users on ATF DR
  Cavity Comptons
  ATF2
Low emittance for ATF2 (~10pm)
  Maintained in each startup of the beam weeks
  Usually done in a shift
Studies for the smaller emittance (2pm)
  It has not been done in 2012 because of the ATF2 priority.
  It should be re-scheduled from now on.

## Slide 3: Emittance
Measured in DR
  XSR monitor
  ATF2
Measured in EXT
  wire scanners (Tungsten 10 um, Carbon 6 um)
  Multi-OTR monitor

## Slide 4: Laser Wire with Optical Cavity (DR)
The most accurate emittance monitor in ATF DR.
    14.7µm laser wire for X scan
    5.7µm for Y scan
But the measurement is
  time consuming.
  (scan: 15 min for X, 6 min for Y)
300mW 532nm Solid-state Laser
fed into optical cavity
Multi-bunch separated measurement
Two mirror cavity
Difficult to maintain
low signal intensity
Not in function in recent years
Upgrade is ongoing!

## Slide 5
Zone plate
image of 1ms exposure
SR X-ray beam line
sx = 48.2 ± 0.5 [mm]
sy = 6.4 ± 0.1 [mm]
Real-time monitor for emittance tuning in DR
X-Ray Telescope using Zone Plate at 3.2KeV
magnification : 20
  Non destructive measurement
  High resolution (< 1mm)
  2D direct imaging of the electron beam
  Exposure time (1 ms ~ 20 ms)
X-ray SR Monitor (XSR)

## Slide 6: Beta Measurement
Emittance is calculated by the formula;
y2=y y
 is calculated by fitting the  s at near Qs,
which are measured by tune slope.
ex.)->
by S.Kuroda, ATF2 Review

## Slide 7
Modified from figure in 13th ATF2 Project Meeting, January 12 2012, by Mark Woodley
Layout of Extraction Line
Skew Quads
(Coupling correction)
Beam size monitors
(Emittance,
Optics measurement)
Dispersive area.
Quads and skew Quads
(Dispersion correction)
septum magnets
2nd kicker
Damping Ring
FF
Kicker

## Slide 8: OTR beam profile monitor
J. Alabau, et.al.
Measure Single pulse beam size (faster than wire scanner).
We have 4 monitors  Evaluate projected x, y emittance
  Could evaluate normal mode emittance (4-D analysis)
microscope

## Slide 9: Example of OTR profile
from ATF Log Book

## Slide 10: DR Emittance Summary
2009 autum
I=4-5x109
2009 spring
I=5-6x109
Low emittance was recovered in the operation 2008-2009.
Measured y=8.56±0.46/ 8.43±1.79/ 3.50±1.78/ 2.00±1.61pm by XSR/ IF/ LW00/ LW01.
Study for the discrepancy is still on going.
Terunuma, Kuroda
by S.Kuroda, ATF2 Review

## Slide 11: Emittance Summary 2011-2013
Big Earthquake
3.11 2011

Test operation
Emittance in DR is around 10-12 pm
by S.Kuroda, ATF2 Review

## Slide 12: Emittance of extracted beam
Extracted emittance before May 2013 was bigger than that of DR about twice or more.
Is the DR emittance 10 pm?
Change of the coupling-correction scheme in May 2013, seems to remove the discrepancy between EXT and DR.

## Slide 13
by T.Okugi , ATF operation meeting

## Slide 14
by T.Okugi , ATF operation meeting

## Slide 16: DR BPM Upgrade for 2 pm emittance
The original read-out system designed for the single path position measurement has a 10 mm resolution.
Upgraded BPM readout system:
  FNAL-KEK collaboration
Broadband turn-by-turn mode (< 10 µm resolution)
  Injection 1,000 turns
  Extraction 64 turns
Narrowband mode with high resolution (~ 100 nm range)
  160 ms, 500,000 turns after injection
Installed in 2010 for all DR BPMs (96)
Downmix box at the beamline
BPM digitizer station

## Slide 17: Summary: Emittance in Damping Ring
We achieved minimum vertical emittance ~4pm in 2002~2003.
Recently, we have kept (nearly) the best condition.
For smaller vertical emittance (~ 2pm, ILC DR design),
  New beam size monitor for confirmation.
  Keep good alignment.
  Keep good BPM performance.
However, present priority is ATF2 study (Final focus test, demonstration).
  Damping Ring emittance is small enough for ATF2
by K.Kubo, ATF review, August 2012

## Slide 18: Optical Cavities in ATF DR
High intense gamma-ray generation
Optical cavities: 2-mirror  4-mirror
for the polarized positron source (Hiroshima/KEK)
for other application (LAL)
for the upgrade of Laser Wire scanner

## Slide 19
Laser-Compton-Scheme &
Laser Pulse Stacking
for pol. e+ generation
French Labs. : LAL (Orsay) in Collaboration with CELIA (Laser lab., Bordeaux) and LMA (mirror coatings Lab., Lyon)
Japanese Labs. : KEK, ATF group, Hiroshima University
France-Japan collaboration
by T.Omori

## Slide 20: Introduction
Polarized e+ by laser Compton Scheme
Ee~1GeV for 10MeV gammas
easy to control polarization
Toward the positron sources
-> increase intensity of gamma rays
-> Laser Pulse stacking cavity
by T.Omori

## Slide 21: Way 4-mirror Cavity? get small sport size
2 mirrors is not stable
for small spot size
α
2d 4M has astigmatism
3D (or twisted)
4M ring cavity
by T.Omori

## Slide 22: 2010 Summer: French cavity Installation
by T.Omori

## Slide 23
10
11
12
01
02
03
04
05
06
07
08
09
10
11
12
01
02
03
04
05
06
07
10/25 :
 observed
12/08 :
 observed
03/11 :
earthquake
07/20 :
Laser Failure
10/20
ATF Recovering



21012.12.10
MightyLaser
Main Events Summary
2010
2011
2012
06/03 :
Fibre amp
damage


Setup on
Standby Mode
Sapphire Mirrors
Finesse 30000
Coupling 15% on air
3% under Vacuum
Equipments sent to Orsay
Locking more stable using Frequency Shifter
60% coupling
Laser Mode-lock unstable
New laser ?
New design required for
Fibre amplifier
Gamma observed
08
09
10
11
04/11
03/23
05/22
12/17
12/26
New Mirrors Finesse 3000 installed
Coupling 59% on Air
20% on vacuum
CELIA
Eric CORMIER
MENLO
Laser Orange
decision
12
Origami Laser
sent to Orsay
New MENLO Laser + Fibre Amplifier under tests at LAL
11/29
Request to Terunuma-san
Challenge
F=30000
Problem: Coupling Decrease in Vac.
CEP?
g-ray
observation
by T.Omori

## Slide 24: French Cavity aiming very high finesse. Issue: Lost stacking when goes vacuum. Carrier Envelope Phase (CEP)
Carrier
Envelope
Cure is on going at LAL
-> Cavity back to KEK this summer
by T.Omori

## Slide 25: 2011 Autumn: KEK-Hiroshima 4M Cavity Installation
by T.Omori

## Slide 26: Stable resonance with small spot size
Stable resonance by new feedback sys. (analog)
2.6kW average power w/ 1.4% fluctuation
laser waist size at IP(σ)=13um (vertical scan)
Finesse 4040+-110 (Enhance = 1200)
38W
4pm
(1.4%)
stack power [W]
13um (V)
2.6kW stacking
by T.Omori

## Slide 27: g-ray Generation / electron
ATF 2.16MHz
~2.6×108/sec
5bunches/train
2970±20 MeV
⇒ ~128gs/trainのガンマ線に相当
e-
laser
g
5.6ns
Eg[MeV]
by T.Omori

## Slide 28: Summary
Optical Cavity at the ATF is in progress for Polarized positron source for the ILC
  Good collaboration between France – Japan team
    information / technology exchange
R&D of 4 mirror ring cavities are in progress
  Sophisticated mechanism aminig very high laser power enhancement ,,, French team
  Relatively simple but new cavity control practical experience w/ the ATF ,,, Japanese team
Next Step (2013 and ,,,)
  France : Laser with CEP control (ongoing@LAL)
    Summer: Re Install whole system
  Japan: Finesse 48,000 (16600 enhancement)
  Japan: Digital Feedback (ongoing)
by T.Omori

## Slide 29: Application for the DR Laser Wire
2-mirror  4-mirror
Improve the reliability of system
Pulsed laser increase intensity faster measurement

## Slide 30: Design Of Mirror holders & Mirror Alignment scheme
Injection
Reflection
Transmission
Transmission
Long PZT Actuator
Short PZT Actuator
Concave
Concave
Plane
Cavity length is 102.8 mm only , and side by side mirror distance is kept to 29.2 mm
by R.Arpit, ATF2 project meeting

## Slide 31: Parameters of Compact 4 mirror laser wire in comparison to old 2 mirror laser wirer system
Parameter | 2 mirror Horizontal wire | 2 mirror Vertical wire | 4 mirror laser wire
Reflectivity of mirrors | 99.1%, 99.9% | 99.8%, 99.9% | 99.9%,99.99%,99.99%,99.99%
Mirror curvature | 20 mm | 20 mm | 101.81 mm
Finesse (measured) | 620 | 1700 | 4126.6
Power gain | 660 | 1300 | 2000
Waist size ( value) | 5.7 um | 14.7 um | (6 um,14 um)
Wavelength | 532nm (CW green) | 532 nm (CW green) | 532 nm (Pulsed green, 714 M Hz)
1. Four mirror resonator reduces the sensitivity to the misalignment of mirror compared to two mirror resonator, thus more stable.
2. CW laser wire system takes more time in scanning of electron beam compare to Pulsed laser. Pulsed Compact resonator will take less than one minute to scan electron beam profile
3. With pulsed laser wire, more efficient laser-beam collision can be realized
4. High Finesse and high enhancement factor is achieved in 4 mirror pulsed laser wire system in comparison to 2 mirror laser wire system
MERITS
by R.Arpit, ATF2 project meeting

## Slide 32: Preparation of Pulsed Green Laser oscillator
714 M Hz IR LASER OSCILLATOR
Yb doped
Fiber
Pre Amplifier
PCF based
Main Amplifier
SHG using Non Linear Crystal
4 Mirror
Compact Cavity
700 m W
W
20 W
W
Pulsed green
We are now working on development of fiber amplifier in order to obtain high power green laser beam.
We achieved 2 W IR power after Yb doped fiber amplifier.
Conversion efficiency of Non linear crystal for 2nd harmonics generation is 15 -20 %, so we have to achieve good amount of IR pulsed power after Photonic crystal fiber based main amplifier system.
Fiber coupler
2nd harmonics Generation
by R.Arpit, ATF2 project meeting

## Slide 33: New Laserwire in ATF DR
It was installed in January 2013.
Unfortunately the cavity was out of the range for the possible DR frequency changes.
Removed from DR in May 2013.
Re-optimization of cavity and re-installation wil be done in this summer
The improvement of the laser amplifier is also ongoing.
Hope to run in following autumn runs.

## Slide 34: Summary
Emittance of the ATF DR is typically 10 pm recently.
  It is tuned within a shift in every startup of ATF.
  No more tuning had not been done in recent years because of the ATF2 priority.
Small emittance study toward 2 pm should be resumed.
Cavity Compton studies are also resumed.
Others
  TBT by Yevs (next talk)
  CLIC issues will be planned but mostly at EXT/ATF2.

## Slide 35: Schedule? of ATF-DR since 2013
JFY
2013
2014
ATF2(50%)
(10pm or less)
4
7
10
1
4
7
10
1
1~2pm
Cavity Comptons
DR-LW
installation
Return to LAL?
Laser Re-installation
LAL
Hiroshima/KEK
Others (50%)
CLIC etc.?