## Slide 1: FPCCD SOFTWARE
Weekly Software meeting 9/28
Tohoku University M1 Tatsuya Mori
Notes: So, I’m gonna talk about FPCCD SOFTWARE.

## Slide 2: FPCCD Vertex Detector
FPCCD Vertex Detector may give the followings
Good IPResolution for flavor tagging.
a=5um
b=10um*GeV
Notes: First of all, let me refer to summary about FPCCD Vertex Detector. FPCCD Vertex Detector may come true the followings. 1st is Good Impact Parameter Resolution for flavor tagging.
In this presentation, I concentrate on Impact Parameter Resolution Study.

## Slide 3: Performance Study
Especially, now I’m studying
the IPResolution Performance of FPCCD.
Which pixel size config. is the best for physics
and electronics performance?
smaller pixel size  better physics
performance but worse electronics performance.
If BG is taken into account, does IPResolution
keep the required level?
For now, I’m tackling the former question.
Notes: Next, let’s go to performance study. Especislly, now I’m studying the IPResolution Performance of FPCCD and handling with the following two question. Which pixel size config. Is the Best for physics and electronics performance? Of course the smaller pixel size becomes, the better physics performance becomes, but
the worse electronics performance. The other is, ”If BG is taken into account, does IPResolution keep the required level?”. For now, I’m tackling the former
Question.

## Slide 4: My Status
Until yesterday, I have not resolved the following.
Why is the σ of “d0 pull distribution”
so away from 1 ??
Finally, Dr.Stieve updated tracking algorithm yesterday.
The σ gets equal to almost 1.
Notes: Until yesterday, I have not resolved the following. “Why is the σ of “d0 pull distribution so away from 1??”. Finally, Dr.Stieve updated tracking algorithm
yesterday. The σ gets equal to almost 1. From now, let me show my process to the result.

## Slide 5: TrackerHit Resolution
Spatial Resolution of FPCCD Cluster was determined by simulating single muon+ events without Energy Loss and Multiple Scattering.
Resolution was assigned depending on the size of cluster
for pixel size = 1, σ = 1.02um
> 1, σ = from 0.57um to 0.59um
Notes: So, Spatial Resolution of FPCCD Cluster was determined by simulating single muon+ events without Energy loss and multiple scattering.
Resolution was assigned depending on the size of cluster for pixel size =1, σ=1.02um. And for pixel size > 1,σ=from 0.57um to 0.59um.
So Next Slide is the more detailed condition and result.

## Slide 6: Pull Distribution Without dE and MS
Condition:
muon+, θ=20,30,85deg,|P|= from 1 to 200 GeV
Spatial Resolution Config. is preceeding chapter’s
one.
Result:
σ’s ~ 1. Each shift from 1 is less than 10%.
Notes: I used the following event. Muon+, theta = 20 ,30 ,and 85deg, Absolute Momentum equals from 1 to 200GeV,
And of course Spatial Resolution Config. Is preceeding chapter’s one.
Now then, the Result is that σ’s almost equal 1. Each shift from 1 is less than 10%.

## Slide 7: Pull Distribution with dE and MS
Next, I turned dE and MS “On”.
Condition:
same except for dE and MS
Result:
σ’s ~1. Almost each shift from 1
is less than 10%, but some σ’s ~1.1
Notes: I got a good result without Energy Deposite and Multiple Scattering, so next I turned Energy Deposite and Multiple Scattering “On”.
The condition is of course same except for Energy Deposite and Multiple Scattering.
The Result is that σ’s are almost 1. Almost each shift from 1 is less than 10%, but some σ’s are almost 1.1

## Slide 8: Part of efforts
This shows d0 pull distribution of “mu+, θ=85deg, |P|~200GeV” event
and says the σ = 1.034. This means that the tracking does almost best performance.
Notes: This is part of efforts. This shows d0 pull distribution of “mu+, theta=85deg, Absolute momentum = 200GeV” event and says the σ=1.034. This means that the
Tracking does almost best performance.

## Slide 9: From Here
I am trying to the followings.
Find the two configuration of pixel size (“all5um”, “inner two layer:5um outer 4 layer:10um”)for physics performance.
Try IPReso estimation with e+e- pair background(condition:1TeV,1train).
The former may be easy, so I’ll show you this result next week.
But the latter may be difficult for the computer capability.
I try my best.
Notes: Next, let me explain “the plan from here”. I am trying to the followings. 1st is to find the two configuration of pixel size, more detailed speaking, “all5um”,”inner two layer:5um outer 4 layer:10um” for physics performance.
2nd is to try Ipresolution estimation with e+e- pair background in condition of 1TeV, 1train. The former may be easy, so I’ll show you this result next week.
But the latter may be difficult for the computer capability.
I try my best.

## Slide 10: Thank you very much.