Calicoes
Calice OnlinE System
Frédéric Magniette
ANR-2010-BLANC-0429-01

---
The Needs
- Acquisition Chain : developpement from scratch
- Control-Command Chain (replacement for buggy Liblda)
- Human-Machine interfaces
  - For DAQ debugging
  - For data acquisition
- Properties
  - Calice compatible (DIF-LDA-Ethernet Calice format – can use different Omega Rocs)
  - Highly reliable
  - Strong evolutivity (developpement phase)

---
Design Concepts
- Internal Modularity
  - Functional blocks with easy communication channels (on the Unix model)
  - Every block is making few but making it fast and good
  - Easy evolutivity
- Parallelism
  - Massively multi-threads approach
  - Pipelined treatments
  - Low-latency code (no barrier)
- External Genericity
  - Connected to the outside with open formats (xml, tcp sockets)

---
Low level Transfer
- Standard Ethernet driver (e1000)
- Low-level socket (SOCK_RAW)
- Limited in rate by the SOCK_RAW implementation
- Projects to speed up: integrating UDP in GDCC

---
LDA/DIF Readout uncap
- One of the two specific parts of the system (dependant of the DIF Firmware version)
- Functionalities : uncapping packets, DIF tagging, loss control, integrity control
- Implemented in an external library for genericity and maintainability

---
The distribution bus
- Split data into beams (by dif)
- Offer the maximum flexibility in data treatment
  - Offline through files
  - Remote online through sockets
  - Subsampling sockets for slow online analysis programs
  - High performance online through Shared Memory

---
Signal Uncap
- The second specific block of the system (dependant on the roc chip version)
- Actually adapted for skiroc, can be ported easily to spiroc or any other Omega chip
- Uncaps the skiroc data to produce isolated physical events
- Output a plain text format (without loss of information)

---
The Control-Command chain
- All devices has their module in the control-command
- Based on the pyrame framework (LLR)
- All accessible through the pyrame GUI

---
The actual ECAL hardware
Hardware	Comm Bus
Pulse generator	Ethernet LXI/TCP
High Voltage power supply	RS232
Low Voltage power supplies	GPIB
LDA Reset device	Arduino
CCC	RS232/USB
LDA/DIF	Ethernet

---
The Big Picture

---
The detector control command
- Detector Abstraction Layer
- Allows only the global detector transitions with integrity checks
- Commands all the other blocks
- Based on a state machine

---
Unified XML configuration format
Parser sends « init » and « config » orders to every modules

---
Pycaldaq : a scripting interface
- Embedded Python scripts to pilot the whole detector
- Programmed or interractive sessions
- Very useful for calibration
- Used for a global calibration during summer 2012 : testing 22000 configurations without any human help (3 weeks)
import caldaq
def acq_run():
    caldaq.start_acq()
    caldaq.start_spill()
    caldaq.start_trigger()
    time.sleep(15)
    caldaq.stop_trigger()
    caldaq.stop_spill()
    caldaq.stop_acq()
caldaq.flush_files("trash")
for trig in range(150,401,15):
    caldaq.set_gtrigger(trig)
    acq_run()
    caldaq.flush_files("calib_trig%d" % (trig))

---
Online Monitoring
- Ongoing work
- Integrating online data in a circular buffer
- Allows to display real-time physics histograms and curves
- Soon available for Root and R

---
Hitcam
Graphical visualisation of hits
Online visualisation tool
Adjustable gain
Can be used offline : video generation
Useful for :
beam spotting
online visual data control
beam supervision

---
Results
- Good data rate : perfect for 10 Hz Spill
- Very good reliability
  - 15 days of beamtest at DESY without bugs
  - 3 weeks of calibration without a problem
- Easy to use
  - Multiples graphical interfaces
  - Programming interface
- Good evolutivity
  - Any block can be improved and modified easily by anybody

---
 Perspectives ?
Increasing the flow rate by specific modification : plan to use UDP in GDCC
Online event building : Eudaq / AIDA
Integrating the system in a global SCADA system (XDAQ / AIDA)

---
The Framework connection
- Not implemented now
- Connection to XDAQ for Lyon SDHCAL compatibility
- Can be easily compatible with any other framework Doocs, Tango...
- High level integration : replacing the detector GUI (the state machine steering)

---
Output Perspectives

---
Thank you for your attention, any questions ?