## Slide 1: TMD2 amplifier test
N. Blaskovic

## Slide 2: Introduction
Kicker K1 scans in October are anomalous at a K1 DAC setting of 1000 counts:
N. Blaskovic
position at P3 (Δ/Σ units)
K1 DAC setting (counts)

## Slide 3: TMD2 amplifier test
The performance of amplifier TMD2 (at K1 in October) was tested in the lab using last week’s set-up.
The waveforms from the monitor of Colin’s 8-to-2 box were recorded for a range of DAC settings.
The waveforms obtained using TMD2 were compared to those using TMD1.
N. Blaskovic

## Slide 4
N. Blaskovic
TMD1
TMD2
DAC out = 4000
DAC out = -4000

## Slide 5
N. Blaskovic
TMD1
TMD2
DAC out = 2000
DAC out = -2000

## Slide 6
N. Blaskovic
TMD1
TMD2
DAC out = 1000
DAC out = -1000

## Slide 7
N. Blaskovic
TMD1
TMD2
DAC out = 500
DAC out = -500

## Slide 8
N. Blaskovic
TMD1
TMD2
DAC out = 250
DAC out = -250

## Slide 9: Observations
Waveforms are virtually identical for both TMD1 and TMD2.
The amplifiers seem to saturate at DAC settings ≥ 2000, but not at settings ≤ 1000.
The anomalous behaviour observed in the K1 kicker scans in October appears not to be caused by TMD2 malfunction nor by amplifier saturation.
N. Blaskovic