## Slide 1: Summary of DAC stability tests
Glenn, Neven, Jack, Doug
20/12/2012

## Slide 2: Set-up
FONT5 board
Fast clock
Dig in 1
Dig in 2
DAC 1
DAC 2
Generator
FONT4
FONT4
ADC 1
ADC 2
Loop DAC 1 and 2 back into ADC 1 and 2.
Log DAC output over full DAC range (-4096 to 4095), with 65 triggers per DAC setting
Look at FBFW_v5 firmware first (used in Oct).

## Slide 3
Use sample number 100
Different coloured traces correspond to different triggers

## Slide 4
Minimum and maximum ADCs over all triggers at the given DAC setting

## Slide 5
Minimum and maximum ADCs over all triggers at the given DAC setting
Gradient =
-0.61 ADC counts/DAC count

## Slide 6
Zoom into DAC1 scan
Minimum and maximum ADCs over all triggers at the given DAC setting

## Slide 7
1 point per DAC setting
(different colours represent different DAC settings)

## Slide 9: Comparison with different firmware
For versions of FW other than FBFW_v5 (currently burnt on PROM) only very limited tests were made at DAC codes around 1000-1024 and 2047.
May be useful to do more extensive tests of certain versions to verify working correctly or understand previous behaviour, eg with phase compensating FBFW.

## Slide 10
Bitstream name | Firmware base version | Remarks/modifications | Observations
FBFW_v5.bit | FBFW_v5 | Version on PROM (vanilla version) | Glitching/incorrect values observed
DACtests_reference_181212.bit | FBFW_v5 | Reference bitstream before changes (vanilla version) | Glitching etc as above
DACtests_DefaultDAC1clk_NOIOBregs.bit | FBFW_v5 | DAC1 clock output changed to 12mA drive, slow slew rate | OK, no glitching observed
FBFW_v4_DACtest.bit | FBFW_v4 | Final registers in paths for DAC clock and data packed into IOBs (both DACs) | OK, no glitching observed
font5_9chan_FBFW_v4.bit | FBFW_v4 | Vanilla | OK, no glitching observed
font5_phasecompfb_bigtrigout.bit | Doug’s PCFBFW |  | Glitching/incorrect values observed (1000-1023 OK, >1024 bad!)
font5_couple_duptrig_2-798.bit | Ben’s FBFW | As used April 2010 and beyond | OK, no glitching observed