## Slide 1: Automatic tile/SiPM placement on the HBU boards
21.3.12 - Calice Collaboration Meeting
DESY Hamburg
Phi Chau
Bruno Bauss, Volker Büscher, Reinhold Degele, Karl Heinz Geib, Sascha Krause, Yong Liu, Lucia Masetti, Uli Schäfer, Rouven Spreckels, Stefan Tapprogge, Rainer Wanke, André Welker

## Slide 2: Need for an automatic placement
Hadron tests (2014)
  60 HBU boards  8.500 tiles with SiPM have to be placed on HBU boards
Full prototype (2015)
  160 HBU boards  23.000 tiles with SiPM have to be placed on HBU boards
AHCAL (final design)
  About 8.000.000 tiles have to be placed on HBU boards
Notes: Format noch korrigieren

## Slide 3: Need for an automatic placement
That means with an effort of 20 seconds for a manual placement per tile you will need for
One HBU board: ~ 1 h
Hadron tests (2014): ~ 1 week
Full prototype (2015): ~ 1 month
AHCAL (final design): ~ 15 years
Notes: Format noch korrigieren

## Slide 4: Need for an automatic placement
For this number of tiles an automatic placement is needed
 pick-and-place machine
Notes: Video Hinzufügen

## Slide 5: Present design
Possible drawback of automatic placement to design Alignment and SiPM pins need to be considered
Alignment pins
SiPM pins

## Slide 6: Alignment pins
Automatic pressing of tiles in the alignment pin connectors of HBU board is problematic. Possible problems:
  Force has to be applied to connect alignment pins with the connectors
  Other possible problems:
    The alignment pins may have too much space -> tiles aren‘t fixed
    They may not fit

## Slide 7: Alignment pins
Idea
  Fixation of tiles without alignment pins by glueing on reflector foil/HBU board

## Slide 8: Alignment pins
Present design:
Alignment pins
Reflector foil
HBU
Pin (SiPM)
SiPM
Absorption layer
Possible new design:
 Tile without alignment pins
 Tile fixation with optical glue
Glue points

## Slide 9: Alignment pins
Possible influence of glueing to optical properties?
 Test measurements
with BC-600 (Bicron)

## Slide 10: Measurement Set-up
Pin
Black box
Acrylic glass
tile
Reflector foil
Idea:
Cosmic ray test
SiPM

## Slide 11: Measurement Set-up
Case
Pin
Acrylic glass
SiPM
Black box
Trigger scintillator

## Slide 12: Measurement Set-up
Trigger scintillator
Light guide + PMT
Scope + signal amplifier
Case
Pin
Black box

## Slide 13: Measurement Set-up

## Slide 14: Measurement of optical properties
Four different measurements
  Measurement according to original concept
  Direct contact beween tile and reflector foil without alignment pins (without glue)
  Measurement with one or two glue points on tile (without alignment pins)
  Tests with glue on whole surface of tile (without alignment pins)

## Slide 15: Test configuration
Replica tile with
alignment pins
Replica tile without
alignment pins
Original tile with SiPM
Notes: Bearbeiten!!

## Slide 16: Test configuration
Configuration of test tiles
  Borders of test tiles are painted with white reflecting color
Is the painting comparable?
  Test original ITEP tile and CPTA SiPM
  Then remove etched borders und paint white reflecting color on
Notes: Bearbeiten!!

## Slide 17: SiPM pins
To guarantee a reliable automatic placement
  Robust and linear pins of the SiPM are needed

## Slide 18: SiPM pins
Exact positions in the space of tolerances are absolutely necessary for automatic placement
SiPMs have to fulfill definit specifications
Example: SiPM pins with Hamamatsu MPPC

## Slide 19: SiPM pins
Exact positions in the space of tolerances are absolutely necessary for automatic placement
3.0 mm
0.55
0.55
Pins
1.1 ± 0.2
Example: Hamamatsu
MPPC S10362-11-xxxP
Front view
Back view
Side view

## Slide 20: General schematic of pick-and-place machine
Assembly line transports HBU boards
1. Glue points on reflector foil/HBU board
2. tiles are set on foil/HBU
4. Deposit station – glue can dry
5. Test of functionality for tiles and SiPMs with LEDs on HBU
3. SiPM pins are soldered on HBU
We will obtain a test machine for the automatic placement
 Price for a used machine: 10.000 – 20.000 €

## Slide 21: Forecast
April SMT Hybrid packaging fair in Nürnberg
http://www.mesago.de/de/SMT/Fuer_Besucher/Willkommen/index.htm

## Slide 22: Thank you for your attention!