Understanding of SKIROC performance
T. Frisson (LAL)
On behalf of the SiW ECAL team
Special thanks to the electronic and DAQ experts:
Stéphane Callier, Rémi Cornat and Frédéric Magniette
And to:
Romain De Abreu (Internship student)

---
The road to the technological prototype
Intermediate step:
U structure (single detection layer per slab)
Si wafer:
9x9 cm2 – Thickness = 320 m
pixel size: 5x5 mm2 :lateral granularity = 4 x better than physics prototype
4 SKIROCs per slab (1⁄4 final design)
4 x 64 channels = 256 channels/slab
Spring 2012 : 1 layer
Summer 2012 : 6 layers
Winter 2013 : 10 layers (see Vladik and Yuji talks)
 First test in beam
 Benchmark to go further
DESY : e- (1 - 5 GeV)

---
Front end electronics: SKIROC
SKIROC (Silicon Kalorimeter Integrated Read Out Chip)
SiGe 0.35μm AMS
7.5 mm x 8.7 mm
High integration level (variable gain charge amp, 12-bit ADC, digital logic)
64 channels
Large dynamic range (~2500 MIPS), low noise (0.4 fC – 10 pC)
Auto-trigger at ½ MIP
Low Power: (25µW/ch) power pulsing
On chip zero suppression
Trigger delay
Preamplifier (adjustable gain)
Internal trigger
(self-triggering capability)

---
Calibration of SKIROC
Establishment of calibration procedure for a large number of cells
Trigger threshold
- depends on the gain
  - Individual channel threshold adjustment
Range too small → R to increase current in the 4-bits DAC adjustment
Trigger delay
- depends on the trigger threshold
OK on test bench → to be tested in beam (need new calibration procedure)

---
BCID+1 effect
Retriggering of the ASIC without hit
Understood (see Nathalie and Stéphane talks)
~13% of the events (for Tslowclock = 2.5 MHz):
Calculated: Tslowclock/Tnor64
Measured with test bench and test beam
Easy to cut off-line

---
Plane events
PA is referenced to the analog power supply level
Instabilities of power supply level → fake events
VDD_delay/sca plugged on analog power supply → increase instabilities of power supply level
Analog power supply common to the 4 ASIC
Self-sustained → sometimes filled all the 15 ASIC memories
Highly dependant of the number of ASIC with hits, dependant of the number of triggered channels

---
Plane events
Proposed patchs
Bigger capacitance close to the ASIC to stabilize power supply
2 power supply lines: Modify VDD_delay/sca
routing to protect PA power supply (pin-clipping)
First tests on test bench:
Injection in the 4 ASICs
Reduction of the plane events: ~80% → ~10% (both capa and pin-clipping)
2 slabs modified to be tested during the last test beam
1 slab with big capa
1 slab with pin-clipping
→ see Vladik and Yuji talks

---
PCB
PCB is critical →	Goal :1 mm thick, 8 layers, 1% flatness , ASICs bounded into
FEV COB
- Available since december 2012 (Boards from Exception and Protecno)
- First board for 16 ASICs (btw. Several proposal to assure planarity exist)
- Now equipped with 8 SKIROC ASICs (Boncing by CERN) → Needs testing
- However, bonding was not straightfoward, thin bonding pads can be improved

---
PCB
PCB is critical →	Goal :1 mm thick, 8 layers, 1% flatness , ASICs bounded into
Current: FEV8 Chip in package, 1.4 mm thick
Line density in PCB  routing is crucial
Noise
Cross talk (Digital / readout channels  readout channels)
M1
M2
M3
M4

---
Switched off channels
Noisy channels + no individual channel adjustement → channels linked to several pixels
Cross talk with digital lines (valEvt, startAcq, clocks, injection line):
e.g.: ValEvt line close to M4 35-37: signal > 1 MIP
BCID distribution in channel 35 (M4)
Test bench data
Synchronized with valEvt signal (13 BCID)

---
Noise studies
Noise  Line length
Already improved for the 16 ASIC version of the PCB

---
Coherent noise (general behavior)
Development of algorithm to identify coherent noise (continuation of Roman studies)
e.g. : chip M1
We extract incoherent noise + 2 sources of coherent noise:
Incoherent noise
Channels with switched off PA
Coherent noises
Common to all channels:
Due to the ramp? (Omega expects ~0.5 ADC)
Common to channels with switched on PA:
Due to PA?
To be clearly identified and reduced (if possible): under discussion with experts (Omega)

---
Correlation studies
Chip M2 (all layers):
Another coherent noise source 2 highly correlated channels
No clear idea of the source
Channel 54
Channel 61
We don't see an effect on MIP distribution
Channel 54
Channel 59

---
Correlation studies
Chip M1 (only in slab3)	:
  - Another coherent noise source 2 highly anti-correlated channels
  - No clear idea of the source of this behavior
Channel 32
Channel 33
We don't see an effect on MIP distribution.
We should check the S/N ration @ low gain
Channel 32
Channel 33

---
SKIROC results as a function of the gain
Gain  1/Cf
Saturation of the MIP position → bad holdscan calibration?

---
Fit of the noise as a function of the gain
Slope of the linear fit for all channels / ASICs / Slabs
Constant parameter of the linear fit for all channels / ASICs / Slabs

---
Event display
3 e- (3 GeV, no tungsten)
2 e- (3 GeV, no tungsten)
1 e- (5 GeV)
5 W plates between layers
1 cosmic + 1 e-
(3 GeV, no tungsten)

---
Summary
2012 test beams have provided useful data.
Mainly thanks to the Frédéric's work on DAQ software
Major step forward in the understanding of the detector
BCID+1
Plane events
Switched off channels due to crosstalk with digital line or readout channels
Noise structure
To be continued with power pulsing studies
See Nathalie, Vladik and Yuji talks
R&D in progress… first test beam shows promising results