## Slide 1: January ATF Plans
1/8
Mikey Davis
14 January 2013

## Slide 2: Introduction
I’ve recapped what we did last time
Based this plan on the last one
Have come up with a plan for the first shift
Then all up in the air (again)
2/8
Mikey Davis
14 January 2013

## Slide 3: October Trip
Last time because we didn’t have variable attenuators the first week was a bit of blow out
The second week went better with the last shift being the best
We has two major problems
  We didn’t centre the beam well
  We don’t have good calibrations
3/8
Mikey Davis
14 January 2013

## Slide 4: Things we Learnt
Analysing data it was clear we made a couple of errors
  It is easier to analyse data in single bunch with EPICS
    As such I think we should record as many runs as possible to have lots of cross checks
  Sometimes we cut off (or at least are suspicious) the beginning of the trace
    I think it’s probably better missing the end of the trace and seeing the beginning
    Open to discussion…
4/8
Mikey Davis
14 January 2013

## Slide 5: Shift 1 Plan (Single Bunch)
LO Phase Scan
Upstream Calibration (mover scan)
Centre beam in IP BPMs
  V IMPORTANT !!!
IPBM Calibration
  Go from -100 to 100 (microns) around centre to see sat.
  Do another finer scan around zero
  Record EPICS and compare it, jitters should be the same
  Do this with a number of different attenuation settings, at least 20 dB and 30 dB
Move IP to IPB (IP waist scan)
  Compare it with EPICS
  If it isn’t the same as EPICS then stop there and try and make it the same
5/8
Mikey Davis
14 January 2013

## Slide 6: Shift 1 Plan (Single Bunch)
Do a jitter run (resolution, jitter at FONT and IP, Correlation)
Upstream kicker scan
  This can be compared with EPICs again for a final cross check
Downstream kicker scan
  Not convinced we should bother with this
  Would be worth trying but if we do I think we should continue until it works
6/8
Mikey Davis
14 January 2013

## Slide 7: Shift 1 Plan (Two Bunch)
  Jitter Run (measure 2 bunch resolution and correlation)
  Upstream feedback (several runs, see results at IP)
    From the last trip this is about where we got to in a single shift
    I think it’s worth doing this with at least 2 attenuation settings
  Single loop feedforward at notional gain
    Would be nice to try, depends on kicker scan
  Single loop gain scans
    Optimistic
  Coupled loop feedforward at optimal gain
7/8
Mikey Davis
14 January 2013

## Slide 8: Feedforward Comments
  Obviously this didn’t work last time, why is this?
      The DAQ was incorrectly setup
      Something in the setup we broken (exonerated?)
      The cable was broken (exonerated?)
  If we decide to go for this I think we should start with it at the beginning of a shift
  The first step is a kicker scan, I think even achieving this would be a triumph
8/8
Mikey Davis
14 January 2013