## Slide 1: Summery of the power coupler session at the LCWS13 workshop
E. Kako
W.-D. Möller
H. Hayano
A. Yamamoto
All members of SCRF WG
November 14, 2013

## Slide 2: ILC specification
Power requirements
  We recommend to match the coupler to 30 MV/m for reduced filling time and smaler Qext range
  Max coupler power at operation 450 kW (for 8.8 mA, 10Hz, Eacc=31.5 MV/m ±20%)
  RF processing to at least four times max input power ~ 1.8 MW up to 500 us at test stand TW
  Surface field not a problem for both designs, i.e. 40mm and 60mm are both ok
  Should check flattop regulation at 25 MV/m and Qext ~ 1e7 (LFD)
  TW testing on test stand up to 1.8MW has to be done for both: TTF3 and STF2
Q-ext
  Variable coupling is needed, remote operation
  QL tuning range: 2-7x106 is needed, but we recommend 1-10 x 106
  1-10∙106 is achieved with TTF3
  STF2 has to be improved
Antenna alignment:
  Design should be +-2mm
  For TTF3 coupler the most sensitive parameter is a horizontal antenna shift/tilt. 3mm shift change QL by ~20%. Vertical tolerances are relaxed.
  For STF-2 coupler this is not issue, mechanical design guarantee small shift.
  TTF3 has to be improved

## Slide 3
Cryogenic loss:
  Coupler contribution to cryogenic losses at 2K is ~5%. = not critical.
  Major contribution from coupler is 70K
Conditioning time
  Both designs are ok
  The nominal conditioning time of < 50h is achieved/demonstrated.
Multipacting
  DESY and SLAC simulations, tests and operation show no problem with TTF3
  STF2 will be simulated, tests show no problem
One vs. two windows
  Many single window coupler are successful under operation
  The single window would need to seal-off the cavity before the cavity-string installation into the cryomodule.
  Single window coupler for ILC would need complete new development and test program of coupler (and module)
  But it could be a significant cost saving
Compatibility
  Cavity and attached parts (power coupler, tuner, HOM coupler, feedthroughs, He vessel, thermal connections, magnetic shield…) are tuned/balanced, it is not easy to exchange only parts of this composition
  STF2 coupler design does not fit in the compatibility requirements of the TDR (40mm cavity coupler flange)

## Slide 4
Cost
  CPI: STF2 price is 1.9 higher
  Toshiba: STF2 slightly lower price
  RI: about same price
  Industrial study of STF2 for design optimization and cost reduction is recommended
  The TTF3 coupler mass fabrication has to be investigated
Recommendation:
STF2 coupler has to demonstrate stable long time (>6 month) beam operation in a CM (TTF3 coupler has a long history in FLASH)
The ILC management recommend an adapted STF2 design with 40mm cavity flange. In this case more development steps have to follow in order to realize the compatible design. The new design has to be proven with beam operation.
The concept of plug compatibility has to be further developed in view of a spare part concept. We recommend spare modules, not individual parts.
An industrial study of mass production for both designs is recommended
Industrial study of STF2 for design optimization and cost reduction is recommended

## Slide 5
 | ILC Spec | TTF3 / XFEL | STF-2
Frequency | 1.3 GHz | 1.3 GHz | 1.3 GHz
Operating pulsed RF power | 450 | 100 .. 600 kW | 450
Operating RF pulse length / rep.rate | 1.65 ms / 5 Hz | 1.3 ms / 10 Hz | 1.5 ms / 5 Hz
Max. RF conditioning power (20 .. 500µs) | 1.8 MW | 1 MW | 1.2 MW
Max average power | 3.7 kW | 4.5 kW (tested and calculated limit) | 3.0 kW (not the limit, but tested)
copper coating inner/outer conductor | nn | 30 µm / 10 µm | 25 µm / 10 µm
copper coating RRR | nn | 30 .. 60 | 10-20
Max. cryogenic losses at 2K / 4.2K / 70K dynamic + static | need to check | 0.06 W / 0.5 W / 8 W static+dynamic | 0.06W / 0.8 W / 9 W simulated static
window | 2 windows | 2 cylindrical | 2 disc
Warm coax |  | 60 mm, 50 Ohm | 82 mm, 50 Ohm
Cold coax |  | 40 mm, 75 Ohm | 60 mm, 43 Ohm
Qext range | 1.0 – 10 x10^6 | 1.0 – 15×106 | 2.0 – 6.0×106
bias | yes | yes | no
lateral movement | 5mm (including fabr. Error) | ± 15mm | ± 5mm
max surface field (inner cond cold part) @500kW TW |  | 1MV/m | 0.5MV/m
max voltage, (inner cond cold part) @500kW TW |  | 14kV | 7.5kV
MP levels |  | 150 kW, 250 kW, 450 kW | 
Insertion loss |  | less 0.1 dB | 
ILC RF Power Coupler design criteria comparison