First layers of the Si-W ECAL technological prototype in test beam
Thibault Frisson, Jérémy Rouëné

---
The road to the Si-W ECAL technological prototype
Intermediate step: Conservative layer design for beam tests
First test in beam
Benchmark to go further
Single detection layer per slab (U structure)
Si wafer:
9x9 cm2 – Thickness = 320 mm
pixel size: 5x5 mm2 :lateral granularity = 4 x better than physics prototype
SKIROC2 ASICs
4 ASICs per slab (1⁄4 final design) - conservative design (chip in package)
4 SKIROCs x 64 channels = 256 channels/slab

---
Beam tests @DESY - summary
Summer 2012
- 6 layers
- 1 LDA
- DAQ soft v0
Winter 2013
- 8 layers
- 2 LDA
- DAQ soft v1
Summer 2013
- 6 layers
- 2 GDCC
- DAQ soft v1
- Debugging electronics (SKIROC2, PCB...)
- Establishment of calibration procedures
- Measure of S/N
- Power Pulsing
- Power Pulsing
- Showers

---
Beam tests @DESY - summary
Summer 2012
- 6 layers
- 1 LDA
- DAQ soft v0
Winter 2013
- 8 layers
- 2 LDA
- DAQ soft v1
Summer 2013
- 6 layers
- 2 GDCC
- DAQ soft v1
- Debugging electronics (SKIROC2, PCB...)
- Establishment of calibration procedures
- Measure of S/N
- Power Pulsing
Main results shown by Nathalie and Yuji @ previous CALICE meeting
- Power Pulsing
- Showers

---
Beam tests @DESY - summary
Summer 2012
Summer 2013
- Debugging electronics (SKIROC2, PCB...)
plane events
BCID+1
Noise
- Establishment of calibration procedures
Trigger Threshold calib ~ OK
Trigger delay calib ~ OK
Energy calibration
- MIPs and showers
- no power pulsing
- Position scan
- Several gains (main Cf = 1,2pF)
- Power cycling, GDCC
heavy debugging (5 days) → quick and dirty procedure to switch on the setup
Blind detector:
No trigger threshold calibration
No trigger delay calibration
→ Thanks to Franck, Frédéric, JB, Jérémy, Mickael, Rémi
- MIPs and showers
- power pulsing mode (PP) and no power pulsing mode (CC)
- Position scan
- 1 gain (Cf = 6pF)

---
Software / Simulation
Same tools as previous TB (few improvements)
MC used same data structure with additional information
Raw Data
(1 file per layer)
Geant4
Pedestals
Pedestals
ROOT files
(1 file per layer)
ROOT files
(1 file per layer)
Energy calibration
Energy calibration
Merge & Event reconstruction
Merge & Event reconstruction
Detection efficiency
Event display
Analysis
Event display
Analysis

---
Data quality - Plane events (Summer 2013)
Instabilities of power supply level → fake events
All layers with additional capacitors to stabilize power supply
Ratio (plane events) / (good events) in Summer 2013
MIPs:
CC: ~20-40% (winter TB modified slabs: ~10%)
PP: ~60-200 %
(For BCID+1: ~20-40%)
* difficult to compare winter TB and summer TB: not the same gain, trigger threshold...
* As expected, capa reduce frequency of plane events BUT also the number of hits in a plane event ==> difficult to separate plane events and good events

---
Data quality - BCID synchronization (Summer 2013)
2 DIF with bad firmware version (dif 2 and 5):
1/ not the same BCID counter reference (easy to patch)
2/ start to take data earlier:
- CC mode: first data lost for reconstruction of MIPs or showers
- PP mode: electronics are not stabilized before 600 BCID (see figures)
* data lost for all analysis
- all modes: increase the probability to have an ASIC full before other DIFs
* reduce efficiency
* increase probability to have less than 6 layers in an event
CC
PP
BCID cut for DIFs with bad firmware
Start of others DIFs

---
Detection efficiency (Summer 2013)
* Same tools as previous TB
* Select events:
- without inefficiency due to full ASIC
- without inefficiency due to DIF firmware problem
- at least 4 layers with hits
- only 1 incoming particle
CC
PP
Trigger threshold too high
High dispersion in some layers
Used to define trigger threshold in simulation
→ Need trigger threshold per channel in simulation (done)
→ Inefficiency due to plane events (to be done)
To be understood

---
Reminder – Noise in 2012 TB
M1
M2
M3
M4

---
Comparison CC \ PP - Pedestal (2013)
(BCID cut for bad DIFs firmware is applied)
ASIC M1
ASIC M2
ASIC M3
ASIC M4
DIFs with bad firmware
(BCID cut for bad DIFs firmware is not applied)
ASIC M3
ASIC M1
CC
PP
Same noise pattern as 2012 TB
PCB routing has additional effect in PP

---
Comparison CC \ PP - Energy calibration (2013)
Fit energy distribution: Landau convoluted with a Gaussian
Sigma of the Gaussian is fixed to the noise
ASIC M1 – all layers
ASIC M1 and M3
Trigger threshold too high
bad DIFs firmware
Layer with bad DIF firmware excluded
ASIC M1
ASIC M2
ASIC M3
ASIC M4
ASIC M2 and M4

---
Comparison CC \ PP - Energy calibration (2013)
DIFs with bad firmware
CC
PP
Trigger threshold too high
ASIC M3
ASIC M1
* No trigger delay calibration: response not optimized → bad S/N
* 2012 TB: response flat as a function of the channel number (trigger delay calibration?)
* PCB routing seems to have effect on energy calibration (@ pedestal subtraction step?)

---
Signal over noise (2012)
2013: No trigger delay calibration: response not optimized → bad S/N

---
Showers (2013)
CC
PP
MC
Fit: Cst  a/E  b/E
- Linear fit
The PP fit is disturbed by one bad value.
--> same non linearity effect in MC and data
On going: Inefficiency due to plane events

---
Conclusion
2012 results describe in CALICE Internal Note CIN-023 → Upgrade to publication
==> Successful test beam campaign
encouraging results
identification of open issues
Summer 2013: useful results especially concerning power pulsing studies
Finalize 2012 / 2013 shower analysis
Internal Note to summarize power pulsing studies
Thanks to all people who have a positive impact on the Si-W ECAL developments

---
Event display
MIP
MIP
MIP
MIP
MIP