## Slide 1: Review of Shift 160413
1/13
Mikey Davis
17 April 2013

## Slide 2: Notes on Setup
2/13
Mikey Davis
17 April 2013
The damping ring LO was used throughout last night
This was always set to the correct level for the 2nd stage being use (either Honda or FONT)
We split IPB – the graphs are labelled IPA and IPB, this corresponds to the first and second sets of channels of IPB

## Slide 3: IP Waist Scan - Epics
3/13
Mikey Davis
17 April 2013

## Slide 4: Normal Calibrations
4/13
Mikey Davis
17 April 2013

## Slide 5: Jitter Runs
5/13
Mikey Davis
17 April 2013
Background STD 19 Counts

## Slide 6: Jitter Runs
6/13
Mikey Davis
17 April 2013
Background STD 19 Counts

## Slide 7: FFT of Jit Run
7/13
Mikey Davis
17 April 2013

## Slide 8: Summary of the Problem
8/13
Mikey Davis
17 April 2013
The calibration constant that turns raw I’ in FONT ADC units into microns is :
If you use this to convert the ADC noise into microns you get jitters of :
N.B. I have done this properly and combined the channels to get IPrime
Attenuation Setting | IPA Channel | IPB Channel
20 dB | 0.12 | 0.19
30 dB | 0.40 | 0.59
Attenuation Setting | IPA Channel | IPB Channel
20 dB | 2.3 | 3.0
30 dB | 8.0 | 9.7

## Slide 9: Summary of the Problem
9/13
Mikey Davis
17 April 2013
This is clearly not the only problem we have
However it does contribute a lot to the jitter
I tried using the FONT BPM processor and a rigged up amplifier I found instead of the second stage
Took two calibrations using diff setups and two jitter runs, both worked better than the Honda 2nd stage

## Slide 10: FONT BPM Proc Calibrations
10/13
Mikey Davis
17 April 2013

## Slide 11: Jitter Runs
11/13
Mikey Davis
17 April 2013
Background STD 15 Counts

## Slide 12: FFT of Jit Run
12/13
Mikey Davis
17 April 2013

## Slide 13: Summary of the Problem
13/13
Mikey Davis
17 April 2013
By the same method as last time this then gives us a minimum jitter or 1.5μm
The measured jitter on the last run was 3.6μm
I think this could be further improved by rejiging two processors together
  Not sure what people think