## Slide 1: June ATF Plan
1/7
Mikey Davis
30 May 2013

## Slide 2: Cavity BPM Tests
Work out how to move the X waist, test this
  Use QF1FF to move the waist
  Try and X waist scan using EPICs through both IPA and IPB
  Consider Calibrating Honda X
Y waist scan both epics and Honda
  with X waist nominal
  With X waist at new optimal setting)
2nd stage modules
  Do calibration and jitter run for
  Repeat for modules used in April
  Repeat again for new optimum modules
Try using low pass filters
  Not sure if people think this is a good idea
  Maybe just put them on and use them all the time
2/7
Mikey Davis
30 May 2013

## Slide 3: Upstream Feedback Tests
Repeat with both IPA and IPB calibrated properly
  Maybe put an extra 10 dB in IPA
  Depending on resolution of IPB move waist slightly off
T Shirt Plot
  Do a t shirt plot using a corrector upstream of FONT region
  I’d advocate doing this regardless of resolution
3/7
Mikey Davis
30 May 2013

## Slide 4: Feedforward Tests
Try and make it work again
Spend some time looking at the gains
  I am looking at other ways to calculate this now
    Transfer matrices
    Looking at the 2d surface
  Maybe try some gain scans
4/7
Mikey Davis
30 May 2013

## Slide 5: IP Feedback Tests
If both boards are working us the upstream system to align the two bunches
Try moving the waist
  If we are limited by resolution try moving the waist
  Correction of 500 nm jitter to 100 nm would still be good
T shirt plots
  Use QD0FF to move the beam
  Try putting it back to 0 in the downstream system
5/7
Mikey Davis
30 May 2013

## Slide 6: Things To Consider
How will we setup?
  Where should we put the “bad” FONT V Board
  Should we put the IP board in or out of the tunnel
  How should we setup the attenuators
  Which 2nd stages should we use
  Which LO (I would suggest ref cav)
  Should we instrument X
What is the status of the “broken” FONT V board
Have we got any of the new stuff we ordered yet?
  RF switches
  Variable attenuators + controls
6/7
Mikey Davis
30 May 2013

## Slide 7: Things for Young Im
How do we start the FONT EPICs database
How do we restart the variable attenuator database if this breaks
7/7
Mikey Davis
30 May 2013