## Slide 1
David Attié
Club ‘ILC Physics Case’
CEA Saclay
June 23, 2013
ILD & SiD concepts
and R&D
Notes: I’m here to present a TPC review

## Slide 2: Introduction: Physics Case at ILC
Next collider: linear e+e– collider, length: ~ 31km
Tunable center of mass energy of 200-500 GeV
Two detectors with push-pull concept
Both need to fit into Particle Flow concept

## Slide 3: Two detector concepts
International Large Detector
Silicon Detector
LoI: 2009 (SiD)-2010 (ILD)
DBD: 2012 (ILD)-2013 (SiD)

## Slide 4: Side (quadrant) views
ILD
SiD

## Slide 5: Particule Flow Algorithm (PFA) Approach
Traditionally, Ejet = EECAL + EHCAL
Multi-jet energy resolution needed at the ILC: (E/E  0.3/E)
Solution = PFA: cross-checking of the measurements of all sub-detectors which will be highly segmented from IP
Trackerscharged particles
Calorimetersseparation charged/neutral
particles

## Slide 6: Particule Flow Algorithm (PFA) Approach
1×1
3×3
5×5
10×10
Analogue scintillator tile HCAL: change tile size from 1×1  10×10 mm2
1×1 cm2 and 3×3 cm2 cell size
Cell size > 5×5 cm2 degrades PFA

## Slide 7: Concept overview for SiD
5T magnet
Silicon-based tracking
  Vertex detector: 5 Si pixel layers, pixel size of 20 × 20 m²
  Si main tracker: Si strip of 5 nested cylinders in central region and 4 disks, pitch 50 m
Main calorimeters (barrel+2 end-caps) inside solenoid with imaging capabilities
  30 Si active layers using 5 × 5 mm² Si pixels between W absorber
  (Two other technologies (GEM & Micromegas) are currently prototyped and evaluated as potential options)
Forward calorimeters (compact ECALs): LumiCal + BeamCal
  30 layers of semiconductor-tungsten technology
Muon system: few 103 m² scintillator (or RPCs)

## Slide 8: Concept overview for SiD

## Slide 9: Concept overview for ILD
3.5T magnet
Vertex detector (VTX):
  MAPS
Silicon strip detector (SIT):
Time Projection Chamber (TPC):
  MPGD readout (GEM or Micromegas) with <1 mm pad size
Calorimeters (layers of W and Fe):
  ECAL: Si diodes or scintillators (30 samples in depth)
  HCAL: 3×3cm² scintillator tiles or 1×1cm² gas based (48 long. samples)
Forward calorimeters (compact ECALs): LumiCal + BeamCal
  30 layers of semiconductor-tungsten technology
Muon system:
  Scintillator strips or resistive chambers (RPCs)

## Slide 10: Concept overview for ILD

## Slide 11: SiD costs
860 M $

## Slide 12: ILD costs

## Slide 13: SiD R&D

## Slide 14: R&D
MAPS: monolithic active pixel sensor
DEPFET: active pixel detectors for a future linear e+e- collider

## Slide 15: Micromegas TPC in Saclay
Offline monitor
L: 4.7m
: 3.6m