## Slide 1: Beam test Analysis Micromegas TPC by Wenxin Wang
CEA-Saclay

## Slide 2: Micromegas module
Module size: 22 cm × 17 cm
24 rows × 72 columns
Readout: 1726 Pads
Pad size: ~3 mm × 7 mm

## Slide 3
2008~2011:
Test with one module at the center of LP-TPC
2012~2013:
Test with multi-modules at the endplate of LP-TPC

## Slide 4: Tests with one single module
(2008~2011)
At the center of LP-TPC

## Slide 5: Micromegas modules
Resistive ink
~3 MΩ/□
Resistive Kapton
~5 MΩ/□
Standard
(no resistive layer)
Resistive Kapton
~3 MΩ/□
Module 1
Module 2
Module 3
Module 4 &
Module 5

## Slide 6: Uniformity
Z=5cm
Mean Residual vs Row Number
Z-independent distortions
Distortions up to 50 microns for resistive ink (blue points)
Rms 7 microns for CLK film
(red points)
Z=50cm
Z=35cm
Row number
Resistive CLK Module
Resistive ink Module

## Slide 7: Spatial resolution
Module 5
Module 4
: the resolution at Z=0
: the effective number of electrons
Cd = 315.1 µm/√cm (Magboltz MC)
(B = 0T)

## Slide 8: Spatial resolution
(B = 1T)
Module_INK
Module_CLK
Cd = 94.2 µm/√cm (Magboltz MC)

## Slide 9: Spatial resolution

## Slide 10: Tests with multi-modules
(2012~2013)
Fully cover the endplate of LP-TPC
Using a quasi-industrial production chain

## Slide 11: Integrated electronics
14 cm
25 cm
Front-End Card
(FEC)
12.5 cm
2.8 cm
Remove packaging and protection diodes
Wire-bond AFTER chips
Use two 300-point connectors
0.78 cm
0.74 cm
3.5 cm
3.5 cm
AFTER Chip
  The resistive foil protects against sparks
4.5 cm

## Slide 12: Test bench
Test with collimator
Test without collimator
to check the map of missing pads

## Slide 13: Modules comparison
At Vmesh = 380 V, Energy resolution ~12% r.m.s
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 0.12692 | 0.12361 | 0.11822 | 0.12788 | 0.11539 | 0.11309 | 0.12692

## Slide 14: Modules comparison
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 2469.0098 | 2979.0717 | 2327.5895 | 2559.4998 | 2063.5909 | 3134.0745 | 2844.6615
At Vmesh = 380 V, average gain ~ 2630, gain spread ~15%

## Slide 15: Gain Study using beam events
2500 at Vmesh=380V
( 2700 at Vmesh=380V
From test bench)
Charge per row
For 6.84 mm pitch & 5 GeV e-
Nelectron (MPV) expected = 45
(from HEED simulation)

## Slide 16: Beam events display
2D or 3D display from ILC software
Online monitor
Offline monitor

## Slide 17: Analysis Framework: MarlinTPC
MarlinTPC
Marlin based simulation, digitization, reconstruction and analysis code for the TPC.
KalDet &KalTest: (installed in Marlin)
    A ROOT-based Kalman Filter Package.
    Used to reconstruct tracks.

## Slide 18: Spatial resolution
Event selection
 only single track event

## Slide 19: Spatial resolution
Hit selection
Fit track with all rows
: supposed residual of the detector
: the fitted hit position in test row
: the position of track crossing the test row

## Slide 20: Spatial resolution
Profile histogram of the residual with the track in one row before bias correction
Profile histogram of the residual with the track in one row after bias correction
Pad size
(mm)
(mm)
(mm)
(mm)

## Slide 21: Spatial resolution
Distribution of the residuals (z = 15 cm)

## Slide 22: Spatial resolution
B=1 T Cd = 94.2 µm/√cm (Magboltz MC)
24 rows of a module

## Slide 23: Extrapolation of the spatial resolution
Extrapolate to 2.3m & B=3.5T
B=0T
B=1T
B=3.5T
--- Micromegas with
3 mm width pads
--- GEM with 1 mm
width pads
B=1T

## Slide 24: Distortions
B=1T
B=0T
After alignment B=0T

## Slide 25: Field distortions
Distortions in B=0T or B=1T
at different drift distances z (15cm~50cm)
B=1T
B=0T

## Slide 26: Gain
Gain as a function of Vmesh
(Edrift = 0.2 kV/cm at atmospheric pressure)
A measured 55Fe spectrum
(at Vmesh = 350 V and Vdrift = 400 V)

## Slide 27: Electron transparency

## Slide 28
A lot of experience has been gained in building and operating Micromegas TPC panels.
The characteristics of the Micromegas modules, such as the uniformity, energy resolution, stability have been studied in detail.
7 modules have been successfully tested with full integration of the electronics at the same time.
Thanks to the resistive technology, the measured resolution is about 60 microns at zero drift distance with 3 mm wide pads. This meets ILC needs.
Distortions are observed. Their detailed study will allow to correct them and improve the design to minimize them.
Conclusion