## Slide 1: Applications of Stripline and Cavity Beam Position Monitors in Low-Latency, High-Precision, Intra-Train Feedback Systems
1/**number**
Mikey Davis
19 September2013
M.R. Davis, D.R. Bett, P.N. Burrows, N. Blaskovic Kraljevic, G.B. Christian, Y.I. Kim, C. Perry
John Adams Institute, Oxford University, UK

## Slide 2: Introduction
Motivation for research is beam stabilisation at ILC
Aim to stabilise nm beams for collision at IP
  Misaligned beams at IP cause a beam-beam deflection
  Measure one of the outgoing beams
  Kick the next bunch of the other incoming beam
  Key issue at a collider: latency
2/**number**
Mikey Davis
19 September2013

## Slide 3: The ATF 2 Project
ATF2 – Scaled down mock up of the ILC FF system
Goals:
  Demonstrate 37 nm vertical spot at the focal point (IP)
  Demonstrate nanometre level stability
3/**number**
Mikey Davis
19 September2013

## Slide 4: FONT
Feedback On Nanosecond Timescales (FONT)
Previously demonstrated a system meeting ILC latency and jitter specifications
Extended aims to improve on ILC requirements and meet ATF goal 2
4/**number**
Mikey Davis
19 September2013

## Slide 5: Upstream System
5/**number**
Mikey Davis
19 September2013
Strip-line BPM with mover system
3 Stripline BPMs (P1, P2 and P3)
12 cm long strips
12 mm radius
Mounted on a 2 axis mover system

## Slide 6: Upstream System
6/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
Strip-line BPM with mover system

## Slide 7: Upstream System
7/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Strip-line BPM with mover system
9 analogue input channels
400 MS/s ADCs
2 Analogue output channels
DACs clocked at 210 MHz
Based on a Xilinx Vertex 5 FPGA

## Slide 8: Upstream System
8/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Kicker drive amplifier
Strip-line BPM with mover system
Manufactured by TMD Technologies
±30 A drive current
35 ns rise time (90% of peak)
Output pulse length up to 10 μs

## Slide 9: Upstream System
9/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Kicker drive amplifier
Strip-line BPM with mover system
Strip-line kicker
Shorted at one end to form a transition line

## Slide 10: Upstream System
10/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Kicker drive amplifier
Strip-line BPM with mover system
Strip-line kicker
System Resolution (BPM processor) | <1μm
System Latency | <150 ns
Amplifier/ Kicker Bandwidth | ~30 MHz
Dynamic range of the BPM system | +/- ~500μm

## Slide 11: Upstream BPM Processors
High resolution low latency analogue processors
Difference over sum method
Top and bottom signals:
  Added using a resistive coupler
  Subtracted using a hybrid
Signals then band pass filtered
Down-mixed using DR 714 MHz
Best achieved resolution 350nm
Latency of…
11/**number**
Mikey Davis
19 September2013

## Slide 12: IP System
12/**number**
Mikey Davis
19 September2013
Cavity BPM
2 Cavity BPMs (IPA and IPB)
C-band (5.7 GHz)
Low-Q
Inside IP chamber

## Slide 13: IP System
13/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
Strip-line BPM with mover system

## Slide 14: IP System
14/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Strip-line BPM with mover system
Kicker drive amplifier

## Slide 15: IP System
15/**number**
Mikey Davis
19 September2013
Analogue Front-end
BPM processor
FPGA-based digital processor
Kicker drive amplifier
Strip-line BPM with mover system
Strip-line kicker
Designed in house
Based on the ATF stripline BPMs
Shorter than upstream (less kick)

## Slide 16: IP BPM Processors
Two stage homodyne process
1st stage:
  Down-mixes 5.7 GHz to 714 MHz
2nd stage:
  Down-mixes 714 MHz to 0 MHz
714 MHz generated using upstream reference cavity
We achieve resolutions of order 65 nm
More detail in:
  These proceedings – TUPC22
  Y. I. Kim, PhD, Kyungpook National University, 2012
16/**number**
Mikey Davis
19 September2013

## Slide 17: Experimental Modes
Three experimental modes:
  Upstream feedback
  Upstream -> IP feedforward
  IP feedback
All 3 modes aimed at stabilising the beam at IPB
17/**number**
Mikey Davis
19 September2013

## Slide 18: Upstream Feedback
18/**number**
Mikey Davis
19 September2013

## Slide 19: Upstream FB (Upstream)
19/**number**
Mikey Davis
19 September2013
FB Off Jitter: 2.5 ± 0.1 μm
FB On Jitter: 1.4 ± 0.1 μm
FB Off Jitter: 2.6 ± 0.1 μm
FB On Jitter: 0.9 ± 0.04 μm

## Slide 20: Upstream FB (IPB)
20/**number**
Mikey Davis
19 September2013
FB Off Jitter: 0.35 ± 0.02 μm
FB On Jitter: 0.3 ± 0.01 μm
FB Off Correlation: 79%
FB On Correlation: 14%

## Slide 21: Feedforward
21/**number**
Mikey Davis
19 September2013

## Slide 22: Feedforward Results
22/**number**
Mikey Davis
19 September2013
FB Off Jitter: 160 ± 10 nm
FB On Jitter: 106 ± 10 nm
FB Off Correlation: 73%
FB On Correlation: 23%

## Slide 23: Upstream Corrector Scan
23/**number**
Mikey Davis
19 September2013

## Slide 24: IP Feedback
24/**number**
Mikey Davis
19 September2013

## Slide 25: IP Feedback Results
25/**number**
Mikey Davis
19 September2013
FB Off Jitter: 168 ± 10 nm
FB On Jitter: 93 ± 4 nm
FB Off Correlation: 81%
FB On Correlation: -16%

## Slide 26: IPFB Corrector Scan
26/**number**
Mikey Davis
19 September2013

## Slide 27: IPFB Waist Scan
27/**number**
Mikey Davis
19 September2013

## Slide 28: Conclusions
Demonstrated 3 methods of beam stabilisation
Best vertical beam position stabilisation 100nm
Achieved using feedforward and IP feedback
IP BPMs at ATF have been replaced this summer
28/**number**
Mikey Davis
19 September2013